## Slide 1: VHDL Simulation vs. Synthesis
EL 310
Erkay Savaş
Sabancı University

## Slide 2: Two Models for VHDL Programs
Two models
Simulation
  Describe the behavior of the circuit in terms of input signals, the output signals, knowledge of delays
  Behavior described in terms of occurrences of events and waveforms on signals
Synthesis
  Reverse process – inference of hardware from description
  The synthesis tool will infer a hardware architecture from the VHDL model
  When writing a VHDL program, think of the hardware that synthesis tool would infer from it

## Slide 3: Relationship between Simulation & Synthesis
entity my_ckt is
Port(x, y: in bit;
z: out bit)
end entity my_ckt;
architecture behavioral of my_ckt is
begin -- some code here
end architecture behavioral
entity my_ckt is
Port(x, y: in bit;
z: out bit)
end entity my_ckt;
architecture behavioral of my_ckt is
begin
-- some code here
end architecture behavioral
synthesis
simulation
Simulation and synthesis are
complementary processes

## Slide 4: Simulation Model
Recall, in digital systems
  Events on signals take place at discrete points in time
  Some events cause other events after some delay
  Many events may be generated concurrently
@ 5 ns
0
1
0
@10 ns
0
1
@15 ns
0
1
0  1
a @ 5ns
1  0
s2@ 10ns
0  1
z@ 15ns
1
a
b
s1
s2
z

## Slide 5: Discrete Event Simulation
A programming-based methodology for accurately modeling the generation of events in physical systems.
  A program that specifies how and when events on specific signals are generated
  Discrete event simulator then executes this program, modeling the passage of time and the occurrence of events at various points in time
  Simulator often manages millions of events and keep accurate track of correct order of events
  The way the simulator manages events and their orders, that is called discrete event simulation model, must be very well understood to write, understand and debug VHDL codes

## Slide 6: Discrete Event Simulation Model
Discrete event simulation utilizes a sorted event list structure.
  Each event is described by the type of event (e.g. 10, 01 transitions) and the time it is to occur.
  Transition could be in various forms (Z1, 0X)
  Timestamp of an event is the time at which this event happens.
  Event list is ordered according to increasing timestamp value.
  Simulator clock records the passage of simulated time.
  The value of the clock is called current timestep
  A snapshot of the values of all signals at a timestep is called the state of the simulation.

## Slide 7: Discrete Event Simulation: Example 1
Half Adder
a
b
sum
carry
b
a
carry
sum
event
5 ns
10
15
20
25
30

## Slide 8: Discrete Event Simulation: Example 2
Discrete event simulation of half adder
1  0
a @ 5ns
U  0
sum @ 5ns
U  1
carry @ 5ns
1  0
b @ 10ns
0  1
a @ 10ns
1  0
carry @ 10ns
0  1
sum @ 10ns
1  0
a @ 15ns
For example, sum is scheduled to take value of 0 at simulation time 5 ns. Prior to this time, sum and carry are uninitialized.
Simulator removes these events from the list in the specified order and updates the values of signals accordingly.
The global clock is first updated with the current time, then the event scheduled to this time are executed and then removed.
event list before 5 ns

## Slide 9: Steps of the Simulation Model
Advance the simulation time to that of the event with the smallest timestamp in the event list. This is the event at the head of the sorted event list.
Execute all events at this timestep by updating signal values
All components affected by the new signal values must be re-evaluated( new events that may be generated as a result of changes in signal values must be scheduled by placing them in event list in the order of their timestamp)
Schedule future events
Repeat until the event list is empty or preset simulation time has expired.
The simulation model is very general such that it is applicable to different levels of abstraction.

## Slide 10: Logical Model vs. Physical Model
Discrete event simulation model is just an approximation of behavior of real systems.
  In fact, there are only analog devices where we interpret analog voltage levels as logical 0 or 1.
  We refer discrete event simulation model as logical model while the real device as physical system
  For better accuracy with which to capture the behavior of physical system some complimentary techniques or models must be employed
  VHDL simulators provide facilities for setting the duration of a simulation timestep and query the contents of the event queue during simulation
  user can examine the event at the head of the event queue and force signals to specific values prior to next timestep.

## Slide 11: Accuracy vs. Speed
Think of a 32-bit adder
Low accuracy:
  In VHDL, a 32-bit adder may be described in one line: two inputs and a single output. Inputs generate a value that appears at the output after some propagation delay.
  One step corresponds to the delay of adder
  Easy, fast, and not too accurate
High accuracy:
  We might describe the adder at gate level
  More realistic simulation
  Has to handle many events
  One step in the simulation corresponds to one gate delay.
  Naturally slow

## Slide 12: Synthesis Model
Synthesis is a process
  Where a physical system is constructed from an abstract description using a pre-defined set of basic building blocks (e.g. logic gates, flip-flops, latches, small blocks of memory, LUTs in FPGA)
Synthesis compilers operate on three types of information
  Model of the circuit (e.g. VHDL model)
  Set of constraints (speed, area, etc)
  Set of components ( 2-input NAND gates, flip-flops with asynchronous set and reset, etc.)

## Slide 13: Design Process 1
We use
  Boolean expressions, truth tables, state diagrams to design a digital system.
  With synthesis tools, we can design digital systems at higher level of abstractions such as addition or multiplication of integers or real numbers, masking and shifting operations on Boolean strings, etc.
  The higher the level of abstraction you design at the less control over what is being synthesized by the compiler
  High-level synthesis problem is more challenging for the complier since it has to choose between alternatives
  The one chosen by the compiler may not be optimal.

## Slide 14: Design Process 2
However,
  working at higher level of abstraction we will design the hardware in less time (shorter design cycle)
  It also facilitate design re-use and react to the future changes in the design
  For example, think of 32-bit adder
  By specifying the design constraints the compiler may choose between carry ripple adder (which is area optimized) and carry lookahead adder (which is time optimized)

## Slide 15: Hardware Inference
Just as simulation process is based on discrete event simulation, synthesis process from VHDL model is based on the process of inference.
  Synthesis compilers must infer typical hardware components and their interconnection from the VHDL code.
  Inference is followed by optimization to reduce the size or increase the speed of of the inferred circuit.
  If you follow certain rules while writing VHDL programs, you will have significant control over the inferred hardware.

## Slide 16: Hardware Inference: Example
Inferring Combinational Logic
--
-- pseudo code for a single-bit arithmetic/logic unit
--
s1 <= in1 and in2;
s2 <= in1 or in2;
s3 <= in1 xor in2 xor c_in; -- perform the sum operation
c_out <= (in1 and c_in) or (in1 and in2) or (in1 and c_in);
z <= s1 when sel = “00” else
s2 when sel = “01” else
s3 when sel = “10” else ‘0’;

## Slide 17: Inferring Combinational Logic
Single-bit ALU
sel(1)
sel(0)
in1
in2
c_in
c_out
z
(in1·in2) sel(1)’·sel(0)’
(in1in2c_in) sel(1)·sel(0)’

## Slide 18: Inferring Sequential Logic
-- -- a simple conditional code block --
if (sel = ‘0’) then
z <= in1 nor in2;
end if;
sel
in1
in2
z
Inference of sequential components is more subtle.
Whether a latch of flip-flop is inferred depends on the way we write your VHDL codes.
By careful coding, we can avoid unnecessary sequential components (stay away from conventional programming techniques; stick to “hardware aware” approach)

## Slide 19: Target Primitives 1
Target primitives are the building blocks synthesis compiler use.
  Example: Boolean equation, z = a’bc + b’c + db
z
a
b
c
b
c
d
b
z
a
b
c
b
c
d
b
c
b
c
d
a
z
Simple fact: Circuit produced by the synthesis compiler depends on the set of available building blocks

## Slide 20: Target Primitives 2
Implementation given the description is not necessarily unique.
The way the synthesis compiler choose building blocks is also dependent on selected performance metrics such as area and speed.
Fortunately, CAD tools offers optimization facilities given performance metrics for target devices.
If you know the target primitives, you can anticipate the logic that the compiler infer for a given language construct

## Slide 21: Field Programmable Gate Arrays (FPGA)
Reprogrammable hardware devices
  (Re)configurable hardware, reprogrammable hardware, etc.
  We are interested in one kind of such reprogrammable hardware: FPGA.
Why Reprogrammable hardware?
  ASIC offers the highest performance
  But performs only one function
  Development cost cannot be spread across multiple applications
  Ideal solution: change the interconnection between millions of transistors comprising the chip in order to compute another function.

## Slide 22: Basics of FPGA
Think of a cell (or block)
  That can be programmed to implement any small combinational or sequential circuit
  Tile the surface of a silicon die with these cells.
  Wires running vertically and horizontally between these cells.
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
  Any block can connect itself to horizontal or vertical wires that are adjacent to it.
  Interconnect of the wires are called switching matrix.

## Slide 23: Design with FPGA
Two types of blocks
  CLB – configurable logic blocks (inside the chip)
  IOB - I/O blocks on the periphery (to drive the signals off the chip and read the incoming signals)
Design process
  Partition the “big” design into small sub-circuits.
  Each sub-circuit can be implemented in a CLB
  Establish the connections between sub-circuits through the switching matrix
  If another design to be implemented, go to Step 1.

## Slide 24: Inside the XC 4000 CLB
Many FPGAs look similar
  But they differ in how CLBs are implemented.
  CLB is actually Xilinx terminology
Main components in XC 4000 CLB
  Two 16x1 RAM blocks
  One 8x1 RAM block
    RAM can be used as LUT to implement combinational logic through truth tables
  Two edge-triggered D flip-flops
    Can also be configured as latches
  Several multiplexors to configure the interconnection within the CLB.

## Slide 25: Xilinx XC 4000 CLB
G4
G3
G2
G1
F4
F3
F2
F1
Logic
Function
of
G1 – G4
Logic
Function
of
F’, G’, H1
Logic
Function
of
F1 – F4
G
F
DIN
F ’
G ’
H ’
DIN
F ’
G ’
H ’
H
H ’
G ’
K (clock)
EC
D
Q
SD
RD
1
S/R
Control
S/R
Control
EC
D
Q
SD
RD
1
H1
DIN / H2
SR /
H0
EC
H ’
F ’
X
Y
XQ
YQ
4
C1 … C4
bypass

## Slide 26: Lookup Tables (LUT)
Combinational circuits are implemented using LUT
z
a
b
c
d
a | b | c | d | z
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 1
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 0 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 1 | 0

## Slide 27: Combinational functions in LUT
Four inputs serve as the 4-bit address to the 16x1 memory
Single bit memory hold the output value corresponding to the input value that is used as an address to access to this memory cell.
16x1 LUT can implement any Boolean function of four variables
LUT is also referred as function generator.
Each CLB has two 4-bit function generators: F and G
The third generator, H, can implement any Boolean function of three variables.
  Two inputs come from the outputs of F and G.
  The other input comes from outside

## Slide 28: LUT
Using three function generators F, G, and H
  A single CLB can implement any Boolean function of five variables and some functions of up to nine variables
  It has nine logic inputs: F1, F2, F3, F4, G1, G2, G3, G4, and H1.
  General form of Boolean function of five variables: H = F(F1, F2, F3, F4)·H1’+ G(F1, F2, F3, F4 )·H1
In some 4000 CLBs, LUTs can be configured as memory block
  One 32x1 module
  Dual ported 16x1 memory module
  Synchronous-edge-triggered and asynchronous-memory interfaces are supported

## Slide 29: Odds and Ends
Two D flip-flops with enable clock (EC) input
  Edge-triggered flip-flop or
  Can also be configured as latches with a common clock and clock enable inputs
Four additional inputs and a clock
  (C1 … C4) and K (clock)
CLB has four outputs
  Two from the combinational function generators.
  Two from the flip-flops
Bypass signals
  To facilitate placement and routing, there are bypass signals that pass inputs to outputs without changing it: XQ and YQ

## Slide 30: Odds and Ends
Many vendors typically supply implementation of common building blocks that are optimized to the structure of their hardware components.
  Xilinx, in fact, has a core generator utility that can create common building blocks from parameterized descriptions provided by the user
  Adders, subtractors, multipliers, memories, etc. are such building blocks
FPGA as a sea of LUTs and flip-flops
  A gate-level design can be placed on the array by mapping combinational components to function generators, sequential to flip-flops

## Slide 31: Carry Logic 1
Each cell contains carry logic for two bits
G
F
H
G
Carry
F
Carry
M3
M4
M2
M1
CIN UP
CIN DOWN
COUT
COUT
G4
G3
G2
G1
F3
F2
F1
F4

## Slide 32: Carry Logic 2
F and G generators can be used to generate the sum bits.
Thus, each cell can be programmed to implement both carry and sum for two bits of a full adder
The carry lines between cells are hardwired (not programmable) to provide for fast propagation of carries
The carries can propagate up or down between cells and programmable MUX (M1) selects the direction.
MUXes M2, M3, and M4 allow some of F and G generator inputs to come from carries instead of normal inputs.
The carry logic can be programmed to implement subtracter, incrementer/decrementers, 2’s complementers, and counters

## Slide 33: A CLB as Two-Bit Full Adder
G4: Ai+1
G1: Bi+1
F2: Ai
F1: Bi
Ci
G Function
F Function
Carry Logic
Si+1
Si
Ci+2
Ci+1
hardwired
hardwired

## Slide 34: Connections for 4-bit Adder
CLB
CLB
CLB
CLB
A1
B1
A0
B0
C0
C0
C2
C3
A3
B3
A2
B2
C4
V
Hard-wired
If we want to detect a possible overflow, we add the 4th CLB.
The 3rd CLB outputs C3 instead of C4 (How?)
In the 4th CLB, C4 can be re-computed using the carry logic.
Overflow is computed using the G function generator in the 4th CLB
Overflow: V = C3 C4
4-bit adders can easily be expanded 8 or 16-bit adders
Adder modules are available in Xilinx library

## Slide 35: F and G as RAM Memory: 16x2
G
F
G4
G3
G2
G1
F4
F3
F2
F1
WE
DATA IN
WE
DATA IN
M WRITE G
M WRITE F
WE
D1
D0
EC
C1
C2
C3
C4
M
16x2
Fi = Gi
C1 is write enable (WE)
C2 and C3 are data inputs
Can it be configured as 32x1 memory?

## Slide 36: IOB 1
CE
D
Q
CE
D
Q
Out
0
1
TS
Slew Rate control
Passive Pull-Up
Pull-Down
Output Buffer
Input Buffer
delay
delay
G
D
Q
Output clock
pad
I1
I2
Clock enable
Input clock
Fast Capture Latch
Output
MUX

## Slide 37: IOB 2
4000 IOB
  Implements I/O functionality in the chip
  I1 and I2 signals carry input to the FPGA directly from the pin or from an IOB flip-flop that can be used to capture the input data.
  Additional latch for fast capture of data
  Output signals can pass directly to the pin or can be stored in a flip-flop
  Output multiplexor enables two signals (output data and clock enable) to share a pin (higher number of effective outputs).
  Separate clocks for input and output
  can be programmed to invert input, output, tristate buffer, and clock input

## Slide 38: Switch Matrix
Different levels of interconnections
  Direct interconnects between CLBs. Short wires to connect adjacent CLBs in both directions.
  Switch matrix
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
PSM
PSM
PSM
PSM
PSM: Programmable Switch Matrix
PSM can be configured to connect a horizontal wire to a vertical one.
One wire can be connected to multiple wires
This way output of a CLB can routed through multiple PSMs to the input of another CLB.

## Slide 39: PSM
CLB
12
4
4
2
2
12
6
4
8
4
8
4
3
3
Quad
Single
Double
long
Direct connect
long
long
long
Double
Quad
Direct connect
Carry
chain
Single
Global clock
Global clock

## Slide 40: Types of Lines
Single-length: connects adjacent PSMs
Double-length: connects every other PSM
Quad-length: traverse four CLBs before passing through a PSM.
Long: runs entire chip.
  Using tri-state buffers within the CBLSs, long lines can be configured as buses.
Local connections use direct interconnect or single length lines in order to avoid to many switching points
Global Nets: Low skew signal paths used to distribute high fan-out signals such as clock and reset signals.

## Slide 41: Double Length Lines
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
PSM
PSM
PSM
PSM

## Slide 42: Example Interconnects
Direct interconnects between adjacent CLBs
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
CLB
PSM
PSM
PSM
PSM
PSM
PSM
CLB
CLB
CLB
CLB
General-purpose interconnects

## Slide 43: Tri-state Buffers
Bus
  Each CLB has tri-state buffers that connect to long lines.
  Bus contention must be avoided
DA
A
DB
B
DC
C
DN
N
Z = DA A’ +DB B’ + DC C’ + … +DN N’
Wired-AND implementation
DA
Z = DA DB DC … DN
DB
DC
DN
VCC
VCC

## Slide 44: Configuration 1
Configuration data for CLBs
  Provide the contents of the LUTs (16+16+8 = 40 bits)
  Configure multiplexors within the CLB
    To determine the input sources of the flip-flops, and the inputs to the H function etc.
  Bits for configuring flip-flops
Configuration data for PSM
  Connecting horizontal and vertical lines
  Tristate devices within the CLBs

## Slide 45: Configuration 2
G4
G2
G1
F4
F3
F2
F1
Logic
Function
of
G1 – G4
Logic
Function
of
F’, G’, H1
Logic
Function
of
F1 – F4
G
F
DIN
F ’
G ’
H ’
DIN
F ’
G ’
H ’
H
H ’
G ’
K (clock)
EC
D
Q
SD
RD
1
S/R
Control
S/R
Control
EC
D
Q
SD
RD
1
H1
DIN / H2
SR /
H0
EC
H ’
F ’
X
Y
XQ
YQ
4
C1 … C4
bypass
Xilinx X4000
M
M

## Slide 46: Configuration 3
Configuration data for IOB
  IO clocks
  Storage vs. direct access to the pin.
Size of the configuration file
  Each of the configuration requires at least a bit of memory
  Configuration data from several Kbits to several Mbits
  Rule of Thumb: 20 configuration bits per available user gates
CAD tools translate VHDL code to bit stream to configure FPGA device

## Slide 47: Configuration 4
Output clock
Clock enable
Input clock
CE
D
Q
CE
D
Q
Out
0
1
TS
Slew Rate control
Passive Pull-Up
Pull-Down
Output Buffer
Input Buffer
delay
delay
G
D
Q
pad
I1
I2
Fast Capture Latch
Output
MUX
M
M

## Slide 48: FPGA Design Flow 1
  HDL editor
State machine editor
  Schematic capture
Synthesis
Place and Route
Programming
Behavioral simulation
Functional simulation
Verification
Device programming
Xilinx Foundation Express
Core
Generation
Utilities
Model Development

## Slide 49: FPGA Design Flow 2
Model development:
  VHDL code
  State-machines may be described in a graphical manner and translated into VHDL code.
  Traditional schematic capture can be translated into VHDL source.
Behavioral Simulation
  Before synthesis; for testing functional correctness
Synthesis
  The design is synthesized to a library of primitive components such as gates, flip-flops, and latches
Functional Simulation
  To find out preliminary performance estimates
  For example, timing information can be obtained from known properties of FPGA components
  Still not too accurate

## Slide 50: FPGA Design Flow 3
Place and Route:
  The design in mapped to the primitives in the target chip
  In FPGA, there are function generators, flip-flops, and latches
  Each primitive must be assigned to a specific CLB (Placement)
  Connections between CLBs that implement the primitives must be established (routing)
  Accurate timing can be obtained in Verification step (Post-placement and routing simulation)
  The configuration bits are generated.

## Slide 51: FPGA Design Flow 4
Programming:
  The configuration data (bit stream) is finally loaded into the target FPGA chip.
These steps are fairly generic although the terminology used here is adopted from Xilinx.

## Slide 52: Xilinx Foundation Tools: Design Flow

## Slide 53: Efficient Design
Generally, we try to reduce the number of flip-flops in the design
  X4000 (like many other FPGAs) has two flip-flops in a CLB
  Instead of trying to reduce the number of flip-flops, try to reduce the number of CLBs and interconnects between them
One-Hot State Assignment
  Use one flip-flop for each state (N state N flip-flops)

## Slide 54: One-Hot State Assignment: Example
Four states: T0, T1, T2, and T3.
Four flip-flops: Q0, Q1, Q2, and Q3.
Assignment:
T0: (1000), T1: (0100), T2: (0010), T3: (0001).
T0
T1
T2
T3
X1/Z1
X2/Z2
X3/Z1
X4/Z2
Q3+ = X1Q0Q1’Q2’Q3’ +
X2Q0’Q1Q2’Q3’ +
X3Q0’Q1’Q2Q3’ +
X4Q0’Q1’Q2’Q3
= X1Q0 + X2Q1 +
X3Q2 + X4Q3
Z1 = X1Q0 + X3Q2
Z2 = X2Q1 + X4Q3

## Slide 55: One-Hot State Assignment: Example
With One-Hot state assignment, the next state and output equations will contain one term for each arc leading into the corresponding state.
Resetting the system requires one flip-flop be set to 1 instead of resetting all flip-flops to 0.
  If flip-flops do not have a preset input (as in the case for the Xilinx 3000 series).
  New assignment: T0: (0000), T1: (1100), T2: (1010), T3: (1001).
  Q3+ = X1Q0’ + X2Q1 +X3Q2 + X4Q3
  Z1 = X1Q0’ + X3Q2 and Z2 = X2Q1 + X4Q3

## Slide 56: Typical FGPA
XC4003 FPGA
  Aprox. 3000 gates
  100 CLBs (10 x 10)
  80 user I/Os
  360 flip-flops (200 in CLBs and 160 in the IOB)
  45536 configuration bits
XC4010E/XL
  7000 – 20000 Gates
  400 CLBs ( 20 x 20)
  160 User I/O
  1120 flip-flops
  Several hundred bits of configuration data per CLB

## Slide 57: Summary
Simulation Model
  Discrete event execution model for VHDL programs
  Accuracy vs. time
Synthesis Model
  Need for inference from language constructs
  Basic principles behind the use of FPGAs
  Challenges in the design flow