## Slide 1: VHDL Basic I/O
EL 310
Erkay Savaş
Sabancı University

## Slide 2: Basic I/O and Its Applications
Objects of file type
  it is a special type that serve as an interface between the VHDL programs and the host environment.
Motivation
  how file objects are created, read, written and used within VHDL simulations
To get it right
  File input and output cannot be synthesized
  I/O operations do not refer to I/O pins of FPGA chips

## Slide 3: Test Benches with File Object
Test bench
  VHDL programs for testing VHDL models
A typical test bench
  reads test inputs from a file
  applies them to the VHDL model under test
  and records model outputs for analysis

## Slide 4: Basic I/O Operations
Type of a file object
  depends what sort of data is stored in them
  can be anything: integer, string, real number, std_logic_vector, etc.
Three types of basic operations
  Declaration of a file and its type
  opening and closing a file of a specified type
  reading and writing a file.

## Slide 5: File Declarations
Syntax
  type TEXT is file of string; -- ASCII
  type INTF is file of integer;
  The first types of files contain ASCII characters, that form human readable text.
  The second can store sequence of integers that are stored in binary form.
  string and integer are predefined types of the language and can be found in the package STANDARD.
  file integer_file: INTF;
  file input_file: TEXT;

## Slide 6: File Declarations
TEXT is also a predefined type in the package TEXTIO.
  we will learn more about it.
The files integer_file and input_file can be thought of pointers to files contains sequences of integers and characters, respectively.
  they are also being called as file handles.

## Slide 7: Opening and Closing Files
After declaration, files must be opened prior to use
After use the files must be closed
We have procedures for opening and closing files:
procedure FILE_OPEN(file file_handle: FILE_TYPE; File_Name: in STRING; Open_Kind: in FILE_OPEN_KIND:=READ_MODE);
procedure FILE_OPEN(File_Status: out FILE_OPEN_STATUS; file file_handle: FILE_TYPE; File_Name: in STRING; Open_Kind: in FILE_OPEN_KIND:=READ_MODE);
procedure FILE_CLOSE(file file_handle: FILE_TYPE);

## Slide 8: Opening and Closing Files
file file_handle: FILE_TYPE; -- pointer to the file
File_Name: in STRING –- name of the file
Open_Kind: in FILE_OPEN_KIND:=READ_MODE –- in which mode the file is to be opened.
The opening modes for a file:
  READ_MODE -- default mode
  WRITE_MODE
  APPEND_MODE
File_Status: out FILE_OPEN_STATUS -- the result of the procedure FILE_OPEN. Four values:
  OPEN_OK
  STATUS_ERROR
  NAME_ERROR
  MODE_ERROR

## Slide 9: Example
-- declare a file type in the architecture declarative region
type IntegerFileType is file of integer; process is file data_in: IntegerFileType; -- declare the file handle
variable fstatus: file_open_status; -- declare file -- status variable of file_open_status type
-- other declarations
begin file_open(fstatus, datain, “myfile.txt”, read_mode); -- -- body of process; reading and writing files and -- performing computations -- end process; -- termination implicitly causes a call to FILE_CLOSE

## Slide 10: Example: Implicit File Open
-- declare a file type in the architecture declarative region
type IntegerFileType is file of integer; process is -- implicitly open a file in file declaration file data_in: IntegerFileType open read_mode is “my_file.txt”;
-- other declarations begin -- -- body of process; reading and writing files and -- performing computations -- end process; -- termination implicitly causes a call to FILE_CLOSE

## Slide 11: Reading & Writing Files
The standard VHDL subprograms
  procedure READ(file file_handle: FILE_TYPE; value: out type);
  procedure WRITE(file file_handle: FILE_TYPE; value: in type);
  function ENDFILE(file file_handle: FILE_TYPE) return Boolean;
The read/write functions can be used after the file is opened.
The language supports reading and writing from files of the predefined types of the language.
For other types, you need to write your own I/O procedures built on these basic procedures.

## Slide 12: VHDL 1987 I/O
VHDL 1993
  file infile: text open read_mode is “inputdata.txt”;
  file outfile: text open write_mode is “outputdata.txt”;
VHDL 1987
  file infile: text in is “inputdata.txt”;
  file outfile: text out is “outputdata.txt”;
  procedure READ(file file_handle: FILE_TYPE; value: out type);
  procedure WRITE(file file_handle: FILE_TYPE; value: in type);
  function ENDFILE(file file_handle: FILE_TYPE) return Boolean;
  No explicit FILE_OPEN and FILE_CLOSE

## Slide 13: Example
entity io93 is end entity io93;
architecture beh of io93 is begin
process is
type IntegerFileType is file of integer;
file data_out: IntegerFileType;
variable fstatus: FILE_OPEN_STATUS;
variable count: integer:= 0;
begin
file_open(fstatus, data_out, “myfile.txt”, write_mode);
for i in 1 to 8 loop write(data_out, count); count := count + 2; end loop;
wait;
end process;
end architecture beh;

## Slide 14: The Package TEXTIO
A standard package supported by all VHDL simulators.
It provides a standard set of file types, data types, and I/O functions.
TEXTIO is in the library STD;
The library STD does not have to be explicitly declared.
However, the packages must be declared in order to use the package content
  use STD.textio.all;

## Slide 15: The Package TEXTIO
Standard file type: TEXT
  package provides the procedures for reading and writing the predefined types of the language such as bit, integer, and character.
  See Appendix F in the textbook.
Several lines
  -- A LINE is a pointer to a string type LINE is access STRING;
  -- A file of variable-length ASCII records type TEXT is file of STRING;
  procedure READLINE(file F: TEXT; L: out LINE);
  procedure READ(L: inout LINE; value: out bit);
  procedure WRITELINE(file F: TEXT; L: inout LINE);
  procedure WRITE(L: inout LINE; value: out bit);

## Slide 16: TEXTIO Mechanism
LINE serve as a buffer area for reading and writing
  read() and write() procedures access and operate on this buffer
  They are overloaded and defined for bit, bit_vector, and string.
  readline() and writeline() procedures move the contents of this buffer to and from files.
Access types are similar to pointers in Pascal and C languages.
There are two special file handles called input and output that are defined in the package TEXTIO.

## Slide 17: TEXTIO: input and output
Two special predefined file handles
input and output
they are mapped to the std_input and std_output of the host environment that is the console window of the VHDL simulator.
  file INPUT: TEXT open READ_MODE is “STD_INPUT”;
  file OUTPUT: TEXT open WRITE_MODE is “STD_OUTPUT”;

## Slide 18: Example: TEXTIO
use STD.textio.all;
entity formatted_io is end entity;
architecture beh of formatted_io is begin
process is
file outfile: text;
variable f_status: FILE_OPEN_STATUS;
variable count: integer := 5;
variable value: bit_vector(3 downto 0) := x”6”;
variable buf: LINE; -- buffer between the program and file
begin
file_open(fstatus, outfile, “myfile.txt”, write_mode);
... end process; end architecture beh;

## Slide 19: Example: TEXTIO
... process is begin
file_open(f_status, outfile, “myfile.txt”, write_mode);
L1: write(buf, string'("This is an example of formatted IO"));
L2: writeline(outfile, buf);
L3: write(buf, string'("The first parameter is="));
L4: write(buf, count);
L5: write(buf, ' ');
L6: write(buf, string'("The second parameter is="));
L7: write(buf, value);
L8: writeline(outfile, buf);
L9: write(buf, string'(“... and so on"));
L10: writeline(outfile, buf);
L11: file_close(outfile);
wait;
end process; end architecture beh;

## Slide 20: ModelSim Note
A common error when calling
  WRITE (L, "hello"); or
  WRITE (L, "010111");
  will cause the following error
  ERROR: Subprogram "WRITE" is ambiguous.
In the TextIO package, the WRITE procedure is overloaded for the types STRING and BIT_VECTOR.
  procedure WRITE(L: inout LINE; VALUE: in BIT_VECTOR; JUSTIFIED: in SIDE:= RIGHT; FIELD: in WIDTH := 0);
  procedure WRITE(L: inout LINE; VALUE: in STRING; JUSTIFIED: in SIDE:= RIGHT; FIELD: in WIDTH := 0);

## Slide 21: ModelSim Note
"hello" could be interpreted as a string or a bit
Use the following syntax: WRITE (L, string’("hello")); WRITE (L, bit_vector’(" 010111 "));

## Slide 22: Output of The Program
buf of LINE type can be accessed by only write and read procedures.
The file “myfile.txt” will contain
This is an example of formatted IO
The first parameter is=5 The second parameter is=0110
... and so on
If you write “STD_OUTPUT” instead of “myfile.txt” then the output will be written to simulator console (ModelSim’s Main Window )
Note that “STD_OUTPUT” must be in capital letters.

## Slide 23: Yet Another Example
use STD.textio.all;
entity formatted_io_02 is end entity;
architecture beh of formatted_io_02 is begin process is
file infile, outfile: text; -- two files
variable f_status: FILE_OPEN_STATUS;
variable buf_in, buf_out: LINE; -- buffers between the -- program and file
variable count: integer;
begin file_open(f_status, infile, "STD_INPUT", read_mode);
file_open(f_status, outfile, "STD_OUTPUT", write_mode);
...
end process;
end architecture beh;

## Slide 24: Yet Another Example
... process is ... begin
L1: write(buf_out, string'("This is an example of formatted IO"));
L2: writeline(outfile, buf_out);
L3: write(buf_out, string'("Enter the parameter"));
L4: writeline(outfile, buf_out);
L5: readline(infile, buf_in);
L6: read(buf_in, count);
L7: write(buf_out, string'("The parameter is="));
L8: write(buf_out, count);
L9: writeline(outfile, buf_out);
L10: file_close(outfile);
wait;
end process;
end architecture beh;

## Slide 25: Yet Another Example

## Slide 26: Use of STD_OUTPUT

## Slide 27: STD_INPUT and STD_OUTPUT
use STD.textio.all;
entity formatted_io_02 is end entity;
architecture beh of formatted_io_02 is begin process is
variable count: integer;
variable buf_in, buf_out: LINE; -- buffers between the -- program and file
begin ...
end process;
end architecture beh;

## Slide 28: STD_INPUT and STD_OUTPUT
variable count: integer;
variable buf_out, buf_in: LINE;
begin
L1: write(buf_out, string'("This is an example of formatted IO"));
L2: writeline(output, buf_out);
L3: write(buf_out, string'("Enter the parameter"));
L4: writeline(output, buf_out);
L5: readline(input, buf_in);
L6: read(buf_in, count);
L7: write(buf_out, string'("The parameter is="));
L8: write(buf_out, count);
L9: writeline(output, buf_out);
wait;
end process;
end architecture beh;

## Slide 29: Dealing with std_logic_vector
library IEEE; use IEEE.std_logic_1164.all;
use STD.textio.all;
package classio is
procedure read_v1d(file f: text; v: out std_logic_vector);
procedure write_v1d(file f: text; v: in std_logic_vector);
end package classio;
package body classio is
...
end package body classio;
Aim: to create a package that contains procedures to
handle reading and writing of std_logic_vector type
objects in a human-readable format.

## Slide 30: Classio Package
package body classio is procedure read_v1d(file f: text; v: out std_logic_vector) is
variable buf: line; variable c: character;
begin
readline(f, buf); -- complete line is read into buffer buf
for i in v’range loop read(buf, c); case c is when ‘X’ => v(i) := ‘X’; when ‘U’ => v(i) := ‘U’; when ‘Z’ => v(i) := ‘Z’; when ‘0’ => v(i) := ‘0’; when ‘1’ => v(i) := ‘1’; when ‘-’ => v(i) := ‘-’; when ‘W’ => v(i) := ‘W’; when ‘H’ => v(i) := ‘H’; when ‘L’ => v(i) := ‘L’; when others => v(i) := ‘0’; end case; end loop;
end procedure read_v1d;
...
end package body classio;

## Slide 31: Classio Package
package body classio is
... procedure write_v1d(file f: text; v: in std_logic_vector) is
variable buf: line; variable c: character;
begin
for i in v’range loop
case v(i) is when ‘X’ => write(buf, ‘X’); when ‘U’ => write(buf, ‘U’); when ‘Z’ => write(buf, ‘Z’); when ‘0’ => write(buf, character’(‘0’)); when ‘1’ => write(buf, character’(‘1’)); when ‘-’ => write(buf, ‘-’); when ‘W’ => write(buf, ‘W’); when ‘H’ => write(buf, ‘H’); when ‘L’ => write(buf, ‘L’); when others => write(buf, character’(‘0’)); end case; end loop;
writeline(f, buf); end procedure write_v1d;
end package body classio;

## Slide 32: Classio Package

## Slide 33: Using the Classio Package
library IEEE; use IEEE.std_logic_1164.all; use STD.textio.all;
use WORK.classio.all; -- the package classio has been compiled in -- the working directory
entity checking is end entity;
architecture beh of checking is begin process is file infile: TEXT open read_mode is “infile.txt”; file outfile: TEXT open write_mode is “outfile.txt”; variable check: std_logic_vector(15 downto 0) := x”0008”; begin
while not (endfile(infile)) loop read_v1d(infile, check); write_v1d(outfile, check);
end loop; file_close(outfile); wait; end process; end architecture beh;

## Slide 34: The Output of the Example

## Slide 35: Reading File Names From Console
library IEEE;
use IEEE.std_logic_1164.all;
use STD.textio.all;
entity filename is
end entity;
architecture beh of filename is
begin
process is
file thefile: text;
variable buf_out, buf_in: LINE;
variable fname: string(1 to 10);
variable f_status: FILE_OPEN_STATUS;
begin ...

## Slide 36: Reading File Names From Console
...
begin
write(buf_out, string'("Enter file name:"));
writeline(output, buf_out);
readline(input, buf_in);
read(buf_in, fname);
file_open(f_status, thefile, fname, read_mode);
readline(thefile, buf_in);
writeline(output, buf_in);
wait;
end process;
end architecture beh;

## Slide 37: Reading File Names From Console

## Slide 38: Testbenches
Basic testing strategy:
  place the unit in a test frame
  apply it a set of inputs whose corresponding output values are known
  observe the outputs of the unit and compare them against the given output values
Test what?
  the model is operating as designed
  the design itself is correct.
Testing during simulation will save a lot of manufacturing efforts.

## Slide 39: Testbench Model in VHDL
Many simulators provide some tools to construct testbenches.
The VHDL itself is very expressive to construct such testbenches
  Along with the component under test, the units that are generating the input stimulus and comparing the outputs can also be written in VHDL.
VHDL Modules in a testbench
  model.vhd
  tester.vhd
  testbench.vhd

## Slide 40: Testbench Model in VHDL
testbench.vhd
Testbench
output ports
input ports
Model
under test
model.vhd
Tester
tester.vhd

## Slide 41: Example: Testing a D Flip-Flop
library IEEE; use IEEE.std_logic_1164.all;
entity asynch_dff is port (r, s, d, clock: in std_logic; q, qbar: out std_logic); end entity asynch_dff;
architecture beh of asynch_dff is begin
output: process (r, s, clock) is begin if (r = ‘0’) then q <= ‘0’ after 5ns; qbar <= ‘1’ after 5 ns; elsif(s = ‘0’) then q <= ‘1’ after 5ns; qbar <= ‘0’ after 5 ns; elsif(rising_edge(clock)) then q <= d after 5ns; qbar <= not d after 5 ns; end if; end process output;
end architecture beh;

## Slide 42: Sample Test Pattern on D Flip-Flop
d
clock
s
r
10 ns
20
30
40
50
60
70
q

## Slide 43: A Simple Tester
library IEEE; use IEEE.std_logic_1164.all; use STD.textio.all; use WORK.classio.all;
entity asynch_dff_tester is
port(r, s, d, clock: out std_logic; q, qbar: in std_logic);
end entity asynch_dff_tester;
architecture beh of asynch_dff_tester is
begin
clock_process: process is
begin
clock <= '1', '0' after 10 ns;
wait for 20 ns;
end process clock_process;
...

## Slide 44: A Simple Tester
...
architecture beh of asynch_dff_tester is
...
io_process: process is
file infile: TEXT open read_mode is “infile.txt”;
file outfile: TEXT open write_mode is “outfile.txt”;
variable buf: line;
variable msg: string(1 to 20):=“This vector failed!”;
variable check: std_logic_vector(4 downto 0);
begin
...
end process io_process;
end architecture beh;

## Slide 45: A Simple Tester
begin while not (endfile(infile)) loop read_v1d(infile, check); r <= check(4); s <= check(3); d <= check(2); wait for 20 ns;
if(q /= check(1) or qbar /= check(0)) then write(buf, msg); writeline(outfile, buf); write_v1d(outfile, check); end if;
end loop; file_close(outfile); wait; end process io_process;
end architecture beh;

## Slide 46: VHDL Model for Testbench
use WORK.classio.all;
entity asynch_dff_testbench is end entity;
architecture beh of asynch_dff_testbench is
component asynch_dff is port (r, s, d, clock: in std_logic; q, qbar: out std_logic); end component asynch_dff;
component asynch_dff_tester is port(r, s, d, clock: out std_logic; q, qbar: in std_logic); end component asynch_dff_tester;
for T1: asynch_dff_tester use entity WORK.asynch_dff_tester;
for M1: asynch_dff use entity WORK.asynch_dff(beh);
signal tb_set, tb_reset, tb_d, tb_q, tb_qbar, tb_clk: std_logic;
begin
T1: asynch_dff_tester port map (r=>tb_reset, s=>tb_set, d=>tb_d, clock=>tb_clk, q=>tb_q, qbar=>tb_qbar);
M1: asynch_dff port map(r=>tb_reset, s=>tb_set, d=>tb_d, clock=>tb_clk, q=>tb_q, qbar=>tb_qbar);
end architecture beh;

## Slide 47: Test Vectors
infile.txt contains
  11001 01101 11110 10010 10011
  reset set d q qbar
Testbench will write into outfile.txt
  This vector failed! 11001 This vector failed! 10011

## Slide 48: Simulation Results for Testbench

## Slide 49: A Better Tester
begin
wait for 5 ns;
while not (endfile(infile)) loop read_v1d(infile, check); r <= check(4); s <= check(3); d <= check(2); wait for 20 ns;
if(q /= check(1) or qbar /= check(0)) then write(buf, msg); writeline(outfile, buf); write_v1d(outfile, check); end if; end loop; file_close(outfile); wait; end process io_process;
end architecture beh

## Slide 50: A Better Tester

## Slide 51: Tester with ASSERT Statement
io_process: process is file infile: TEXT open read_mode is "infile.txt“; variable check: std_logic_vector(4 downto 0); begin wait for 5 ns; while not (endfile(infile)) loop read_v1d(infile, check); r <= check(4); s <= check(3); d <= check(2); wait for 20 ns;
assert Q = check(1) and Qbar = check(0) report "Test Vector failed!“ severity ERROR;
end loop;
wait; end process io_process;

## Slide 52: Simulator Console

## Slide 53: Testbench Overview
A testbench is a structural model with two components:
  model under test
  tester
Components in tester module
  processes to generate waveforms
  VHDL statements to read test vectors from input files and apply them to the model under test
  VHDL statements to record the outputs that are produced by the model under test in response to the test vectors

## Slide 54: Testbench Template
library Lib1; library Lib2; use Lib1.package_name.all; use Lib2.package_name.all;
entity test_bench_name is end entity;
architecture arch_name of test_bench_name is
component tester_name is port (input signals: in type; output signals: out type); end component tester_name;
component model_name is port (input signals: in type; output signals: out type); end component model_name;
signal internal signals : type:=initialization;
begin
T1: tester_name port map(port=>signal1, ...);
M1: model_name port map(port=>signal1, ...);
end arch_name;

## Slide 55: Other Ways to Create Testbenches
Tabular Approach:
  testbench for 3-bit counter
library ieee; use ieee.std_logic_package.all;
entity counter is
generic (n: integer);
port(clock, reset: in std_logic;
count: inout signed(n-1 downto 0));
end entity;

## Slide 56: Tabular Approach
library ieee;
use ieee.std_logic_1164.all;
use ieee.std_logic_arith.all;
entity counter is
generic (n: integer);
port(clock, reset: in std_logic;
count: inout signed(n-1 downto 0));
end entity;
architecture beh of counter is
begin
counter: process(clock, reset)
begin
if reset = '1' then
count <= (others => '0');
elsif(rising_edge(clock)) then
count <= count + 1;
end if;
end process;
end beh;

## Slide 57: Tester for the Counter 1/5
library ieee; use ieee.std_logic_1164.all; use ieee.std_logic_arith.all;
entity counter_tester is end entity;
architecture beh of counter_tester is
component counter generic(n:integer:=6); port(clock, reset: in std_logic; count: inout signed(n-1 downto 0)); end component;
signal clock, reset: std_logic;
signal count: signed(2 downto 0);
type test_vector is record
clock: std_logic;
reset: std_logic;
count: signed(2 downto 0);
end record;
...

## Slide 58: Tester for the Counter 2/5
type test_vector_array is array(natural range <>) of test_vector;
constant test_vectors: test_vector_array := (
-- reset the counter
(clock => '0', reset => '1', count => "000"),
(clock => '1', reset => '1', count => "000"),
(clock => '0', reset => '0', count => "000"),
-- clock the counter several times
(clock => '1', reset => '0', count => "001"),
(clock => '0', reset => '0', count => "001"),
(clock => '1', reset => '0', count => "010"),
(clock => '0', reset => '0', count => "010"),
(clock => '1', reset => '0', count => "011"),
(clock => '0', reset => '0', count => "011"),
(clock => '1', reset => '0', count => "100"),
(clock => '0', reset => '0', count => "100"),
(clock => '1', reset => '0', count => "101"),
(clock => '0', reset => '0', count => "101"),

## Slide 59: Tester for the Counter 3/5
(clock => '1', reset => '0', count => "110"),
(clock => '0', reset => '0', count => "110"),
(clock => '1', reset => '0', count => "111"),
(clock => '0', reset => '0', count => "111"),
(clock => '1', reset => '0', count => "000"),
(clock => '0', reset => '0', count => "000"),
(clock => '1', reset => '0', count => "001"),
(clock => '0', reset => '0', count => "001"),
(clock => '1', reset => '0', count => "010"),
-- reset the counter
(clock => '0', reset => '1', count => "000"),
(clock => '1', reset => '1', count => "000"),
(clock => '0', reset => '0', count => "000"),
-- clock the counter several times
(clock => '1', reset => '0', count => "001"),
(clock => '0', reset => '0', count => "001"),
(clock => '1', reset => '0', count => "010"),
(clock => '0', reset => '0', count => "010")
);

## Slide 60: Tester for the Counter 4/5
begin
-- instantiate counter under test
CUT: counter generic map(3) port map(clock=>clock, reset=>reset, count=>count);
-- apply test vectors and check results
verify: process is
variable vector: test_vector;
variable errors: Boolean:=false;
begin
for i in test_vectors'range loop
-- get vector i
vector := test_vectors(i);
-- schedule vector i
clock <= vector.clock;
reset <= vector.reset;
-- wait for circuit to settle
wait for 20 ns;

## Slide 61: Tester for the Counter 5/5
-- check output vectors
if count /= vector.count then
assert false
report "counter mulfunctioning";
errors := true;
end if;
end loop;
-- assert reports on false
assert not errors
report "Test vectors failed."
severity note;
assert errors
report "Test vectors passed."
severity note;
wait;
end process;
end beh;

## Slide 62: Simulation Results

## Slide 63: Simulator Console

## Slide 64: Record Data Types
An object of a record type is composed of elements of the same or different types.
  It is analogous to struct type in C.
Example:
  type pin_type is range 0 to 10; type MODULE is record size : integer range 20 to 200; critical_delay : Time; no_inputs : pin_type; no_outputs : pin_type; end record;
  variable nand_comp:module; nand_component:=(50, 20 ns, 3, 2);

## Slide 65: Record Data Types
Examples:
  variable nand_comp: module; signal nand_generic: module;
  nand_generic <= nand_comp;
  nand_comp.no_inputs := 2;

## Slide 66: Array Data Types
An object of an array type consists of elements of the same type.
Examples:
  type ADDRESS_WORD is array(0 to 63) of bit;
  type DATA_WORD is array(7 downto 0) of std_ulogic;
  type ROM is array(0 to 127) of data_word;
  type DECODE_MATRIX is array(positive range 15 downto 1, natural range 0 to 3) of std_ulogic;
  subtype natural is integer range 0 to integer’high;
  subtype positive is integer range 1 to integer’high;

## Slide 67: Array Data Types
Examples
  variable ROM_ADDR: ROM;
  signal ADDRES_BUS: ADDRESS_WORD;
  constant DECODER: DECODE_MATRIX; -- deferred
  variable DECODE_VALUE: DECODE_MATRIX;
  ROM_ADDR(5) := “01000101”;
  DECODE_VALUE := DECODER;
  ADDRESS_BUS(8 to 15) <= x”ff”;
Unconstrained Arrays:
  We specify the number of elements when we declare objects of unconstrained array type.
  Subtype declaration may also specify the dimension.
  type STACK_TYPE is array (integer range<>) of ADDRESS_WORD;

## Slide 68: Array Data Types
  type STACK_TYPE is array (integer range<>) of ADDRESS_WORD;
  subtype stack is stack_type(0 to 63);
  type op_type is (add, sub, mul, div);
  type timing is array (op_type range <>, op_type range <>) of time;
  variable FAST_STK: STACK_TYPE(-127 to 127);
  constant ALU_TIMING: TIMING:= -- ADD, SUB, MUL ((10 ns, 20 ns, 45 ns), -- ADD (20 ns, 15 ns, 40 ns), -- SUB (45 ns, 40 ns, 30 ns)); -- MUL

## Slide 69: Array Data Types
STRING and BIT_VECTOR are two predefined one-dimensional unconstrained array types.
Examples:
  variable message: string(1 to 17):= “Hello, VHDL World”;
  signal rx_bus: bit_vector(0 to 5) := o”37”;
  constant add_code: bit_vector := (‘0’, ‘1’, ‘1’, ‘1’, ‘0’);
No unconstrained array of an unconstrained array
  type memory is array (natural range <>) of std_ulogic_vector;
  type reg_file is array (natural range <>) of bit_vector(0 to 7);

## Slide 70: String Literals
One-dimensional array of characters is called string literal.
  “This is a test”
  “Spike is detected”
  “State “”ready”” entered!”
Two types of objects can be assigned with string literals
  STRING and BIT_VECTOR.
  Example: variable ERROR_MESSAGE: string(1 to 19); error_message := “Fatal Error: ABORT!” variable bus_value: bit_vector(1 to 3); BUS_VALUE := “1101”;

## Slide 71: String Literals
The type of a string literal can also be explicitly stated by qualified expression.
  WRITE(L, BIT_VECTOR’(“1110001”));
  CHARINT’(‘1’, N); -- ambiguous
  CHARINT’(character’(‘1’), N);
Bit String Literals
  X”FF0”;
  B”00_0011_1101”;
  O”327”;
  X”FF_F0_AB”;

## Slide 72: String Literals: Assigning
There are different ways to assign values to an array object
  variable op_codes: bit_vector(1 to 5);
  op_codes := “01001”;
  op_codes := (‘0’, ‘1’, ‘0’, ‘0’, ‘1’);
  op_codes := (2 => ‘1’, 5 => ‘1’, others => ‘0’);
  opcodes := (others => ‘0’);

## Slide 73: Type Conversion
VHDL allows for very restricted type casting:
  sum := INTEGER(polywidth * 1.5);
Type conversion is allowed between closely related types
  Between integer and real
  between array types that have the same dimensions whose index types are closely related and element types are the same
  Any other type conversion is done through user-defined functions.

## Slide 74: Type Conversion Examples
Examples:
  type signed is array (natural range <>) of bit;
  type bit_vector is array(natural range <>) of bit;
  signal FCR: signed(0 to 7);
  signal EMA: bit_vector(0 to 7);
  FCR <= EMA; -- illegal
  FCR <= signed(EMA);
  signal real_sig: real;
  signal int_a, int_b: integer;
  real_sig <= real(int_a)/real(int_b);

## Slide 75: Access Types
Pointers to dynamically allocated object of some other type:
  type pin_type is range 0 to 10; type MODULE is record size : integer range 20 to 200; critical_delay : Time; no_inputs : pin_type; no_outputs : pin_type; end record;
  type PTR is access MODULE;
When they do not point to an object, they have value of null.
  variable mod1ptr, mod2ptr: ptr; -- default value is null;
  mod1ptr := new MODULE;

## Slide 76: Access Types
The objects can be created dynamically
  variable mod1ptr, mod2ptr: ptr; -- default value is null;
  mod1ptr := new MODULE;
  mod1ptr := new MODULE’(25, 10 ns, 4, 9);
Access & misc.
  mod1ptr.size, mod1ptr.critical_dly, etc.
  deallocate(mod1ptr);
  mod1ptr := mod2ptr;
  type bitvec_ptr is access bit_vector;
  variable bitvec1: bitvec_ptr := new bit_vector(“1001”);
  mod2ptr := new MODULE’(critical_dly=>10 ns, no_inputs=>2, no_outputs=>3, size=>100);

## Slide 77: Operators
Logical operators
  not
  associative: and, or, xor, xnor,
  non-associative: nand, nor
  Example: A nand B nand C; -- illegal
Relational
  =, /=, <, <=, >, >=
  bit_vector(‘0’, ‘1’, ‘1’) < bit_vector((‘1’, ‘0’, ‘1’) is true
  type MVL is (‘U’, ‘0’, ‘1’, ‘Z’) MVL’(‘U’) < MVL’(‘Z’) is true
  “VHDL” < “VHDL92” is true

## Slide 78: Operators
Shift Operators
  sll, srl, sla, sra, rol, ror
  Examples:
  “1001010” sll 2 is “0101000”
  “1001010” srl 3 is “0001001”
  “1001010” sla 2 is “0101000”
  “1001010” sra 3 is “1111001”
  “1001010” rol 2 is “0101010”
  “1001010” ror 3 is “0101001”
  “1001010” ror -5 is “0101010”
  “1001010” rol -4 is “0101001”

## Slide 79: Operators
Arithmetic
  +, -, &
  ‘0’ & ‘1’ is “01”
  ‘C’ & ‘A’ & ‘T’ is “CAT
  *, /, mod, rem
  A rem B = A – (A/B)*B
  A mod B = A – B*N –- for some integer N
  abs, **

## Slide 80: Aliases
An alias declares an alternate names for all or part of a named item.
  It provides a convenient shorthand for items that have long names
  Example: signal S: bit_vector (31 downto 0);
sign
31
exponent
30
mantissa
22
0
opcode
31
offset
18
0
base
23
reg
26

## Slide 81: Aliases
Examples:
  signal S: bit_vector (31 downto 0);
  alias sign: bit is S(31);
  alias exponent: bit_vector(7 downto 0) is S(30 downto 23);
  alias mantissa: bit_vector(22 downto 0) is S(22 downto 0);
  alias opcode: bit_vector(0 to 4) is S(31 downto 27);
  alias reg: bit_vector(2 downto 0) is S(26 downto 24);
  alias base: bit_vector(4 downto 0) is S(23 downto 19);
  alias offset: bit_vector(18 downto 0) is S(18 downto 0);