## Slide 1: VHDL Modeling Behavior from Synthesis Perspective - Part A -
EL 310
Erkay Savaş
Sabancı University

## Slide 2: Motivation
Synthesis of VHDL models with process construct.
Processes provide powerful modeling abstraction for simulation purposes.
  modeling complex digital system behavior that cannot be captured with only CSA statements.
Increasing the level of modeling abstraction makes hardware inference process harder.
  More than one hardware implementation is possible
  Inference process has more work to do. Relationship between the language constructs and the real systems is no longer explicit.
  Simple coding guidelines in order to ease the synthesis compiler’s task.

## Slide 3: Synthesis with Processes
Process construct models have similarities to high-level programming languages
  sequential style of high-level programming languages may lead to excessive logic and often long signal paths.
Good rule of thumb:
  Avoid long processes
  promote concurrency within models through the use of multiple processes and CSA statements.
  After all, processes are concurrent to other processes and to CSA statements.

## Slide 4: Recall
Combinational logic
  The value of an output signal is defined for every combination of values of input signals
  “Previous” values do not have to be remembered.
  Make sure that every time a process is executed, each output should be assigned a value.
Sequential logic
  The values of an output signal may depend on “previous” values stored in the circuit
  if-then-else constructs leads to a latch element if else branch does not assign a value to one of the output signals
  Next issue: will edge-sensitive flip-flop or latch be inferred?
  wait until (falling_edge(clk));

## Slide 5: One Old Example
library IEEE; use IEEE.std_logic_1164.all;
entity sig_var is port(x,y,z: in std_logic; res1, res2: out std_logic); end entity sig_var;
architecture behavioral of sig_var is signal sig_s1, sig_s2: std_logic; begin
proc1:process(x,y,z) is –- process 1 using variables variable var_s1, var_s2:std_logic; begin var_s1 := x and y; var_s2 := var_s1 xor z; res1 <= var_s1 nand var_s2; end process;
proc2:process(x,y,z) is –- process 1 using signals begin sig_s1 := x and y; sig_s2 := sig_s1 xor z; res1 <= sig_s1 nand sig_s2; end process; end architecture behavioral;

## Slide 6: Simulation Results

## Slide 7: Example: The Synthesized Logic
Two processes result in identical logic for res1 and res2.
Both circuit are combinational
combinational logic is a natural result of using “variables” that are assigned immediately with values evaluated at the RHS of assignment statements.
z
y
x
res1
res2

## Slide 8: Synplify Pro RTL View
res1 = res2 = z + (xy)’

## Slide 9: Example: The Synthesized Logic
Recall that
  the values of sig_s1 and sig_s2 used when the process proc2 is executed are the ones when the process is invoked,
  Not the values are newly evaluated within the procedure
  This would cause inference of storage elements.
However, compilers generally optimize this sequence to produce combinational logic.
  Thus, signals and variables behave identically with respect to the synthesis in this case.
  Dependency in the sequential execution of signals will increase the critical path.

## Slide 10: Sensitivity List Mismatch
The signal sig_s1 is not in the sensitivity list.
  Therefore, an event on it (caused by another process perhaps) will not lead to the execution of process proc2.
  However, an event on sig_s1 will cause the re-computation of the output values in the synthesized circuit.
Simulation semantics may not match the behavior of the synthesized circuit.

## Slide 11: Data Dependency
Independent of whether variables and signals are used, process statements introduce a data dependency between the process statements
s1 <= ... s2 <= ... s1 ... s3 <= ... s2 ... s4 <= ... s2 ... and so on.
Result: long chain of dependency to calculate s4.
Consequence: a long signal path in the synthesized logic.

## Slide 12: Synthesis of Conditional Statements
If-Then-Else and If-Then-Elsif statements
  All Boolean valued expressions are evaluated sequentially until the first true expression is encountered.
library IEEE; use IEEE.std_logic_1164.all;
entity inf_latch is port(sel,x,y,z: in std_logic; w: out std_logic); end entity inf_latch;
architecture behavioral of inf_latch is variable s1, s2:std_logic; begin process(x,y,z,sel) is begin if (sel = ‘1’) then s1 := x and z; s2 := s1 xor y; w <= s1 and s2; end if; -- w gets a value only conditionally -- hence a latch is inferred. end process;

## Slide 13: Example: Latch Inference
If sel = ‘1’ the new value of the signal w is computed as shown in the code.
Otherwise it will keeps its previous value stored in the latch.
Rule: to avoid unnecessary latched inferred, the signal values should be assigned a value in every branch of conditional statements (both in then and else statements).
remember that we have to make sure that all output signals get a value in every execution of process.
z
y
x
sel
w
L
s1
s2
enable signal
for the latch
E

## Slide 14: Alternative to Avoid Latches
Assign a default value to the signal prior to the if statement
library IEEE; use IEEE.std_logic_1164.all;
entity inf_latch is port(sel,x,y,z: in std_logic; w: out std_logic); end entity inf_latch;
architecture behavioral of inf_latch is variable s1, s2:std_logic; begin process(x,y,z,sel) is begin w <= ‘0’; -- output signal set to a default value to avoid latch if (sel = ‘1’) then s1 := x and z; -- body generates combinational logic s2 := s1 xor y; w <= s1 and s2; end if; end process;

## Slide 15: Avoid Latches by Default Value
z
y
x
sel
w
s1
s2
if sel = ‘0’ the w gets ‘0’

## Slide 16: Efficiency
Avoiding unnecessary latches is one aspect of effective design for combinational circuit synthesis
Efficiency in terms of speed and/or size is the other.
library IEEE; use IEEE.std_logic_1164.all;
entity inference is port(sel,x,y,z: in std_logic; w: out std_logic); end entity inference;
architecture behavioral of inference is variable s1, s2:std_logic; begin process(x,y,z,sel) is begin if (sel = ‘1’) then w <= x and y; else w <= x and z; end if; end process; end architecture;

## Slide 17: Example: Efficiency
The general principle:
combinational logic is generated for each branch of an if-then-else construct.
A multiplexor is generated to select the outcome
z
x
y
w
sel
logic for then part
logic for else part
2-to-1 MUX

## Slide 18: More Efficient Design - 1
a small rearrangement will simplify the design
library IEEE; use IEEE.std_logic_1164.all;
entity inference is port(sel,x,y,z: in std_logic; w: out std_logic); end entity inference;
architecture behavioral of inference is begin process(x,y,z,sel) is variable right: std_logic; begin if (sel = ‘1’) then right := y; else right := z; end if; w <= x and right; end process;
end architecture;

## Slide 19: More Efficient Design - 2
Coding styles help us to control how much hardware is generated.
Golden rule: move complex or hardware intensive operations that are replicated in then and else branches out of the if-then-else statement.
z
x
y
w
sel

## Slide 20: Multiple Levels of Nesting
library IEEE; use IEEE.std_logic_1164.all;
entity nested is port(sel1, sel2, sel3, x,y,z: in std_logic; res: out std_logic); end entity nested;
architecture behavioral of nested is begin process(x, y, z, sel1, sel2, sel3) is begin if (sel1 = ‘1’) then res <= x and y; elsif(sel2 = ‘1’) then res <= y xor z; elsif(sel3 = ‘1’) then res <= x or y; end if; end process;
end architecture;
Question: Is latch inferred?

## Slide 21: Example: Multiple Levels of Nesting
Priority logic is implemented.
What is the highest priority?
z
y
x
sel2
sel1
sel3
res
x + y
y  z
xy
(x+ y) sel1’ sel2’
sel1’ sel2
xysel1
0 if sel1 = sel2 = sel3 = 0
E
L

## Slide 22: Nested If Statements
library IEEE;
use IEEE.std_logic_1164.all;
entity nested_ifs is
port(sel0, sel1, x,y,z: in std_logic;
res: out std_logic);
end entity nested_ifs;
architecture behavioral of nested_ifs is
begin
process(x, y, z, sel0, sel1) is
begin
if (sel0 = '0') then
if (sel1 = '1') then
res <= x and y; else -- included to avoid latch inference res <= '0‘;
end if;
end if;
end process;
end architecture;

## Slide 23: Nested If Statements
Latch is inferred because of the outer if-then-else statement

## Slide 24: Nested If Statements
library IEEE;
use IEEE.std_logic_1164.all;
entity nested_ifs is
port(sel0, sel1, x,y,z: in std_logic;
res: out std_logic);
end entity nested_ifs;
architecture behavioral of nested_ifs is
begin
process(x, y, z, sel0, sel1) is
begin
if (sel0 = '0') then
if (sel1 = '1') then
res <= x and y; end if;
end if;
end process;
end architecture;

## Slide 25: Nested If Statements
Remove the inner if-then-else from the outer one in order to infer combinational logic

## Slide 26: Don’t Cares in Conditional Expressions
comparisons with don’t cares in conditional expressions return always FALSE.
library IEEE; use IEEE.std_logic_1164.all;
entity sig_var is port(sel: in std_logic_vector(1 downto 0); x,y,z: in std_logic; w: out std_logic); end entity sig_var;
architecture behavioral of sig_var is begin process(x, y, z) is begin if (sel = ‘-0’) then w <= x xnor y; else w <= x xnor z; end if; end process;
end architecture;

## Slide 27: Don’t Cares in Conditional Expressions
Synthesis compiler generates a logic in which then branch is never taken

## Slide 28: Case Statement
Case statement is similar to if-then-else constructs
  but identifies mutually exclusive blocks of code.
  Only one branch of a case statement can be true
  and collectively all branches cover all possible values of select expression.
  The others clause helps cover all possible values of select expression
  Selecting one of the several possible alternatives suggests that a multiplexor is inferred.
  Select expression provides the control signals for multiplexor.

## Slide 29: Case Statement: Example
A combinational logic is inferred when output signals receive a value in all branches of the case
library IEEE; use IEEE.std_logic_1164.all;
entity case_ex is port(sel: in integer range 0 to 3; x,y,z: in std_logic; res: out std_logic); end entity case_ex;
architecture behavioral of case_ex is begin process(x, y, z, sel) is begin case sel is when 0 => res <= x and y; when 1 => res <= y xor z; when 2 => res <= x nand z; when others => res <= x nor z; end case; end process;
end architecture;

## Slide 30: Case Statement: Example
z
y
x
sel(1)
sel(0)
res
(x nor y)
x nand z
(x nor y) when sel=3
when sel=2
y xor z
when sel=1
x and y
when sel=0
sel: in integer range 0 to 3; is mapped to a two-bit signal

## Slide 31: Latch Inference from Case Statement
library IEEE; use IEEE.std_logic_1164.all;
entity case_ex is port(sel: in integer range 0 to 3; x,y,z: in std_logic; res: out std_logic); end entity case_ex;
architecture behavioral of case_ex is begin process(x, y, z, sel) is begin case sel is when 0 => res <= x and y; when 1 => res <= y xor z; when 2 => res <= x nand z; when others => null; -- in this case the value of res -- remains unaltered end case; end process;
end architecture;

## Slide 32: Latch Inference from Case Statement
x
z
y
sel[1:0]
1 when sel = 0
x and y
z xor y
x nand z
latch
1 when sel(0) = 1
1 when sel(1) = 1
don’t enable the latch when sel0,1,2

## Slide 33: Avoiding Latch Using Default Value
entity case_ex is port(sel: in integer range 0 to 3; x,y,z: in std_logic; res: out std_logic); end entity case_ex;
architecture behavioral of case_ex is begin process(x, y, z, sel) is begin res <= ‘0’; case sel is when 0 => res <= x and y; when 1 => res <= y xor z; when 2 => res <= x nand z; when others => null; end case; end process;
end architecture;
Any case statement has an equivalent if-then-elsif form.
Question: what is the difference between the two?

## Slide 34: Using don’t cares in Case Statements
entity case_ex is port(sel: in integer range 0 to 3; x,y,z: in std_logic; res: out std_logic); end entity case_ex;
architecture behavioral of case_ex is begin process(x, y, z, sel) is begin case sel is when 0 => res <= x and y; when 1 => res <= y xor z; when 2 => res <= x nand z; -- when others => res <= ‘0’; when others => res <= ‘-’; end case; end process;
end architecture;
Use don’t cares in when others to let the synthesis tool to optimize the circuit.

## Slide 35: Using don’t cares in Case Statements
circuit output res is not defined for sel = 3

## Slide 36: Loop Statements
For-Loop
  Most common construct for loops supported by synthesis compilers
  At compile-time, it is possible to know when the loops ends; the logic is inferred accordingly.
  With while-loops, when the loop ends may be data dependent.
  Therefore, a state machine controller is synthesized to cycle datapath a data-dependent number of times.
  For-loops, on the other hand, is easy to synthesize. since the number of iterations is known.

## Slide 37: For Loops
Example:
  for N in 3 downto 1 loop shift_reg(N) <= shift_reg(N-1); end loop;
  The loop can easily be replaced by sequential code shift_reg(3) <= shift_reg(2); shift_reg(2) <= shift_reg(1); shift_reg(1) <= shift_reg(0);
  This technique is known as loop unrolling, and it is also being commonly used in conventional languages for optimization purposes.
  In VHDL synthesis, loop unrolling is also used as an optimization technique.

## Slide 38: Loop Unrolling: Example
library IEEE; use IEEE.std_logic_1164.all;
entity iteration is port(clk, reset, data: in std_logic; res: out std_logic_vector(3 downto 0)); end entity iteration;
architecture behavioral of iteration is signal shift_reg: std_logic_vector(3 downto 0); begin process(clk, reset, data) is begin if(rising_edge(clk)) then if(reset = ‘1’) then res <= “0000”; else for N in 3 downto 1 loop shift_reg(N) <= shift_reg(N-1); end loop; shift_reg(0) <= data; res <= shift_reg; end if; end if; end process;
end architecture;

## Slide 39: Loop Unrolling: Example
Latch inference
  Because of if(rising_edge(clk)) then with no else, a storage element will be inferred.
  Bu due to the call to function rising_edge() a flip-flop instead of a latch is inferred.
clk
data
reset
res<0>
res<1>
res<2>
res<3>
Q
Q
Q
Q
Q
Q
Q
Q
E
E
E
E
R
R
R
R
D
D
D
D
D
D
D
D

## Slide 40: While Loop
entity iteration is port(clk, reset, data: in std_logic; res: out std_logic_vector(3 downto 0)) end entity iteration; architecture behavioral of iteration is signal shift_reg: std_logic_vector(3 downto 0); begin process(clk, reset, data) is variable N: integer; begin if(rising_edge(clk)) then if(reset = '1') then res <= "0000"; else N := 3; while N > 0 loop shift_reg(N) <= shift_reg(N-1); N := N - 1; end loop; shift_reg(0) <= data; res <= shift_reg; end if; end if; end process;
end architecture;

## Slide 41: Exit Statement
sum := 1; j := 0;
L2: loop; j := j+21; sum := sum *10; exit when sum > 100; end loop L2;
The exit statement can be used only inside a loop.
It causes execution to jump out of the innermost loop or the loop whose label is specified.
exit [loop-label][when condition];
sum := 1; j := 0; L3: loop; j := j+21; sum := sum *10; if sum > 100 then exit L3; end if; end loop L3;

## Slide 42: Next Statement
A sequential statement that can be used only inside a loop.
Syntax: next [loop-label][when condition];
It results in skipping the remaining statements in the current iteration of the loop;
execution resumes with the first statement in the next iteration of this loop, if one exists.
for j in 10 downto 5 loop if sum < total_sum then sum := sum + 2; elsif sum = total_sum then next; else null; end if; k := k + 1; end loop;

## Slide 43: Next Statement
The next statement can also cause an inner loop to be exited.
L4: for k in 10 downto 1 loop -- statements section 1 L5: loop -- statements section 2 next L4 when WR_DONE = ‘1’; -- statements section 3 end loop L5; -- statements section 4 end loop L4;
When WR_DONE = ‘1’ becomes true, statements section 3 and 4 are skipped, and execution jumps to the beginning of the next iteration of loop L4.
Notice that loop L5 is terminated by next statement.

## Slide 44: Loops
Some synthesis compilers forces the type of the loop index to integers or only a subsets of array types.
The dependencies across iterations of a loop will lead to long signal paths.
Example:
  reg(0)<= datain(0); for N in 1 to 3 loop reg(N) <= reg(N-1) xor datain(N); end loop;
  When you unroll reg(0)<= datain(0); reg(1)<= reg(0) xor datain(1); reg(2)<= reg(1) xor datain(2); reg(3)<= reg(2) xor datain(3);

## Slide 45: Loops: Example
library IEEE;
use IEEE.std_logic_1164.all;
entity iteration is
port(data: in std_logic_vector(3 downto 0);
res: out std_logic_vector(3 downto 0));
end entity iteration;
architecture behavioral of iteration is
signal reg: std_logic_vector(3 downto 0);
begin
forl: process(data) is
begin
reg(0) <= data(0);
for N in 1 to 3 loop
reg(N) <= reg(N-1) xor data(N);
end loop;
res <= reg;
end process;
end architecture;

## Slide 46: Loops: Example

## Slide 47: Sensitivity List in Synthesis
Process is executed when there is an event on any signal in the sensitivity list.
  When a signal is not in the sensitivity list, an event on this signal does not cause the execution of the process.
  However, when the VHDL code is synthesized in to a logic circuit, a change on any signal will lead to the re-calculation of the other signals that depends on this signal.
  Therefore, simulation results after synthesis may not match exactly to those before the synthesis.
  Lesson: Include all signals of process in the sensitivity list when performing simulations.

## Slide 48: Variables
Variables are language objects that is useful in describing the behavior of the circuit.
  They are typically used to transfer values between statements in a process
  Compiler may collapse variable assignment statements and eliminate some of them.
  When it is not possible to do so, then a variable is synthesized to a wire connecting gates.

## Slide 49: Inferring Latches
Question: Is a latch for Aout inferred?
...
L1: if(s1 = ‘1’) then ... L2: if(s2 = ‘1’) then Aout <= ‘1’; else Aout <= ‘0’; end if; end if; ...

## Slide 50: Buffer and Inout Entity Modes
A signal can serve as both a driver and as an output signal
  Aout <= in1 and in2; Bout <= Aout xor in3;
In this case, Aout signal must be defined as either buffer or inout;
It is important for hierarchical models
For the time being, try to avoid situations like this, using the following:
  VarAout := in1 and in2; Bout <= VarAout xor in3; Aout <= VarAout;

## Slide 51: Inference Using Signals vs. Variables
library IEEE; use IEEE.std_logic_1164.all; entity sigvar is port(sel: in std_logic; x, y, z: in std_logic; v: out std_logic); end entity sigvar;
architecture behavioral of sigvar is signal sig_s1: std_logic; begin process(x, y, z, sel) is variable var_s1: std_logic; begin L1: if(sel = '1') then sig_s1 <= x and z; v <= sig_s1 xor y; end if;
L2: if(sel = '0') then var_s1 := x and z; v <= var_s1 xor y; end if; end process;
end architecture;
Question: Find the latches that will be inferred?

## Slide 52: Inference Using Signals vs. Variables
Synthesis using Synopsys

## Slide 53: Inference Using Signals vs. Variables
Synthesis using Synplify Pro
L2
var_s1
sig_s1

## Slide 54: Latch Inference for Variables
library IEEE; use IEEE.std_logic_1164.all; entity sigvar is port(clk, x, y: in std_logic; res: out std_logic); end entity sigvar;
architecture behavioral of sigvar is begin process variable var_s1, var_s2: std_logic; begin wait until(rising_edge(clk)); var_s1 := x nand var_s2; var_s2 := var_s1 xor y; res <= var_s1 xor var_S2;
end process;
end architecture;
Question: Find the latches that will be inferred

## Slide 55: Latch Inference for Variables
Signal res:
  wait until(rising_edge(clk)); statement causes a flip-flop.
  When there is no rising_edge of the clock, the signal res should retain its value.
Variable var_s2:
  variable var_s2 is used before it is defined.
  Variables retain their values across process invocations.
  Therefore, a flip-flop is inferred when a variable is used before it is defined.

## Slide 56: Latch Inference for Variables

## Slide 57: Latch and Flip-Flop Inference
if, case, wait, conditional and selected signal assignment statements can be used to infer latches.
  For example, “if (sel = ‘1’) then“ will lead to the inference of a latch.
if(rising_edge(clk)) then is used to infer an edge-triggered flip-flop.
  if(clk’event and clk = ‘1’) then may not detect a transition from ‘0’ to ‘1’.
  The attribute clk’last_value may be useful in detecting 0-to-1 transition.
  However, it cannot be used in synthesis.
  Use functions rising_edge() or falling_edge().
  The Xilinx XC4000 series FPGAs support both edge-triggered and level-sensitive devices.

## Slide 58: Flip-Flops with Asynchronous Reset
library IEEE; use IEEE.std_logic_1164.all; use IEEE.std_logic_arith.all;
entity counter_async is port(clk, reset: in std_logic; res: out unsigned(3 downto 0)); end entity counter_async;
architecture behavioral of counter_async is begin process(clk, reset) is variable var_count: unsigned(3 downto 0); begin if(reset='1') then res <= "0000";
else if (rising_edge(clk)) then var_count := var_count + 1; res <= var_count;
end if;
end if;
end process;
end architecture;

## Slide 59: Flip-Flops with Asynchronous Resets
Asynchronous clear and set signal can be synthesized only
if they exist in the target library.

## Slide 60: Flip-Flops with Synchronous Resets
library IEEE; use IEEE.std_logic_1164.all; use IEEE.std_logic_arith.all;
entity counter_async is port(clk, reset: in std_logic; res: out unsigned(3 downto 0)); end entity counter_async;
architecture behavioral of counter_async is begin process(clk, reset) is variable var_count: unsigned(3 downto 0); begin if (rising_edge(clk)) then if(reset='1') then res <= "0000"; else var_count := var_count + 1; res <= var_count; end if; end if;
end process;
end architecture;

## Slide 61: Flip-Flops with Synchronous Resets

## Slide 62: Example in the Textbook
library IEEE; use IEEE.std_logic_1164.all; use IEEE.std_logic_arith.all;
entity counter_async is port(clk, reset: in std_logic; res: out unsigned(3 downto 0)); end entity counter_async;
architecture behavioral of counter_async is begin process(clk, reset) is variable var_count: unsigned(3 downto 0); begin if (rising_edge(clk)) then if(reset='1') then res <= "0000"; else var_count := var_count + 1; end if; res <= var_count; end if;
end process;
end architecture;

## Slide 63: Example in the Textbook
What is the reason for this difference?