## Slide 1: VHDL Basic Language Concepts: Simulation
EL 310
Erkay Savaş
Sabancı University

## Slide 2: Motivation
Construct VHDL models of digital systems for the purpose of simulating
Quick start in building useful simulation models
Core set of language constructs for describing attributes of digital systems
  signals, events, propagation delays, concurrency, and waveforms

## Slide 3: Signals 1
Digital systems are about signals
Signal is the basic part of any HDL
The first VHDL object type: signal
Signals may take values such as 1, 0, Z, X, L, H
We can think of signal type as representative of the wires in a digital system in its simplest form
Signals are different from variables
  They have an associated time value.
  A signal receives a value at a specific point in time.
  It retains this value until it receives another value at a point in future.

## Slide 4: Signals 2
A sequence of values assigned to a signal over time is the waveform of the signal
Signals may be declared to be of a specific type
  Integer, real, or character
  If this is the case, signal does not represent a single wire.
  If we are simulating at a higher level of abstraction we wouldn’t be concerned how many bit an integer signal should be assigned.

## Slide 5: Entity-Architecture
Design entity: primary programming abstraction
  Register, logic block, chip, or entire system
What aspects of a digital system we want to describe?
  Interface: how is it connected to other components? (inputs and outputs)
  Function: what does it do for us? Internal behavior of the design (Boolean equations, truth tables, structural description).
a
b
sum
carry

## Slide 6: Modeling a Digital System
VHDL Language provides two distinct constructs to model these two aspects of a digital system:
Entity
Architecture

## Slide 7: Entity Declaration
Case insensitive
Hyphen is not allowed in user supplied names first character must be a letter, last character cannot be underscore
The interface is a collection of input and output ports.
Ports are signals.
They have types, e.g. bit, integer, character, etc.
They have a mode of operation, e.g. in, out, inout (bi-directional)
entity half_adder is
port(a, b: in bit; sum, carry: out bit);
end entity half_adder;
reserved key words
VHDL 1993
a
b
sum
carry

## Slide 8: IEEE 1164 Standard Object Types
Signals may be of different types
  Vendors may define propriety types  incompatibility problem.
  SimVHDL defines a new type called RealSignal that can take on 12 values.
  IEEE 1164 standard is developed to describe the logic systems more accurately.
  The type bit is a part of VHDL.
  But it is not sufficient to simulate the behavior of digital system since a wire can take values such as Z, X, L, H, etc.
  IEEE 1164 Standard offers object type of std_ulogic, std_ulogic_vector

## Slide 9: IEEE 1164
entity half_adder is
port(a, b: in std_ulogic; sum, carry: out std_ulogic);
end entity half_adder;
entity mux is
port(I0, I1: in std_ulogic_vector(7 downto 0); I2, I3: in std_ulogic_vector(7 downto 0); Sel : in std_ulogic_vector(1 downto 0); Z : out std_ulogic_vector(7 downto 0)); end entity mux;
Z
I0
I1
I2
I3
Sel
4x1
MUX

## Slide 10: Example Entity Descriptions
S’
R’
D
Clk
Q
Q’
entity D_ff is
port(D, Clk, R, S: in std_ulogic; Q, Qbar : out std_ulogic); end entity D_ff;
A
B
C
Op
N
Z
entity ALU32 is
port(A, B: in std_ulogic_vector(31 downto 0); C : out std_ulogic_vector(31 downto 0); Op : in std_ulogic_vector(5 downto 0); N, Z: out std_ulogic); end entity ALU32;

## Slide 11: Describing Behavior: Architecture Construct
The signal assignment statement: Description of events on the signals in left-hand-side (LHS) in terms of events on the signals in right-hand-side (RHS).
Specification of propagation delays
Recall: signal values are time-value pairs.
architecture behavioral of half_adder is begin sum <= (a xor b) after 5 ns;
carry <= (a and b) after 5 ns; end architecture behavioral;
a
b
sum
carry

## Slide 12: Architecture Construct
-- VHDL 1993
architecture behavioral of half_adder is
-- place declarations here
begin -- place description of behavior here --
end architecture behavioral;
-- VHDL 1987
architecture behavioral of half_adder is
-- place declarations here
begin -- place description of behavior here --
end behavioral;

## Slide 13: Concurrent Assignment Statements
Signal assignment operator: <=
The operation of digital systems is inherently concurrent
  Many components of a circuit can be simultaneously operating and concurrently driving distinct signals to new values.
  Multiple signal assignment statements are executed concurrently in simulated time and referred to as concurrent signal assignment statements (CSA).

## Slide 14: Simple CAS
When a transition occurs at the right side of the assignment statement, the expression is evaluated and the assignment is scheduled to be performed at a future time determined by the time value after after keyword.
library IEEE; use IEEE.std_logic_1164.all;
entity half_adder is port(x, y: in std_ulogic; sum, carry: out std_ulogic); end entity half_adder;
architecture concurrent_behavioral of half_adder is begin sum <= (a xor b) after 5 ns;
carry <= (a and b) after 5 ns; end architecture concurrent_behavioral;
Textual order is not important
Flow of signals is important
Simulation time does not proceed from one statement to the next

## Slide 15: Simple CAS
b
a
carry
sum
event
5 ns
10
15
20
25
30

## Slide 16: VHDL Libraries
Libraries are repositories for frequently used design entities
  The library clause identifies a library we want to access
  The logical name (IEEE in the example) usually map to a directory in the system
  The directory contains various design units that have been previously compiled.
  A package is one such design unit
  It may contain definition of types, functions, or procedures
  The use clause determines which packages will be accessed in the library.

## Slide 17: IEEE Library

## Slide 18: VHDL Model of a Full Adder
in1
sum
c_in
in2
c_out
s2
s3
s1
-- VHDL 1993
architecture dataflow of full_adder is
-- place declarations here
begin -- place description of behavior here --
end architecture dataflow;

## Slide 19: VHDL Model of a Full Adder
library IEEE; use IEEE.std_logic_1164.all; entity full_adder is port(in1, in2, c_in: in std_ulogic; sum, c_out : out std_ulogic); end entity full_adder; architecture dataflow of full_adder is -- declarations signal s1, s2, s3: std_ulogic; constant gate_delay: Time:= 5 ns;
begin
L1: s1 <= (in1 xor in2) after gate_delay; L2: s2 <= (c_in and s1) after gate_delay; L3: s3 <= (in1 and in2) after gate_delay; L4: sum <= (s1 xor c_in) after gate_delay; L5: carry <= (s2 or s3) after gate_delay;
end architecture dataflow;

## Slide 20: VHDL Model of a Full Adder
Constant: can be declared to be of a specific type. Its value is set at the start of the simulation and cannot be changed during simulation
Time is the only predefined physical type of language.
type TIME is range implementation_defined units fs; -- femtosecond ps = 1000 fs; -- picosecond ns = 1000 ps; -- nanosecond
us = 1000 ns; -- microsecond
ms = 1000 fu; -- millisecond
sec = 1000 ms; -- second min = 60 sec; -- minutes hr = 60 min; -- hours end units;
subtype DELAY_LENGTH is TIME range 0 fs to TIME’HIGH;

## Slide 21: Waveform of Full Adder
in2
in1
L5: c_out = s2 + s3
c_in
L4: sum = s1  c_in
15
20
25
30
35
40
45
L1: s1 = in1  in2
L2: s2 = s1 · c_in
L3: s3 = in1 · in2
5
10

## Slide 22: Activities at 15 ns
Event: in1 (1  0) [in2 0 0 (no event)]
Expressions evaluated because of this event: L1: s1 = in1  in2 (1 0) and L3: s3 = in1 · in2 (00)
s1 and s3 does not take the evaluated values immediately. Instead, they are scheduled to take the evaluated values at 20 ns.
Therefore, expressions L2: s2 = s1 · c_in and L4: sum = s1  c_in use the current value of s1 which is 1.
The scheduled event on s1 is executed at 20 ns, which is itself an event and triggers other events.

## Slide 23: Concurrent Assignment Rules
model of simulation time:
  All statements with event occurring at the current time on signal in the RHS of the signal assignment are evaluated.
  All future events that are generated from the execution of these statements are then scheduled
  Simulation time is advanced to the time of next event.
  Process repeats
  User can specify events, delays, and concurrency
  The order of execution of the statements depends on the flow of values.

## Slide 24: Implementation of Signals 1
Initialized declaration: signal s1 : std_ulogic:=‘0’; (initialization is not necessary)
General form of concurrent signal assignment signal <= value expression after time expression;
A signal has a history of values over time: waveform.
RHS is referred to as waveform element.
Time-value pair is referred to as a transaction.
Can we specify multiple waveform elements? s1 <= (x xor y) after 5 ns, (x or y) after 10 ns, (not x) after 15 ns;
Three transactions will be generated.
The list of all the current transactions pending on a signal is called driver for the signal.
Driver is essentially a waveform on the signal

## Slide 25: Implementation of Signals 2
The transactions that have not been occurred in simulation is called projected output waveform.
Specifying waveforms:
Example: a single waveform element s1 <= ‘0’, ‘1’ after 10 ns, ‘0’ after 20 ns, ‘1’ after 40 ns;
10
20
30
40
50
All waveforms must be ordered in increasing time.
s1 <= ‘0’, ‘1’ after 10 ns, ‘1’ after 5 ns, ‘0’ after 20 ns, ‘1’ after 40 ns  Invalid

## Slide 26: Resolved Signals 1
One assumption
  There is only one driver for a signal.
  In real devices, there may be multiple drivers for a signal, e.g. busses, wired logic.
  s1 <= ‘0’,‘1’ after 10 ns,‘0’ after 20 ns,‘1’ after 40 ns;
  s1 <= ‘1’ after 10 ns,‘1’ after 20 ns,‘0’ after 40 ns;
Resolution function
  A shared signal must be of special type: resolved
  VHDL uses resolution function to resolve driver conflicts
  std_logic and std_logic_vector are resolved versions of std_ulogic and std_ulogic_vector
  User may define new resolved types, but he must also provide an implementation of resolution function.

## Slide 27: STD_ULOGIC
type std_ulogic is( ‘U’, -- Uninitialized ‘X’, -- Forcing unknown ‘0’, -- Forcing 0 ‘1’, -- Forcing 1
‘Z’, -- High impedance
‘W’, -- Weak unknown
‘L’, -- Weak 0
‘H’, -- Weak 1
‘-’, -- don’t care );
subtype std_logic is RESOLVED std_ulogic; RESOLVED is the name of resolution function.

## Slide 28: Resolved Signals 2
‘1’ @ 10 ns
‘0’ @ 5 ns
‘1’ @ 2 ns
driver 1
‘0’ @ 20 ns
‘1’ @ 5 ns
‘0’ @ 4 ns
driver 2
‘1’ @ 20 ns
‘1’ @ 10 ns
driver 3
resolution function
Z signal value

## Slide 29: Resolved Signals 3
function WIRED_OR(inputs: bit_vector) return bit is begin for j in inputs’range loop if(inputs(j)= ‘1’ then return ‘1’; end if; end loop; return ‘0’; end WIRED_OR;
subtype resolved_bit is WIRED_OR bit; -- resolved_bit signal is associated with resolution -- function WIRED_OR

## Slide 30: Conditional Signal Assignment
4-to-1, 8-bit MUX
library IEEE; use IEEE.std_logic_1164.all; entity mux4 is port(in0, in1, in2, in3: in std_logic_vector(7 downto 0); S0, S1: in std_logic; Z : out std_logic_vector(7 downto 0)); end entity mux4; architecture behavioral of mux4 is
begin
Z <= in0 after 5 ns when S0 = ‘0’ and S1 = ‘0’ else in1 after 5 ns when S0 = ‘0’ and S1 = ‘1’ else in2 after 5 ns when S0 = ‘1’ and S1 = ‘0’ else in3 after 5 ns when S0 = ‘1’ and S1 = ‘1’ else “00000000” after 5 ns;
end architecture behavioral;
Question: What does the last statement cover?

## Slide 31: 4-to-1, 8-bit MUX
Any event on input signals in0-in3 or control signals S0, S1 may cause a change in the value of the output signal
  When this happens, all four conditions are checked and appropriate one is evaluated.
  Expressions in the RHS are evaluated in the order they appear.
  This is what is called priority order.
  In the previous example, only one condition holds; thus the order does not matter.
  In some models, priority is important

## Slide 32: Priority Behavior
4-to-2 priority encoder
library IEEE; use IEEE.std_logic_1164.all; entity priority_encoder is port(S0, S1, S2, S3: in std_logic; Z : out std_logic_vector(1 downto 0)); end entity priority_encoder; architecture behavioral of priority_encoder is
begin
Z <= “00” after 5 ns when S0 = ‘1’ else “01” after 5 ns when S1 = ‘1’ else “10” after 5 ns when S2 = ‘1’ else “11” after 5 ns when S3 = ‘1’ else “00” after 5 ns;
end architecture behavioral;
What if S0 and S1 are ‘1’ at the same time?
This model is a combinational logic.

## Slide 33: Unaffected Keyword
Semantics:
  When S2 = ‘1’ and both S0 and S1 have the value ‘0’, then the value of the output signal does not change.
  This model represents a sequential circuit.
  unaffected keyword is only supported in VHDL 1993.
Z <= “00” after 5 ns when S0 = ‘1’ else “01” after 5 ns when S1 = ‘1’ else unaffected when S2 = ‘1’ else “11” after 5 ns when S3 = ‘1’ else “00” after 5 ns;

## Slide 34: Selected Signal Assignment 1
Register file design
  Read-only register file with two reading ports
library IEEE; use IEEE.std_logic_1164.all; entity register_file is port( addr1, addr2: in std_logic_vector(2 downto 0); reg_out_1, reg_out_2 : out std_logic_vector(31 downto 0)); end entity register_file; architecture behavioral of register_file is
signal reg0,reg2: std_logic_vector(31 downto 0):=x”12345678”; signal reg1,reg3: std_logic_vector(31 downto 0):=x”abcdef00”;
begin
...
end architecture behavioral;

## Slide 35: Selected Signal Assignment 2
select is similar to case statement in C.
All choices are evaluated; only one must be true.
Specified choices must cover all the possibilities
Question: Why do we need others in the last statement
...
begin
with addr1 select reg_out_1 <= reg0 after 5 ns when “000”; reg1 after 5 ns when “001”; reg2 after 5 ns when “010”; reg3 after 5 ns when “011”; reg3 after 5 ns when others; with addr2(1 downto 0) select reg_out_2 <= reg0 after 5 ns when “00”; reg1 after 5 ns when “01”; reg2 after 5 ns when “10”; reg3 after 5 ns when “11”; reg3 after 5 ns when others;
end architecture behavioral;

## Slide 36: A Note in Portability
signal reg0,reg2: std_logic_vector(31 downto 0):=x”12345678”;
In some old simulators, hexadecimal values must be converted to the type std_logic_vector.
The function to_stdlogicvector() is available in std_logic_1164 package.
signal reg0,reg2: std_logic_vector(31 downto 0):= to_stdlogicvector(x”12345678”);
CAD vendors offer many type conversion functions with different names in packages
Those kinds of packages are usually in IEEE library.
Check IEEE library.

## Slide 37: VHDL Models with CSAs
Construct Schematic
  Model each component (e.g. gate) as a delay element.
  Draw a schematic interconnecting all the components. Uniquely label each component.
  Identify the input signals as input ports.
  Identify the output signals as output ports.
  All remaining signals are internal signals
  Associate a type with each input, output, and internal signals (e.g. std_logic)
  Make sure that each input port, output port, and internal signal are labeled with a unique name

## Slide 38: An Example Schematic
Delay element model of a digital system
D
D
D
D
D
Input
ports
Output
ports
Component
Internal
signal

## Slide 39: A Template for VHDL with CSA
library library-name-1, library-name-2; use library-name-1.package-name.all; use library-name-2.package-name.all;
entity entity_name is port (input signals: in type; output signals: out type); end entity entity_name;
architecture arch_name of entity_name is -- declare internal signals -- you may have multiple signals of different types signal internal-signal-1: type := initialization; signal internal-signal-2: type := initialization;
begin -- specify value of each signal as a function other signals
internal-signal-1 <= simple, conditional, or selected CSA; internal-signal-2 <= simple, conditional, or selected CSA;
output-signal-1 <= simple, conditional, or selected CSA; output-signal-2 <= simple, conditional, or selected CSA;
end architecture behavioral;

## Slide 40: Block Statement
It disables signal drivers by using guards
block-label: block[(guard-expression)][is] [block-header] [block-declarations] begin concurrent-statements; -- any number or none end block;
If a guard-expression appears in the block statement, there is a signal called GUARD of type Boolean within the block.
B1: block(STROBE=‘1’) begin Z <= guarded not A; end block B1;
CSA statement is executed if the implicit signal GUARD is TRUE. In the example, Z gets the value of A’ when STROBE = ‘1’.

## Slide 41: Block Statement
The signal GUARD can be used explicitly.
B2: block(CLEAR=‘0’ and PRESET=‘1’) begin Q <= ‘1’ when not GUARD else ‘0’; end block B2;
entity d_flip-flop is port(d, clk: in std_logic; q, qbar: out std_logic); end entity d_flip_flop;
architecture behavioral of d_flip_flop is begin
L1: block(clk=‘1’ and not clk’STABLE) signal temp: std_logic; begin temp <= guarded d; q <= temp; q <= not temp; end block L1; end architecture behavioral;
Rising-edge triggered D flip-flop.

## Slide 42: Delay Models
Propagation delay is an important aspect of a component
We need various delay models to accurately represent the behavior of digital circuits.
These are
Inertial
Transport
Delta

## Slide 43: Inertial Delay Model
Digital circuits have inertia.
  It takes a finite amount of time and energy for the output of circuit to respond to any change on the input.
  The change on the input (event) has to persist for certain period of time in order the output to respond.
  Otherwise, there will be no change at the output corresponding to the event.
  This inertial delay model is the default delay model for VHDL programs.

## Slide 44: Inertial Delay Model: Example
Output <= Input + 0 after propagation-delay;
Out1 is the output waveform for delay = 8 ns
Out2 is the output waveform for delay = 2 ns
Any pulse with a width of less than the propagation delay through the gate is rejected.
Out 2
Out 1
Input
Input
Output
8 ns
2 ns
5 ns
10 ns
15 ns
20 ns
25 ns
30 ns
35 ns

## Slide 45: Inertial Delay Model
If the event does not persist for the duration of pulse rejection width the output does not respond
  The VHDL language uses the propagation delay through the component as the default pulse rejection width.
If we know the pulse rejection width of a component, we can use it
sum <= reject 2 ns inertial (x xor y) after 5 ns.
General form in VHDL’93 signal <= reject time-expression inertial value-expression after time-expression.
We cannot specify pulse rejection width in VHDL’87. Delay value is used for this.

## Slide 46: Transport Delay Model
We use transport model for components with no inertia.
  e.g. accurate modeling of wire delays
  With small feature size in modern day circuits, it is important to model the propagation delay of wires.
  Any event is propagated to the output. The change does not have to persist.
  Even very short pulses are propagated in this model.
  sum <= transport (x xor y) after 5 ns;
  Transport model is not commonly used.
  Default delay model is inertial.

## Slide 47: Transport Delay Model: Example
library IEEE; use IEEE.std_logic_1164.all;
entity half_adder is port (a, b: in std_logic; sum, carry: out std_logic); end entity half_adder;
architecture transport_delay of half_adder is signal s1, s2: std_logic := ‘0’; begin s1 <= (a xor b) after 2 ns; s2 <= (a and b) after 2 ns; sum <= transport s1 after 4 ns; carry <= transport s2 after 4 ns;
end architecture transport_delay;
Modeling wires as delay elements
delay type is transport
a
b
sum
carry
wire delay is 4 ns
s1
s2

## Slide 48: Transport Delay Model: Example
b
a
carry
sum
2 ns
4
6
8
10
12
s2
s1
inertial
transport
What if we used inertial delay for wires?

## Slide 49: Inertial vs. Transport
Which model is being used depends on the component
  For example, assume that we have a model of board level design, and VHDL models for chips on the board.
  We may use transport model for the delay experienced by signals connecting chips on the board

## Slide 50: Delta Delays
What if we do not specify any delay? sum <= (x xor y);  sum <= (x xor y) after 0 ns;
we may choose to ignore delays when
  we do not have realistic delay for the components
  we are not interested in physical timing behavior
How can we preserve the concurrency in case of no propagation delays for components
  For functional correctness, we must maintain the correct ordering of events
  VHDL language provides a infinitesimally small delay called delta delay.

## Slide 51: Delta Delays
Assignment takes place a delay of  after the RHS is evaluated.
  If events with zero delay are produced at timestep T, the simulator simply organizes and processes events in time order of occurrence:
  Events at T+ are processed first,
  then events at T+2
  followed by the events occurring 3 seconds later.
  While the time advances with steps of  seconds, the simulation time does not actually proceed.

## Slide 52: Delta Delays: Example
library IEEE; use IEEE.std_logic_1164.all;
entity combinational is port (in1, in2: in std_logic; z: out std_logic); end entity combinational;
architecture behavior of combinational is signal s1, s2, s3, s4: std_logic := ‘0’; begin L1: s1 <= not in1; L2: s2 <= not in2; L3: s3 <= not (s1 and in2); L4: s4 <= not (s2 and in1); L5: z <= not (s3 and s4); end architecture behavior;
in1
in2
s1
s2
s3
s4
z

## Slide 53: Delta Delays: Example
in2
in1
10 ns
20
30
40
50
60
s2
s3
70
z
s1
s4
L1:
L2:
L3:
L4:
L5:

## Slide 54: Delta Delays: Closer Look
At time 10 ns, in2: 1  0
This event leads to another events triggering an event on Z.
event on Z occurs at the same time the event on in2
Simulator does not show the actual trace as below.
in2
s2
s3
z
10 ns
10 + 
10 + 2
10 + 3
20 ns

## Slide 55: Delta Delays
Textual order is not important
Flow of signals counts
library IEEE; use IEEE.std_logic_1164.all;
entity combinational is port (in1, in2: in std_logic; z: out std_logic); end entity combinational;
architecture behavior of combinational is signal s1, s2, s3, s4: std_logic := ‘0’; begin L5: z <= not (s3 and s4); L2: s2 <= not in2; L4: s4 <= not (s2 and in1); L3: s3 <= not (s1 and in2); L1: s1 <= not in1; end architecture behavior;

## Slide 56: Summary
Entity and architecture constructs
Concurrent signal assignments (CSA)
  simple concurrent assignments
  conditional concurrent assignments
  selected concurrent assignments
Constructing models using CSA
  modeling events, propagation delays, and concurrency
Modeling delays
  inertial
  transport
  delta

## Slide 57: Summary (cont)
Signal drivers and waveforms
Shared signals, resolved types, and resolution functions
generating waveforms using waveform elements
events and transactions