## Slide 1: VHDL MIPS32
EL 310
Erkay Savaş
Sabancı University

## Slide 2: MIPS32 Architecture
32 bit architecture
  registers, ALU, instructions, shifter, data and address are 32 bit
Load/Store architecture
  There are special instructions to access memory such as lw (load word) and sw (store word)
  No ALU operation involves an operand from the memory.
RISC based
  simple instructions
  most of the instruction can be completed in five clock cycles

## Slide 3: MIPS32 Registers
Name | Register no | Usage | Preserved on call
$zero | 0 | the constant value 0 | n.a.
$v0-$v1 | 2-3 | values for results and expression evaluation | no
$a0-$a3 | 4-7 | arguments | no
$t0-$t7 | 8-15 | temporaries | no
$s0-$s7 | 16-23 | saved | yes
$t8-$t9 | 24-25 | more temporaries | no
$gp | 28 | global pointer | yes
$sp | 29 | stack pointer | yes
$fp | 30 | frame pointer | yes
$ra | 31 | return address | yes

## Slide 4: Instruction Formats
There are three instruction format types
op
rs
rt
rd
shamt
funct
6 bits 5 bits 5 bits 5 bits 5 bits 6 bits
R type
op
rs
rt
16-bit address
I type
op
26-bit address
J type

## Slide 5: R-type Instruction
op
rs
rt
rd
shamt
funct
6 bits 5 bits 5 bits 5 bits 5 bits 6 bits
R type
sub $s1, $s2, $s3
42
0
17
19
18
0
slt
sub $s1, $s2, $s3
34
0
17
19
18
0
sub
add $s1, $s2, $s3
32
0
17
19
18
0
add
Comments
Example
name
jr $ra
8
0
0
0
31
0
jr

## Slide 6: I-type Instruction
op
rs
rt
16-bit address
I type
name | Example |  |  |  | Comments
lw | 35 | 18 | 17 | Immediate | lw $s1, 100($s2)
sw | 43 | 18 | 17 | Immediate | sw $s1, 100($s2)
beq | 4 | 17 | 18 | Immediate | beq $s1, $s2, 100
bne | 5 | 17 | 18 | Immediate | bne $s1, $s2, 100

## Slide 7: Addressing Modes
op
rs
rt
16-bit address
register
data memory
lw $s1, index($s2)
Base addressing
op
rs
rt
16-bit address
PC
instruction memory
beq $s1, $s2, Loop
PC-relative addressing

## Slide 8: J-type Instructions
instruction memory
j Address
op
26-bit address
J type
op
26-bit address
PC
word
Pseudo-direct addressing
name | Example |  | Comments
j | 2 | Immediate | j 10000
jal | 3 | Immediate | jal 10000

## Slide 9: ALU Symbol & Control
ALU control lines | Function
000 | and
001 | or
010 | add
110 | subtract
111 | Set on less than

## Slide 10: Implementing Instruction Fetch

## Slide 11: Implementing R-Type ALU Operations
op
rs
rt
rd
shamt
funct
6 bits 5 bits 5 bits 5 bits 5 bits 6 bits
rs
rt
rd
add rd, rs, rt

## Slide 12: Implementing Load & Stores
op
rs
rt
Imm
6 bits 5 bits 5 bits 16 bits
rs
rt
Imm
lw rt, index(rs)
rt
load
store

## Slide 13: Implementing Branches
op
rs
rt
Imm
6 bits 5 bits 5 bits 16 bits
rs
rt
Imm
multiply by 4
beq rs, rt,Label

## Slide 14: Building the Datapath
Idea: Use multiplexors to stitch them together

## Slide 15: Control
Control Signals
  Selecting the operations to perform (ALU, load/store, beq, etc.)
  Controlling the flow of data (multiplexor’s select inputs)
  Read/write enable inputs of memory and register file
Information comes from the 32 bits of the instruction

## Slide 16: ALU Control Unit
ALU performs
  addition for loads and stores
  subtraction for branches (beq)
  no operation for jumps
  or the operation is determined by the function field for R-type of information.
ALU Control unit will have the following inputs:
  two-bit control field called ALUOp
  and Function field

## Slide 17: ALU Control Unit
111
slt
101010
slt
10
R-type
001
or
100101
OR
10
R-type
000
and
100100
AND
10
R-type
110
subtract
100010
Subtract
10
R-type
010
add
100000
Add
10
R-type
110
subtract
xxxxxx
Branch equal
01
beq
010
add
xxxxxx
Store word
00
sw
010
xxxxxx
00
add
Load word
lw
ALU control output
Desired ALU action
Funct field
Instruction operation
ALUop
Instruction opcode

## Slide 18: Truth Table for ALU Control Unit
ALUOp |  | Funct field |  |  |  |  |  | Operation
ALUOp1 | ALUOp0 | F5 | F4 | F3 | F2 | F1 | F0 | 
0 | 0 | X | X | X | X | X | X | 010
X | 1 | X | X | X | X | X | X | 110
1 | X | X | X | 0 | 0 | 0 | 0 | 010
1 | X | X | X | 0 | 0 | 1 | 0 | 110
1 | X | X | X | 0 | 1 | 0 | 0 | 000
1 | X | X | X | 0 | 1 | 0 | 1 | 001
1 | X | X | X | 1 | 0 | 1 | 0 | 111
You can map the truth table to gates

## Slide 19: Implementing the Control
ALU Control Block
F0
F(5-0)
Operation
ALUOp
Operation(0)
Operation(2)
Operation(1)
F1
F2
F3
ALUOp(0)
ALUOp(1)

## Slide 20: Datapath with the ALU Control Unit

## Slide 21: Seven Control Signals
Signal name | Effect when de-asserted | Effect when asserted
RegDst | The destination register no comes from rt. | The destination register no comes from rd.
RegWrite | None | Destination register is written with value on Writedata
ALUSrc | 2nd ALU operand comes from Read_Data_2 | 2nd ALU operand is the sign extended, lower 16 bit of the instruction
PCSrc | The PC is replaced by PC + 4 | The PC is replaced by the branch target address
MemRead | None | Memory is read
MemWrite | None | Memory is written
MemtoReg | The value to the register Writedata input comes from the ALU. | The value to the register Writedata input comes from the data memory

## Slide 22: RegDst & RegWrite
read register #1
read register #2
write
register
write
data
Register file
read #1
Write
read #2
RegWrite
RegDst
0
1
rt: Ins[20-16]
load
rd: Ins[15-11]
R-type

## Slide 23: ALUSrc
read register #1
read register #2
write
register
write
data
Register file
read #1
read #2
RegWrite
ALUSrc
32
sign extend
0
1
Imm: Ins[15-0]
16
result
Zero
ALU

## Slide 24: MemtoReg
Address
write
data
Data Memory
read data
MemtoReg
1
0
Zero
To the write data input of Register File
From the read data 2 output of Register File

## Slide 25: PCSrc
PC
0
1
Imm:
Ins[15-0]
Add
Shift left
by 2
32
sign extend
Add
4
PcSrc
zero
branch

## Slide 26: Datapath & Control

## Slide 27: Operation of the Datapath
1
0
1
0
0
0
X
0
X
beq
0
0
0
1
0
0
X
1
X
sw
0
0
0
0
1
1
1
1
0
lw
0
1
0
0
0
1
0
0
1
R-format
ALU Op0
ALU Op1
Branch
Mem
Write
Mem
Read
RegWrite
Memto-Reg
ALUSrc
RegDest
Instruction
Example Flow: beq $s0, $s1, address
The instruction is fetched from memory and PC is incremented
Read two register values
Subtract one from the other, calculate the branch address
Use the zero signal to determine which of the addresses is to be used for fetching the next instruction

## Slide 28: Single Cycle Datapath

## Slide 29: The Stages of an Instruction
MIPS instructions classically take five steps:
Fetch instruction from memory (IF)
Read registers while decoding the instruction (ID)
Execute the operation or calculate an address (EX)
Access an operand in memory (MEM)
Write result into a register (WB)

## Slide 30: Times of Different Instruction Steps
5 ns
2 ns
1ns
2 ns
Branch
6 ns
1 ns
2 ns
1ns
2 ns
R-format
7 ns
2 ns
2 ns
1ns
2 ns
sw
1 ns
2 ns
2 ns
1ns
2 ns
8 ns
lw
Total time
Register write
Data access
ALU
op
Register Read
Inst. Fetch
Instruction class
Clock period that can be used in single-cycle
implementation will be 8 ns for all instruction.

## Slide 31: Pipelined vs. Nonpipelined
Time
2
4
6
8
10
12
14
16
18
Program
execution
order
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
lw $t1, 100($s1)
lw $t2, 200($s1)
lw $t2, 300($s1)
lw $t1, 100($s1)
lw $t2, 200($s1)
lw $t2, 300($s1)
Time
2
4
6
8
10
12
14
16
18
Program
execution
order
IF
EX
MEM
ID
WB
EX
MEM
ID
IF
WB
EX
MEM
ID
IF
WB

## Slide 32: Design of Pipelined Datapath
Break the datapath into smaller segments
Portions of datapath can be shared by instructions
Use registers between two consecutive segments of the datapath to hold the intermediate results.
Pipeline registers
Data transfer between the stages happens through the pipeline registers

## Slide 33: Pipelined Datapath

## Slide 34: Example: IF of lw
Instruction Memory
PC
Registers
Data Memory
Add
Add
ALU
M
U
X
M
U
X
M
U
X
4
Sign Ext
Shift
Left 2
IF/ID
ID/EX
EX/MEM
MEM/WB
16
32

## Slide 35: Example: ID of lw
Instruction Memory
PC
Registers
Data Memory
Add
Add
ALU
M
U
X
M
U
X
M
U
X
4
Sign Ext
Shift
Left 2
IF/ID
ID/EX
EX/MEM
MEM/WB
16
32

## Slide 36: Example: EX of lw
Instruction Memory
PC
Registers
Data Memory
Add
Add
ALU
M
U
X
M
U
X
M
U
X
4
Sign Ext
Shift
Left 2
IF/ID
ID/EX
EX/MEM
MEM/WB
16
32

## Slide 37: Example: MEM of lw
Instruction Memory
PC
Registers
Add
Add
ALU
M
U
X
M
U
X
M
U
X
4
Sign Ext
Shift
Left 2
IF/ID
ID/EX
EX/MEM
MEM/WB
16
32
Data Memory

## Slide 38: Example: WB of lw
Instruction Memory
PC
Add
Add
ALU
M
U
X
M
U
X
M
U
X
4
Sign Ext
Shift
Left 2
IF/ID
ID/EX
EX/MEM
MEM/WB
16
32
Data Memory
Registers

## Slide 39: Corrected Datapath
Instruction Memory
PC
Add
Add
ALU
M
U
X
M
U
X
M
U
X
4
Sign Ext
Shift
Left 2
IF/ID
ID/EX
EX/MEM
MEM/WB
16
32
Data Memory
Registers

## Slide 40: Example 2: Store word, EX stage
Instruction Memory
PC
Registers
Data Memory
Add
Add
ALU
M
U
X
M
U
X
M
U
X
4
Sign Ext
Shift
Left 2
IF/ID
ID/EX
EX/MEM
MEM/WB
16
32

## Slide 41: Example 2: MEM of sw
Instruction Memory
PC
Registers
Add
Add
ALU
M
U
X
M
U
X
M
U
X
4
Sign Ext
Shift
Left 2
IF/ID
ID/EX
EX/MEM
MEM/WB
16
32
Data Memory

## Slide 42: Example 2: WB of sw
Instruction Memory
PC
Registers
Add
Add
ALU
M
U
X
M
U
X
M
U
X
4
Sign Ext
Shift
Left 2
IF/ID
ID/EX
EX/MEM
MEM/WB
16
32
Data Memory
Oops! Nothing happening

## Slide 43: Pipelined Control
PC is written on each clock cycle (no write signal)
No write signals for pipeline registers.
IF stage: no control signal since instruction is read and PC is updated each cycle
ID stage: No control signals
EX stage: RegDst, ALUOp, ALUSrc
MEM stage: branch, MemRead, MemWrite
WB stage: MemtoReg, RegWrite

## Slide 44: Pipelined Datapath with Control Signals
Instruction Memory
PC
Registers
Add
Add
ALU
M
U
X
M
U
X
4
Sign Ext
Shift
Left 2
IF/ID
ID/EX
EX/MEM
MEM/WB
16
32
Data Memory
ALU cntrl
[15 0]
[20 16]
[15 11]
M
U
X
M
U
X
branch
ALUSrc
RegDst
ALUOp
PCSrc
zero
MemWrite
MemRead
RegWrite
MemtoReg
6
rd
rt

## Slide 45: Reminder: Seven Control Signals
Signal name | Effect when deasserted | Effect when asserted
RegDst | The destination register number comes from rt. | The destination register number comes from rd.
RegWrite | None | Destination register is written with value on Writedata
ALUSrc | 2nd ALU op comes from Read data 1 (i.e. rt) | 2nd ALU op is the sign extended, lower 16 bit of the instruction
PCSrc | The PC is replaced by PC + 4 | The PC is replaced by the branch target address
MemRead | None | Memory is read
MemWrite | None | Memory is written
MemtoReg | The value to the register Writedata input comes from the ALU. | The value to the register Writedata input comes from the data memory

## Slide 46: Control Signals for Instructions
Nine control signals that start in the EX stage
Main control unit generates the control signals during the ID stage.
Instruction | EX Stage |  |  |  | MEM Stage |  |  | WB Stage | 
 | RegDest | ALU Op1 | ALU Op0 | ALUSrc | Branch | Mem Read | Mem Write | RegWrite | Memto-Reg
R-format | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0
lw | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 1
sw | x | 0 | 0 | 1 | 0 | 0 | 1 | 0 | x
beq | x | 0 | 1 | 0 | 1 | 0 | 0 | 0 | x

## Slide 47: Control Lines for the Last Three Stages
IF/ID
EX
MEM
WB
ID/EX
EX/MEM
MEM/WB
MEM
WB
WB
Control
instruction

## Slide 48: Pipelined Datapath with Control Signals
Instruction Memory
PC
Registers
Add
Add
ALU
M
U
X
4
Sign Ext
Shift
Left 2
IF/ID
ID/EX
EX/MEM
MEM/WB
16
32
Data Memory
ALU cntrl
[15 0]
[20 16]
[15 11]
M
U
X
M
U
X
branch
ALUSrc
RegDst
ALUOp
PCSrc
zero
MemWrite
MemRead
RegWrite
MemtoReg
EX
M
WB
M
WB
WB
M
U
X
Control

## Slide 49: Example
Show these five instructions going through the pipeline: lw $10, 20($1) sub $11, $2, $3 and $12, $4, $5 or $13, $6, $7 add $14, $8, $9

## Slide 50: Clock 1
IF: lw $10, 20($1)
PC
Registers
Add
Add
ALU
M
U
X
4
Sign Ext
Shift
Left 2
IF/ID
ID/EX
EX/MEM
MEM/WB
16
32
Data Memory
ALU cntrl
[15 0]
[20 16]
[15 11]
M
U
X
M
U
X
branch
ALUSrc
RegDst
ALUOp
PCSrc
zero
MemWrite
MemRead
RegWrite
MemtoReg
EX
M
WB
M
WB
WB
M
U
X
Instruction Memory
00
000
0000
00
000
0
00
0
00
0
0
0
0
0
ID: before<1>
EX: before<2>
MEM: before<3>
WB: …
Control

## Slide 51: Clock 2
IF: sub $11, $2, $3
PC
Add
Add
ALU
M
U
X
4
Sign Ext
Shift
Left 2
IF/ID
ID/EX
EX/MEM
MEM/WB
16
32
Data Memory
ALU cntrl
[15 0]
[20 16]
[15 11]
M
U
X
M
U
X
branch
ALUSrc
RegDst
ALUOp
PCSrc
zero
MemWrite
MemRead
RegWrite
MemtoReg
EX
M
M
WB
WB
M
U
X
Instruction Memory
11
010
0001
00
000
0
00
0
00
0
0
0
0
0
ID: lw $10, 20($1)
EX: before<1>
MEM: before<2>
Registers
WB
Control
WB: …

## Slide 52: Clock 3
IF:and $12, $4, $5
PC
Add
Add
ALU
M
U
X
4
Sign Ext
Shift
Left 2
IF/ID
ID/EX
EX/MEM
MEM/WB
16
32
Data Memory
ALU cntrl
[15 0]
[20 16]
[15 11]
M
U
X
M
U
X
branch
ALUSrc
RegDst
ALUOp
PCSrc
zero
MemWrite
MemRead
RegWrite
MemtoReg
EX
M
M
WB
WB
M
U
X
Instruction Memory
10
000
1100
11
010
0
00
1
00
0
0
0
0
0
ID: sub $11, $2, $3
EX: lw $10, 20($1)
MEM: before<1>
WB: …
Registers
WB
Control

## Slide 53: Clock 4
IF:or $13, $6,$7
PC
Add
Add
ALU
M
U
X
4
Sign Ext
Shift
Left 2
IF/ID
ID/EX
EX/MEM
MEM/WB
16
32
ALU cntrl
[15 0]
[20 16]
[15 11]
M
U
X
M
U
X
branch
ALUSrc
RegDst
ALUOp
PCSrc
zero
MemWrite
MemRead
RegWrite
MemtoReg
EX
M
M
WB
WB
M
U
X
Instruction Memory
10
000
1100
10
000
1
10
0
11
1
0
0
0
ID:and $12, $4, $5
EX: sub $11, $2, $3
MEM: lw $10, 20($1)
WB: …
Registers
WB
Data Memory
Control
0

## Slide 54: Clock 5
IF:add $14, $8, $9
PC
Add
Add
ALU
M
U
X
4
Sign Ext
Shift
Left 2
IF/ID
ID/EX
EX/MEM
MEM/WB
16
32
ALU cntrl
[15 0]
[20 16]
[15 11]
M
U
X
M
U
X
branch
ALUSrc
RegDst
ALUOp
PCSrc
zero
MemWrite
MemRead
RegWrite
MemtoReg
EX
M
M
WB
WB
M
U
X
Instruction Memory
10
000
1100
10
000
1
10
0
10
0
0
1
1
ID:or $13, $6,$7
EX:and $12, $4, $5
MEM:sub …
WB: lw
Registers
WB
Data Memory
Control
0

## Slide 55: Example: Exception in the Pipelined Datapath
0x40 sub $11, $2, $4 0x44 and $12, $2, $5 0x48 or $13, $2, $6 0x4C add $1, $2, $1 0x50 slt $15, $6, $7 0x54 lw $16, 50($7)
Suppose an overflow exception occurs in the add instruction.
Exception handling routine 0x40000040 sw $25, 1000($0) 0x40000044 sw $26, 1004($0)

## Slide 56: Example: clock 6
Instruction Memory
PC
Registers
+
ALU
M
U
X
4
Sign Ext
Shift
Left 2
IF/ID
ID/EX
EX/MEM
MEM/WB
Data Memory
M
U
X
M
U
X
RegWrite
EX
M
WB
Control
M
WB
WB
M
U
X
Hazard
Detection
Unit
=
Forwarding
Unit
+
M
U
X
0
M
U
X
IF.FLUSH
OR
ID.Flush
M
U
X
M
U
X
0
0
EX.Flush
Except
PC
Cause
lw $16, 50($7)
slt $15, $6, $7
add $1, $2, $1
or $13, …
causing an exception

## Slide 57: Example: clock 7
Instruction Memory
PC
Registers
+
ALU
M
U
X
4
Sign Ext
Shift
Left 2
IF/ID
ID/EX
EX/MEM
MEM/WB
Data Memory
M
U
X
M
U
X
RegWrite
EX
M
WB
Control
M
WB
WB
M
U
X
Hazard
Detection
Unit
=
Forwarding
Unit
+
M
U
X
0
M
U
X
IF.FLUSH
OR
ID.Flush
M
U
X
M
U
X
0
0
EX.Flush
Except
PC
Cause
sw $25, 1000($0)
bubble
bubble
bubble
or $13, …