## Slide 1: VHDL Modeling Behavior from Simulation Perspective
EL 310
Erkay Savaş
Sabancı University

## Slide 2: Motivation
Previously
  we modeled the digital components as delay elements and their internal behavior is describe using CSA statements
  This approach works well when modeling digital systems at gate level.
Large and complex systems cannot always be built at gate level.
  The goal is to hide the unnecessary details while capturing and preserving the external behavior.
  More abstraction
  More powerful statements than CSA statements
Process construct

## Slide 3: Modeling Complex Behavior
CSA statements are good for simple operations
  logical operations, simple arithmetic operations etc.
Most digital components feature more complex behaviors
  It is not feasible or possible to capture the behavior of complex digital systems such as CPU, memory, communication protocols with CSA statements.
  Event model can still be used
  Large and complex systems utilize state information
  They incorporate complex data structures

## Slide 4: Memory as a Complex Digital Component
Event model is still valid
  events on input address, data or control lines produce events that can cause the memory model to be executed.
  Memory access for read an write operations can be assigned for propagation delays.
  How about internal behavior of memory
Memory
MemRead
MemWrite
read_data
write_data
address

## Slide 5: Memory
Problems
  How can we represent the memory words?
  How can we address the correct word given the values of address lines?
  How can memory write operations store values to be accessed by subsequent memory read operations?
If VHDL had conventional sequential programming language construct these problems would be easily overcome.
  Concurrent behavior is sometimes not appropriate.
  Array construct, address as an index to this array
  Depending on the value of control signals, we can decide whether the array element is to be read or written

## Slide 6: The Process Statement
Sequential behavior of digital systems is best modeled using the process statement
  8x32-bits memory
library IEEE; use IEEE.std_logic_1164.all; use IEEE.std_logic_arith.all; -- we need this package for 1164 related functions
entity memory is port(address: in unsigned(31 downto 0); -- use unsigned for memory address write_data: in std_logic_vector(31 downto 0); Mem Read, MemWrite: in std_logic; read_data: out std_logic_vector(31 downto 0)); end entity memory;
architecture behavioral of memory is
..
end architecture behavioral;

## Slide 7: The Process Statement for Memory
...
architecture behavioral of memory is
type mem_array is array(0 to 7) of std_logic_vector(31 downto 0); -- define a new type, for memory arrays
begin -- begin for architecture mem_process: process (address, write_data) is variable data_mem: mem_array :=( -- declare a memory array X”0000000”, -- initialize data memory X”0000000”, -- X denotes a hexadecimal number X”0000000”, X”0000000”, X”0000000”, X”0000000”, X”0000000”, X”0000000”);
variable addr: integer;
begin -- begin for process
...
end process mem_process;
end architecture behavioral;
Declarative region of a process

## Slide 8: The Process Statement for Memory
...
begin -- begin for architecture
... begin -- begin for process
L1: addr := conv_integer(address(2 downto 0)); -- this -- conversion function is in std_logic_arith L2: if MemWrite = ‘1’ then -- perform a read or write L3: data_mem(addr) := write_data;
L4: elsif MemRead = ‘1’ then L5: read_data <= data_mem(addr) after 10 ns; end if;
end process mem_process;
end architecture behavioral;
Computational part of a process

## Slide 9: Process Construct
label: process (sensitivity_list)
-- declarative region for variables and constants
begin -- begin for process
...
end process label;
All statements in a process are executed sequentially in the order implied by the text
Therefore, values assigned to variables (not signals though) in a statement are immediately visible to the subsequent statement
Compare sequential nature of statements in a process to concurrent signal assignment statements.

## Slide 10: Properties of Process Construct
Control flow is strictly sequential
  Altered by constructs such as if-then-else or loop statements
  Process can be thought of a traditional sequential program.
  However, a process can assign internally computed values to signals in the interface after a specified delay.
  read_data <= data_mem(addr) after 10 ns; data_mem(addr) := write_data;
  Externally, discrete event execution model is applicable to process.
  Internally, many complex behavior are described.
  With respect to simulation time, a process executes in zero time.

## Slide 11: Sensitivity List
label: process (sensitivity_list)
Concurrent signal assignment statements are executed when there is an event on the signals in RHS of the statement
Process statements are executed when there is an event on the signals in the sensitivity list.
When an input that is not in the sensitivity list changes, process won’t execute
Once started, process executes to the end and may generate further events.
We can think of a process as a big and complex, nevertheless, CSA statement that executes concurrently with other CSA statements.
Or CSA can be seen a simple and special processes.

## Slide 12: Miscellaneous
new type definition:
  type mem_array is array(0 to 7) of std_logic_vector(31 downto 0);
Variable declaration of the new type
  variable data_mem: mem_array := (...);
new type description:
  unsigned in std_logic_arith.
  used for memory addresses.
type conversion function
  conv_integer() in std_logic_arith.
  memory array is indexed by integers.

## Slide 13: Behavioral Models
VHDL models using process constructs are usually referred to as behavioral models.
Like in a structural programming languages, we can write complex VHDL code incorporating several processes and CSA statements.
As we can gain insight, we will know when and how to use processes in order to effectively describe digital systems for both simulation & synthesis
  Behavioral models often make synthesis more challenging while it offers many advantages in simulation

## Slide 14: If-Then-Else and If-Then-Elsif Statements
if MemWrite = ‘1’ then data_mem(addr) := write_data; elsif MemRead = ‘1’ then read_data <= data_mem(addr) after 10 ns; [else] ... end if;

## Slide 15: Case Statement
case expression is when choices => sequential-statements -- branch #1 when choices => sequential-statements -- branch #2 -- Can have any number of branches [when others => sequential-statements ] -– last branch end case;
type week_day is (mon, tue, wed, thu, fri, sat, sun); type dollars is range 0 to 10; variable day: week_day; variable pocket_money: dollars;
case day is when tue => pocket_money := 6; -- branch #1 when mon|wed => pocket_money := 2; -- branch #2 when fri to sun => pocket_money := 7; -- branch #3 when others => pocket_money := 0; -– last branch end case;

## Slide 16: 4-by-1 MUX with Case Statement
library IEEE; use IEEE.std_logic_1164.all;
entity MUX is port(a,b,c,d: in std_logic; ctrl: in std_logic_vector(0 to 1); z : out std_logic); end entity MUX;
architecture mux_behavior of mux is constant mux_delay:time:=10 ns; begin mux_process: process(a,b,c,d,ctrl) is variable tmp:std_logic; begin
case ctrl is when “00” => tmp := a; -- branch #1 when “01” => tmp := b; -- branch #2 when “10” => tmp := c; -- branch #3 when “11” => tmp := d; -- branch #4 when others => tmp := ‘X’; -– last branch end case;
z <= tmp after mux_delay; end process mux_process; end architecture mux_behavior;

## Slide 17: A VHDL Model with Two Processes
library IEEE; use IEEE.std_logic_1164.all;
entity half_adder is port(x, y: in std_logic; sum, carry: out std_logic); end entity half_adder;
architecture behavioral of half_adder is begin sum_proc: process(x, y) is begin if (x = y) then sum <= ‘0’ after 5 ns; else sum <= (x or y) after 5 ns; end if; end process sum_proc;
carry_proc: process(x, y) is begin ... end process carry_proc;
end architecture behavioral;

## Slide 18: A VHDL Model with Two Processes
Each value of the case expression being tested can belong to only one branch of the statement.
A branch can have more then one sequential statement.
The branches of case statements must cover all possible values of expression being tested.
port signals (in the interface) are visible within processes.
We can have a mix of processes and CSA in a VHDL program
carry_proc: process(x, y) is begin case x is when ‘0’ => carry <= x after 5 ns; when ‘1’ => carry <= y after 5 ns; when others => carry <= ‘X’ after 5 ns; end case; end process carry_proc end architecture behavioral;

## Slide 19: Process + CSA
Memory with four 8-bit words.
  One process combined with CSAs.
  A clock is present
library IEEE; use IEEE.std_logic_1164.all; use IEEE.std_logic_arith.all;
entity register_file is port(address, write_data: in std_logic_vector(7 downto 0); Mem Read, MemWrite, clk, reset: in std_logic; read_data: out std_logic_vector (7 downto 0)); end entity register_file;
architecture behavioral of register_file is signal reg0, reg1, reg2, reg3:std_logic_vector(7 downto 0)); begin ...
end architecture behavioral;

## Slide 20: A Register File Model 1
... begin mem_proc: process(clk) is begin if (rising_edge(clk)) then -- wait until next clock edge if reset=‘1’ then –- initialize values on reset reg0 <= x”00”; -- memory locations are reg1 <= x”11”; -- initialized to random values reg2 <= x”22”; reg3 <= x”33”;
elsif MemWrite = ‘1’ then -- if not reset case address(1 downto 0) is when “00” => reg0 <= write_data; when “01” => reg1 <= write_data; when “10” => reg2 <= write_data; when “11” => reg3 <= write_data; when others => reg0 <= x”ff”; end case; endif; endif; end process mem_proc; -- CSA statements
end architecture behavioral;

## Slide 21: A Register File Model 2
... begin mem_proc: process(clk) is begin ... end process mem_proc; -- CSA statements -- memory read is implemented with a conditional signal -- assignment and concurrent to mem_proc process. -- Read operations are not synchronous to rising clk edge. read_data <= reg0 when address( 1 downto 0)=“00” and MemRead = ‘1’ else reg1 when address( 1 downto 0)=“01” and MemRead = ‘1’ else reg2 when address( 1 downto 0)=“10” and MemRead = ‘1’ else reg3 when address( 1 downto 0)=“11” and MemRead = ‘1’ else x”00”;
end architecture behavioral;

## Slide 22: A Register File Model 3
The function rising_edge(clk) is defined in the package std_logic_1164, and is true when the signal clk has just experienced a rising edge (i.e. a true 0-to-1 transition)
  What if the address is out of range?
  Is reset synchronous or asynchronous?
Process for memory write is executing concurrently with a CSA performing memory read operation.
  memory read operation could be included within the process. What if we did so?

## Slide 23: Multiplier

## Slide 24: 32-bit Multiplier 1
library IEEE; use IEEE.std_logic_1164.all; use IEEE.std_logic_arith.all; use IEEE.std_logic_unsigned.all;
entity mult32 is port(multiplicand, multiplier: in std_logic_vector(31 downto 0); product: out std_logic_vector (63 downto 0)); end entity mult32;
architecture behavioral of mult32 is constant module_delay: Time:= 10 ns; begin -- for architecture mult_process: process(multiplier, multiplicand) is variable prod_reg: std_logic_vector(63 downto 0):=X”00000000”; variable multiplicand_reg: std_logic_vector(31 downto 0):=X”00000000”;
begin –- for process ... end process mult_process;
end architecture behavioral;

## Slide 25: 32-bit Multiplier 2
... mult_process: process(multiplier, multiplicand) is ... begin – for process multiplicand_reg := multiplicand; prod_reg(63 downto 0):= X”00000000” & multiplier; -- repeated shift-and-add loop for index in 1 to 32 loop if prod_reg (0)=‘1’ then prod_reg(63 downto 32) := prod_reg(63 downto 32) + multiplicand_reg(31 downto 0); end if; -- perform a right shift with zero fill prod_reg (63 downto 0) :=‘0’ & prod_reg(63 downto 1); end loop; -- write result to output port product <= prod_reg after module_delay;
end process mult_process;
end architecture behavioral;

## Slide 26: What is New?
Loop statements
  for loop: for index in 1 to 32 loop ... end loop;
  while loop: while j < 32 loop ... j := j + 1; end loop;
Concatenation operator &
  Shift right by one bit using concatenation
  prod_reg(63 downto 0) :=‘0’ & prod_reg(63 downto 1);
  There are other ways to implement shift operation
IEEE.std_logic_unsigned package contains the definition for the “+” operator.

## Slide 27: More on Loop
In the for loop
  Loop index variable is declared implicitly.
  It is local to the loop. If a variable or signal is declared with the same name elsewhere in the process or architecture, it is treated as a distinct object. Within the loop, loop index is taken
  loop index cannot be modified in the loop.
While loop enables that the loop index be assigned new values within the body of the loop.
  Thus, the loop can execute for data dependent number of times.

## Slide 28: Process Behavior
Upon initialization all processes are executed once.
Thereafter dataflow determines process execution
  e.g when events occur on the signals in sensitivity list.
  or wait statement is used for process initiation.
  sensitivity list may be imagined as inputs to a digital circuit
  When an input changes, output of the circuit is re-evaluated for the new input independent of whether the output changes its value or not.

## Slide 29: Signals vs. Variables 1
library IEEE; use IEEE.std_logic_1164.all;
entity sig_var is port(x, y, z: in std_logic; res1, res2: out std_logic); end entity sig_var;
architecture behavioral of sig_var is signal sig_s1, sig_s2: std_logic; begin
proc1: process(x,y,z) is variable var_s1, var_s2:std_logic; begin –- for process L1: var_s1 := x and y; L2: var_s2 := var_s1 xor z; L3: res1 <= var_s1 nand var_s2; end process proc1;
proc2: process(x,y,z) is ... end process;
end architecture behavioral;
Two processes: proc1 and proc2

## Slide 30: Signals vs. Variables 2
proc1 uses intermediate variables var_s1, var_s2
proc2 uses intermediate signals sig_s1, sig_s2 (delta delay model)
They demonstrate different execution behaviors
...
proc1: process(x,y,z) is begin L1: var_s1 := x and y; L2: var_s2 := var_s1 xor z; L3: res1 <= var_s1 nand var_s2; end process;
proc2: process(x,y,z) is begin L1: sig_s1 <= x and y; L2: sig_s2 <= sig_s1 xor z; L3: res2 <= sig_s1 nand sig_s2; end process;
end architecture behavioral;

## Slide 31: Signals vs. Variables 3
proc1
  the new value of var_s1 computed in L1 is used in L2 in the same execution
  L3 is executed with the new values of var_s1 and var_s2
proc2
  L1 and L2 computes the new values of sig_s1 and sig_s2.
  These signals will not acquire these new values until after delta delay elapses.
  This means that the new values of sig_s1 and sig_s2 will not be used in this execution of the process.

## Slide 32: Signals vs. Variables 4

## Slide 33: Sensitivity List Subtleties 1
proc2: process(x,y,z)

## Slide 34: Sensitivity List Subtleties 2
proc2: process(x,y,z, sig_s1, sig_s2)

## Slide 35: Sensitivity List Subtleties 2
1st run of the process
  sig_s1 : 01 (an event)
  sig_s2 : 00
  res2 : 1  1
2nd run of the process (after  delay)
  sig_s1 : 11
  sig_s2 : 01 (an event)
  res2 11
3rd run of the process (after 2 delay)
  sig_s1 : 11
  sig_s2 : 11
  res2 : 10

## Slide 36: How Processes Communicate
All of the ports of the entity and the signals declared within an architecture are visible to any process in the architecture.
  A process can read and update these signals.
Processes use these signals to communicate
  For example process A writes signal which is in the sensitivity list of process B
  the event on this signal will cause process B to execute

## Slide 37: Communication Processes 1
Full adder
HA1
HA2
in1
in2
c_in
sum
c_out
s1
s2
s3
Full adder can be modeled as three communicating processes through internal signals: HA1, HA2, OR
  they create events on signals s1, s2 and s3
  s1 must be in the sensitivity list of HA2

## Slide 38: Communication Processes 2
library IEEE; use IEEE.std_logic_1164.all;
entity full_adder is port(in1, in2, c_in: in std_logic; sum, c_out: out std_logic); end entity full_adder;
architecture behavioral of full_adder is signal s1, s2, s3: std_logic; constant delay: Time:=5ns; begin HA1: process(in1,in2) is begin –- for process s1 <= (in1 xor in2) after delay; s3 <= (in1 and in2) after delay; end process HA1;
HA2: process(s1,c_in) is sum <= (s1 xor c_in) after delay; s2 <= (s1 and c_in) after delay; end process HA2;
OR: process(s2,s3) is c_out <= (s2 or s3) after delay; end process OR;
end architecture behavioral;

## Slide 39: The Wait Statement 1
Event model
  CSA: when an event occurs on signal in RHS, then CSA statement is executed
  Process: when an event occurs on signal in the sensitivity list, then process is executed. Otherwise the process is suspended.
Wait statement allows to model circuits
  where output values are computed at specific points in time independent of event on the input
  that respond to only certain events on the input signals (rising edge of the clock)
  provides a more general way of specifying when a process is executed or suspended
  We can suspend the process at multiple points not just beginnings

## Slide 40: The Wait Statement 2
wait for time expression;
  suspend a process for a certain period of time and when this time specified by time expression elapses the process is executed.
  wait for 20 ns;
wait on signal;
  suspend a process until an event occurs on any one of one or more signals
  wait on clk, reset, status;
wait until <condition >
  suspends a process until <condition > becomes TRUE.
wait and sensitivity list shouldn’t be used together.

## Slide 41: Wait Statement: Examples 1
HA2: process(s1,c_in) is sum <= (s1 xor c_in) after delay; s2 <= (s1 and c_in) after delay; end process HA2;
HA2: process sum <= (s1 xor c_in) after delay; s2 <= (s1 and c_in) after delay; wait on s1, c_in end process HA2;
wait for 0 ns; ?
proc2: process begin wait on x, y, z; L1: sig_s1 <= x and y; wait for 0 ns; L2: sig_s2 <= sig_s1 xor z; wait for 0 ns; L3: res2 <= sig_s1 nand sig_s2; end process;

## Slide 42: Wait Statement: Examples 2
y
x
sig_s1
z
5 ns
10
10+
10+2
20
sig_s2
res2
10+3

## Slide 43: Wait Statements: Examples 3
wait on x, y, z;
wait until A = B;
wait for 10 ns;
wait on CLOCK for 20 ns;
wait until SUM > 100 for 50 ns;
wait on CLOCK until SUM > 100;

## Slide 44: Positive-Edge-Triggered D Flip-Flop
D input is sampled at the rising edge of the clock and transferred to the output.
Computation is done at a particular event
wait until(clk’event and clk = ‘1’);
library IEEE; use IEEE.std_logic_1164.all;
entity dff is port(D, clk: in std_logic; Q, Qbar: out std_logic); end entity dff;
architecture behavioral of dff is begin output: process is begin –- for process wait until(clk’event and clk = ‘1’); Q <= D after 5 ns; Qbar <= not D after 5 ns; end process output;
end architecture behavioral;

## Slide 45: Positive-Edge-Triggered D Flip-Flop
clk’event
event is said to be an attribute of signal clk and
the predicate clk’event is TRUE when there is a transition from 0 to 1 in the clock in the most recent simulation cycle.
Recall that an event is a transition on a signal while a transaction occurs on a signal when a new assignment has been made to the signal, but the value may not have changed.
std_logic_1164 package provides useful functions such as rising_edge(clk) and falling_edge(clk).
These functions take a std_logic type signal and return a Boolean value.

## Slide 46: Why Use rising_edge()?
Recall that a signal of type std_logic may have nine different values.
Therefore, the predicate (clk’event and clk = ‘1’) cannot really capture a 0 to 1 transition
  The transition may be X to 1.
  Therefore, use rising_edge() and falling_edge() for detecting a true rising edge and falling edge of a signal, respectively.
Next issue: how do we initialize a flip-flop?
  when a system is powered, flip-flops are set to a known initial state
  However, what we want is to have some control over the initial state

## Slide 47: D Flip-Flops with Asynchronous Inputs
Asynchronous inputs such as Clear or Set and Preset and Reset are used to initialize flip-flops to known states.
  These signals do not work with the clock, on the contrary they override its effect.
DFF
Q
Q’
D
clk
R’
S’
S’ | R’ | clk | D | Q | Q’
0 | 1 | X | X | 1 | 0
1 | 0 | X | X | 0 | 1
1 | 1 | R | 1 | 1 | 0
1 | 1 | R | 0 | 0 | 1
0 | 0 | X | X | ? | ?
Both S and R are active low

## Slide 48: D Flip-Flops with Asynchronous Inputs
During synchronous operation both R and S must be held to 1.
library IEEE; use IEEE.std_logic_1164.all;
entity asynch_dff is port(D, Clk, R, S: in std_logic; Q, Qbar: out std_logic); end entity asynch_dff;
architecture behavioral of asynch_dff is begin output: process(R, S, Clk) is begin –- for process if (R = ‘0’) then Q <= ‘0’ after 5 ns; Qbar <= ‘1’ after 5 ns; elsif (S = ‘0’) then Q <= ‘1’ after 5 ns; Qbar <= ‘0’ after 5 ns; elsif (rising_edge(Clk)) then Q <= D after 5 ns; Qbar <= not D after 5 ns; endif; end process output;
end architecture behavioral;

## Slide 49: Registers and Counters
Constructing a 4-bit register from D flip-flops
library IEEE; use IEEE.std_logic_1164.all;
entity reg4 is port(D: in std_logic_vector(3 downto 0); Cl, enable, Clk: in std_logic; Q: out std_logic_vector(3 downto 0)); end entity reg4;
architecture behavioral of reg4 is begin reg_process: process(Cl, Clk) is begin –- for process if (Cl = ‘1’) then Q <= “0000” after 5 ns; elsif (rising_edge(Clk)) then if(enable = ‘1’) then Q <= D after 5 ns; endif; endif; end process reg_process;
end architecture behavioral;

## Slide 50: How to Model Asynchronous Communication
4 –phase protocol for asynchronous data transfer
  can be modeled two processes communicating via signals.
  The model uses wait statement that can suspend the process at multiple times.
  Not possible with sensitivity list.
RQ
ACK

## Slide 51: How to Model Asynchronous Communication
Transmitter
Receiver
RQ
ACK
transmit_data
input_data

## Slide 52: Asynchronous Communication 1
library IEEE; use IEEE.std_logic_1164.all;
entity handshake is port(input_data: in std_logic_vector(31 downto 0)); end entity handshake;
architecture behavioral of handshake is signal transmit_data: std_logic_vector(31 downto 0); signal RQ, ACK: std_logic; begin transmitter: process is begin –- for process wait until input_data’event; -- wait until input data is -- available transmit_data <= input_data; -- provide the data as producer RQ = ‘1’; wait until ACK = ‘1’; RQ = ‘0’; wait until ACK = ‘0’; end process transmitter;
receiver: process is begin –- for process ... end process receiver; end architecture behavioral;

## Slide 53: Asynchronous Communication 2
library IEEE; use IEEE.std_logic_1164.all;
entity handshake is port(input_data: in std_logic_vector(31 downto 0)); end entity handshake;
architecture behavioral of handshake is signal transmit_data: std_logic_vector(31 downto 0); signal RQ, ACK: std_logic; begin ... transmitter: process is begin –- for process ... end process transmitter;
receiver : process is variable receive_data: std_logic_vector(31 downto 0); begin –- for process wait until RQ = ‘1’; receive_data:= transmit_data; -- read the data as consumer ACK = ‘1’; wait until RQ = ‘0’; ACK = ‘0’; end process receiver; end architecture behavioral;

## Slide 54: Attributes 1
We have seen that an attribute is used to determine various type of information about a signal
  For example, clk’event returns TRUE if there has been a change in the value of the signal
  event is said to be an attribute of a signal
Attributes can also be used to gather information about the other type of VHDL constructs such as entities and arrays.
  Some attributes are predefined by the language
  Programmer can also create attributes

## Slide 55: Attributes 2
An attribute can be a value, function, type, range, signal, or constant that can be associated with certain names within a VHDL description.

## Slide 56: Type of Attributes
Function Attributes
  invokes a function which returns a value
Value Attributes
  returns a constant value
Signal Attributes
  returns a signal
Type Attributes
  returns a type
Range Attributes
  returns a range

## Slide 57: Function Attributes
These attributes represent functions that are called to obtain a value.
Function Attribute | Function
signal_name’event | returns a Boolean value signifying a change on this signal
signal_name’active | returns a Boolean value signifying an assignment made to this signal. This assignment may not be a new value
signal_name’last_event | returns the time since the last event on this signal
signal_name’last_active | returns the time since the signal was last active
signal_name’last_value | returns the previous value of this signal
my_array’length | returns the length of the array my_array

## Slide 58: Function Attributes: Examples
s1’driving: returns FALSE if, the driver for the signal s1 is disconnected; otherwise it returns TRUE.
s1’driving_value: returns the current value of the driver for s1. It is illegal to access this attribute when s1’driving is FALSE.
signal CLOCK: std_logic; constant setup_time: Time:= 5 ns; signal A:std_logic; signal COUNT: integer; if CLOCK = ‘1’ and CLOCK’event then if A’last_event < setup_time then if COUNT=20 and COUNT’last_value=10 then

## Slide 59: Function Attributes: Examples
process begin x <= ‘Z’, ‘1’ after 5ns, ‘1’ after 5ns, null after 15ns, ‘U’ after 25ns; ... x’driving ... -- use of driving attribute ... x’driving_value ... -- use of driving_value -- attribute wait; end process;
‘Z’ @ 
‘1’ @ 5 ns
null @ 15 ns
‘U’ @ 25 ns
x
TRUE
TRUE
FALSE
TRUE
x’driving
‘Z’
‘1’
illegal access
‘U’
x’driving_value

## Slide 60: Value Attributes 1
They return a constant value
For example
  type mem_array is array(0 to 7) of std_logic_vector(31 downto 0);
  mem_array’left = 0
  mem_array’ascending = TRUE
  mem_array’lenght = 8
Another example
  type statetype is (state0, state1, state2, state3);
  statetype’left = state0
  statetype’right = state3
  Do not have to remember the every state we just assign state’left to the state on reset

## Slide 61: Value Attributes 2
Value Attribute | Value
scalar_name’left | returns the leftmost value of scalar_name in its defined range
scalar_name’right | returns the rightmost value of scalar_name in its defined range
scalar_name’high | returns the highest value of scalar_name in its defined range
scalar_name’low | returns the lowest value of scalar_name in its defined range
scalar_name’ascending | returns true if scalar_name has an ascending range of values (VHDL’93)
array_name’length | returns the number of elements
array_name’left | the left bound of array_name
array_name’right | the right bound of array_name

## Slide 62: Value Attributes: Examples
ALLOWED_VALUE’high = ALLOWED_VALUE’left = 31
ALLOWED_VALUE’right = ALLOWED_VALUE’low = 0
WEEK_DAY’left = WEEK_DAY’low = sun
WEEK_DAY’right = WEEK_DAY’high = sat
WORK_DAY’right = WORK_DAY’low = mon
WORK_DAY’left = WORK_DAY’high = fri
ALLOWED_VALUE’ascending is FALSE
WEEK_DAY’ascending is TRUE
WORK_DAY’ascending is FALSE
type ALLOWED_VALUE is range 31 downto 0; type WEEK_DAY is (sun, mon, tue, wed, thu, fri, sat); subtype WORK_DAY is WEEK_DAY range fri downto mon;

## Slide 63: Signal Attributes
Signal attributes create new signals from signals explicitly declared in VHDL models.
  these types of signals are called implicit signals.
  For example, signal_name’delayed(T) create a new signal of the same type, which is delayed by T.
Signal Attribute | Signal
signal_name’delayed(T) | signal delayed by T units of time
signal_name’transaction | returns signal of type bit whose value toggles when signal_name is active
signal_name’quiet(T) | true when signal_name has been quiet for T units of time
signal_name’stable(T) | true when event has not occurred on signal_name for T units of time

## Slide 64: Signal Attributes: Example 1
library IEEE;
use IEEE.std_logic_1164.all;
entity attributes is
port(data:in std_logic_vector(3 downto 0));
end entity attributes;
architecture behavioral of attributes is
signal outtransaction:bit;
signal outdelayed:std_logic_vector(3 downto 0);
begin
outdelayed <= data'delayed(10 ns);
outtransaction <= data'transaction;
end architecture behavioral;

## Slide 65: Signal Attributes: Example 2

## Slide 66: When to Use Implicit Signals?
If we are interested in a change in the value of the signal data for example, we can wait for events on the data‘transaction implicit signal.
Delayed signal is used to check for the relationship between the current value and older value of a signal
wait on ReceiveData’transaction if ReceiveData’delayed(5 ns)- ReceiveData > 5 then ...

## Slide 67: Implicit Signals: Example 1
library IEEE; use IEEE.std_logic_1164.all; entity attributes_01 is port(data:in std_logic_vector(3 downto 0)); end entity attributes_01;
architecture behavioral of attributes_01 is function to_integer(signal arg:std_logic_vector(3 downto 0)) return integer is begin case arg is when "0000" => return 0; when "0001" => return 1; when "0010" => return 2; when "0011" => return 3; when "0100" => return 4; when "0101" => return 5; when "0110" => return 6; when "0111" => return 7; when "1000" => return 8; when "1001" => return 9; when "1010" => return 10; when "1011" => return 11; when "1100" => return 12; when "1101" => return 13; when "1110" => return 14; when "1111" => return 15; when others => return 0; end case; end function to_integer;

## Slide 68: Implicit Signals: Example 2
signal outdelayed:std_logic_vector(3 downto 0):="0000";
signal test: std_logic:='0';
begin
attributes: process(data)
begin
if(to_integer(data)-to_integer(data'delayed(10 ns)) > 1) then
test <= '1';
else
test <= '0';
end if;
end process attributes;
outdelayed <= data'delayed(10 ns);
end architecture behavioral;

## Slide 69: Implicit Signals: Example 3

## Slide 70: Signal Attributes
signal CLOCK_SKEW;
CLOCK_SKEW
5 ns
10
15
20
25
CLOCK_SKEW’DELAYED(5 ns)
5 ns
CLOCK_SKEW’STABLE(4 ns)
4 ns
FALSE
TRUE

## Slide 71: Signal Attributes for Setup Constraint
‘STABLE attribute can be used for catch a setup violation.
  It is required to report a violation if signal DATA has not been stable for the specified SETUP time before the falling edge of the signal CLK occurs.
  Example: process constant SETUP: TIME:=1.2 ns; begin wait until CLK = ‘1’ and CLK’event; assert DATA’STABLE(SETUP) report “setup violation” severity WARNING; end process;

## Slide 72: A D Flip-Flop with Setup & Holdup Violations Check
library IEEE; use IEEE.std_logic_1164.all; entity dff is port(d, clk:in std_logic; q, qbar:out std_logic); end entity dff;
architecture check_times of dff is constant hold_time: Time := 5 ns; constant setup_time: Time := 3 ns; begin process(d, clk) begin -- check for hold time if d’event then assert NOW = 0 ns or clk’last_event >= hold_time report “hold time too short!” severity FAILURE; end if; ... end architecture check_times;
NOW is a predefined function that returns the current simulation time.

## Slide 73: A D Flip-Flop with Setup & Holdup Violations Check
...
-- check for setup time if clk = 1 and clk’event then assert NOW = 0 ns or d’last_event >= setup_time report “setup time too short!” severity FAILURE; end if;
-- behavior of D FF if clk = 1 and clk’event then q <= d; qbar <= not d; end if; end process; end architecture check_times;

## Slide 74: Signal Attributes vs. Function Attributes
Function attributes return value
Signal attributes creates a new signal
  Signal attributes can be used wherever a signal is expected; for example in the sensitivity list of a process
  Example: PSTABLE: process(A, B, CLK’STABLE) begin ... end process;
  It is illegal to use CLK’EVENT, for example, in the sensitivity list.

## Slide 75: Range Attribute
Returns a range
Useful especially when writing loops
  Consider a loop that scans all of the elements in an array value_array();
  The index range is returned by value_array’range.
  We may not know the size of the array after all.
  Example: for i in value_array’range loop ... my_var := value_array(i); ... end loop;

## Slide 76: Range Attribute
Examples:
  variable WBUS: std_logic_vector(7 downto 0);
  WBUS’range returns the range “7 downto 0”
  WBUS’reverse_range returns the range “0 to 7”

## Slide 77: Type Attribute
If T is any type or subtype, T’BASE, which is the only type attribute, returns base type of T
  This attribute cannot be used in expressions since it returns a type.
  It can be used in conjunction with other attributes.
  For example type ALU_OPS is (ADD,SUB,MULT,DIV,AND,NAND,OR,NOR); subtype ARITH_OPS is ALU_OPS range ADD to DIV;
  then ARITH_OPS’BASE is ALU_OPS.
  ARITH_OPS’BASE’LEFT returns ADD.

## Slide 78: User-Defined Attributes 1
Constants of any type (except access or file types)
  They are declared using attribute declarations.
  attribute attribute-name: value-type;
  Example:
architecture beh of user_defined is attribute pin_no: natural; attribute technology: string; ...
They are yet not associated with an entity.
Entity, in this context, could be and entity, a signal, an architecture, a variable, type, subtype, package, procedure, or function.

## Slide 79: User-Defined Attributes 2
architecture beh of user_defined is ... attribute pin_no of Q: signal is 42; attribute technology of all: component is “CMOS”;
To associate
  attribute attribute-name of item-names: name_class is expression;

## Slide 80: Generating Clocks and Periodic Waveforms
library IEEE; use IEEE.std_logic_1164.all;
entity periodic is port(Z: out std_logic); end entity periodic;
architecture behavioral of periodic is begin
process is
begin Z <= ’0’, ‘1’ after 10 ns, ‘0’ after 20 ns, ‘1’ after 40 ns; wait for 50 ns; end process;
end architecture behavioral;

## Slide 81: Generating Clocks and Periodic Waveforms
This process is executed repeatedly with 50 ns period
  recall upon initialization, all processes are executed.
  therefore, every process is executed at least once.
  wait for 50 ns cause the process to be re-executed.
10
20
30
40
50
60

## Slide 82: Generating a Two-Phase Clock
library IEEE; use IEEE.std_logic_1164.all;
entity two_phases is port(phi1, phi2: out std_logic); end entity two_phases;
architecture behavioral of two_phases is begin
reset_process: reset <= ‘1’, ‘0’ after 10 ns; clock_process: process is
begin phi1 <= ‘1’, ‘0’ after 10 ns; phi2 <= ‘0’, ‘1’ after 12 ns, ‘0’ after 18 ns; wait for 20 ns; end process clock_process;
end architecture behavioral;

## Slide 83: Generating a Two-Phase Clock
The pulses in two clock signals are adjusted not to overlap
reset
10 ns
20
30
40
50
phi1
phi2
60
Note that reset process is executed once.
1st run of processes

## Slide 84: Using Signals in a Process
library IEEE; use IEEE.std_logic_1164.all;
entity combinational is port (in1, in2: in std_logic; z: out std_logic); end entity combinational;
architecture behavior of combinational is signal s1, s2, s3, s4: std_logic := ‘0’; begin s1 <= not in1; s2 <= not in2; s3 <= not (s1 and in2); s4 <= not (s2 and in1); z <= not (s3 and s4); end architecture behavior;
in1
in2
s1
s2
s3
s4
z

## Slide 85: Delta Delays: Example
in2
in1
10 ns
20
30
40
50
60
s2
s3
70
z
s1
s4

## Slide 86: Using Signals in a Process 2
library IEEE; use IEEE.std_logic_1164.all;
entity combinational is port (in1, in2: in std_logic; z: out std_logic); end entity combinational;
architecture behavior of combinational is signal s1, s2, s3, s4: std_logic := ‘0’; begin delta_process: process(in1, in2) is begin s1 <= not in1; s2 <= not in2; s3 <= not (s1 and in2); s4 <= not (s2 and in1); z <= not (s3 and s4); end process delta_process; end architecture behavior;

## Slide 87: Using Signals in a Process 3
in2
in1
10 ns
20
30
40
50
60
s2
s3
70
z
s1
s4

## Slide 88: Using Signals in a Process 4
When we made the process sensitive to all signals then we would obtain the identical trace.
 | 0 ns | 10 | 20 | 30 | 40 | 50 | 60 | 70
in1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1
in2 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 0
s1 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0
s2 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 1
s3 | U | 1 | 1 | 1 | 1 | 1 | 1 | 1
s4 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0
z | U | U | 0 | 1 | 1 | 0 | 0 | 0
z<=not(s3 and s4);
s1 <= not in1;
s2 <= not in2;
s3<=not(s1 and in2);
s4<=not(s2 and in1);

## Slide 89: State Machines
Combinational circuits are sensitive to the inputs
  activated when an event occurs on an input signal
Sequential circuits retain information in internal devices such as flip-flops and latches.
  the value stored in these devices are referred to as the state of the circuit.
  There is a finite number of states.
  the output values are computed as functions of both internal state and input signals.
  The internal state is updated at discrete points in time determined by a periodic signal such as clock.

## Slide 90: Finite State Machine (FSM)
Combinational
logic
outputs
inputs
state
next state
clk
s0
s1
0/1
1/0
0/1
1/0
VHDL Model: Two communicating processes
Process implementing combinational component. Sensitive to events on input signals and changes in the state.
Process implementing the sequential component. Sensitive to active edge of the clock

## Slide 91: VHDL Model for FSM 1
library IEEE; use IEEE.std_logic_1164.all;
entity state_machine is port (reset, clk, x: in std_logic; z: out std_logic); end entity state_machine;
architecture behavioral of state_machine is type state_type is (state0, state1); signal state, next_state: state_type := state0; begin ... end architecture behavioral;

## Slide 92: Combinational Part
comb_process: process(state, x) is begin case state is when state0 => if x = ‘0’ then next_state <= state1; z <= ‘1’; else next_state <= state0; z <= ‘0’; end if; when state1 => if x = ‘1’ then next_state <= state0; z <= ‘0’; else next_state <= state1; z <= ‘1’; end if; end case; end process comb_process;

## Slide 93: Sequential Part
clk_process: process is begin
wait until (rising_Edge(clk)); if reset = ‘1’ then state <= state_type’left; else state <= next_state; end if; end process clk_process; end architecture behavioral;
state and next_state are used by two process to communicate values.
Enumerated type is used.
Attributes of enumerated type statetype’left is used to initialize state machine.

## Slide 94: Simulation

## Slide 95: Alternative Model: with One Process
process(clk, state, x) is
begin
if (rising_edge(clk)) then
if reset = '1' then
state <= state_type'left;
z <= '0';
else
case state is
when state0 =>
if x = '0' then state <= state1; z<='1';
else state <= state0; z<='0';
end if;
when state1 =>
if x = '1' then state <= state0; z<='0';
else state <= state1; z<='1';
end if;
end case;
end if;
end if;
end process;

## Slide 96: Simulation
Output signal z changes with clock.

## Slide 97: Alternative Model: with Three Process
... signal state, next_state: statetype := state0; begin output_process: process(state, x) is begin case state is when state0 => if x = ‘1’ then z <= ‘0’; else z <= ‘1’; end if; when state1 => if x = ‘1’ then z <= ‘0’; else z <= ‘1’; end if; end case; end process output_process;
Output Process

## Slide 98: Alternative Model: with Three Process
next_state_process: process(state, x) is begin case state is when state0 => if x = ‘1’ then next_state <= state0; else next_state <= state1; end if; when state1 => if x = ‘1’ then next_state <= state0; else next_state <= state1; end if; end case; end process next_state_process;
Next State Process

## Slide 99: Alternative Model: with Three Process
clk_process: process is begin wait until(rising_edge(clk)); if reset = ‘1’ then state <= statetype’left; else state <= next_state; end if;
end process clk_process;
end architecture behavioral;
Clock Process

## Slide 100: Simulation

## Slide 101: Constructing VHDL Models
library library-name-1, library-name-2; use library-name-1.package-name.all; use library-name-2.package-name.all;
entity entity_name is port(input signals: in type; output signals: out type); end entity entity-name;
architecture arch_name of entity_name is
-- declare internal signals, you may have multiple signals -- of different types signal internal signals: type := initialization;
begin
-- first process -- second process -- simple, conditional, or selected CSA -- other processes or CSAs end architecture arch_name;

## Slide 102: Constructing VHDL Models
architecture arch_name of entity_name is
begin
label-1: process(--sensitivity list--) is --declare variables to be used in the process variable variable names : type:=initialization; begin -- process body end process label-1; label-2: process is --declare variables to be used in the process variable variable names : type:=initialization; begin wait until (--predicate--);
-- sequential statements wait until (--predicate--);
-- sequential statements end process label-2; internal-signal or ports<=simple,conditional,or selected CSA -- other processes or CSAs end architecture arch_name;

## Slide 103: CSA and Process
They can be in the same architecture body
  as many CSA or process as we want
A process and a CSA are concurrently executed with respect to each other.
We use process when the computation of the signal values are too complex for CSA statements.
  variables declared in a process’ declaration field is only visible within this process.

## Slide 104: Common Syntax Errors
elsif (not elseif)
end if (not endif)
no semicolon (;) after then or if-then-elsif construct
10 ns (10ns is incorrect)
underscore is OK in label names (not hyphen)
Some simulators cannot do the following assignment signal X: std_logic_vector(7 downto 0):=“00000000”; we may have to use to_stdlogicvector(“00000000”) first to make this assignment work.

## Slide 105: Common Run-Time Errors
Make sure if you need a signal or variable
  Signals are updated with the evaluated value in the next execution cycle.
  Variables are assigned immediately.
If multiple drivers exist for a signal, the type of the signal must resolved (i.e. a resolution function must be defined and associated).
A process should have either a sensitivity list or a wait statement; not both.
All processes are executed once when the simulation is started.

## Slide 106: Common Run-Time Errors
Be careful of the assigned values of signals wait until rising_edge(clk); sig_a <= sig_x and sig_y; sig_b <= sig_a; Think of sig_a and sig_b are being stored in flip-flops.

## Slide 107: Summary
Processes
Sequential statements
  if-then-else, case, loop
wait statement of sensitivity list
attributes
communicating processes
modeling state machines
using both CSA statements and processes within the same architecture description