## Slide 1: VHDL Basic Language Concepts: Synthesis
EL 310
Erkay Savaş
Sabancı University

## Slide 2: Preliminaries
Synthesis is the process of analyzing a VHDL program and inferring digital circuit that implements the behavior implied by this VHDL description.
The circuit is constructed using a fixed set of hardware primitives.
  AND, OR, NOT,
  XOR, XNOR
  Multiplexor, decoder
Efficient implementation
  inference techniques and subsequent optimizations are specific to target hardware primitives.

## Slide 3: Preliminaries
The actual circuit also depends on the vendor-specific synthesis compiler
  FPGA Express
  Synplify Pro
  Synopsys FPGA_Complier2 (FC2)
Here, we are interested in hardware inference from concurrent signal assignment (CSA) statements.
For the following class of CSA, we will show the inferred circuits for both gate level and FPGA
  simple concurrent assignments
  conditional concurrent assignments
  selected concurrent assignments

## Slide 4: Motivation
To study each language constructs in order to anticipate the hardware that are going to be inferred for each construct.
  There are more than one way to model a hardware component.
  For example, how many bits are required to represent a signal?
  Order in conditional and selected CSA will affect the inferred logic.
If we can know what is going to be inferred from the code we write, we model our digital system in VHDL in such a way that the most effective circuit is produced.

## Slide 5: Compiler’s Job
We need adders; but how many? and how large?,
how many bits to represent Z?
Integers must be at least 32 bits.
What if we deal with smaller integers?
library IEEE; use IEEE.std_logic_1164.all;
entity synth is port (a, b, c ,d: in integer; sel: in std_logic_vector(1 downto 0); Z: out integer); end entity synth;
architecture behavioral of synth is begin
with sel select Z <= a + b when “00”, c + d when “10”, 0 when others; end architecture behavioral;

## Slide 6: How Compiler Synthesizes

## Slide 7: Inference from Declarations 1
In programming languages, variable and constant declarations mean a memory location
Inference for signals
  Wires, latches, and flip-flops
  In combinational circuits, signals corresponds to wires connecting components.
  In sequential circuits, flip-flops or latches are inferred for signals when they are stored.
  Inference depends on the way we write the code
  Goal is to avoid unnecessary storage elements.

## Slide 8: Inference from Declarations 2
Using integer type for a signal
  no additional information is needed for simulation purposes
However, in synthesis
  compiler needs to know how large it gets.
... signal result: std_logic_vector(12 downto 0); signal count: integer; signal index: integer range 0 to 18; type state_type is (state0, state1, state2, state3); signal next_state:state_type;
...
Question: how many bits will a compiler use to implement signals “count” and “index”?

## Slide 9: Limiting the Range of an Integer 1
library IEEE; use IEEE.std_logic_1164.all;
entity synth is port (a, b, c ,d: in integer range 0 to 18; sel: in std_logic_vector(1 downto 0); Z: out integer); end entity synth;
architecture behavioral of synth is begin
with sel select Z <= a + b when “00”, c + d when “10”, 0 when others; end architecture behavioral;

## Slide 10: Limiting the Range of an Integer 2

## Slide 11: Inference from Declarations 3
Compilers may try to optimize
  even if we do not provide clues such as “range”
  But never count on that!
What about type state_type is (state0, state1, state2, state3); signal next_state:state_type;
We define a new type (enumerated type)
  A signal of the new type form can take at most 4 distinct values
  Compiler needs only 2 bits to encode all the states.
  We may want to have a control over the encoding (recall One-Hot State Assignment for FPGA)

## Slide 12: Inference from Simple CSA
Simple CSA corresponds to combinational logic
  Value of a signal is computed from other signals
Operator inferencing
  Compiler infers logical operations from VHDL CSA statements
  Utilize gate primitives to implement these operations
Interconnection between gates are determined by the dependencies between signals
The way compiler extract these dependencies are not always obvious

## Slide 13: Operator Inferencing: Example
Delay information is redundant for synthesis
Post-synthesis simulation uses the known delay values of components
Therefore, compilers usually ignores delay values specified in VHDL source.
library IEEE; use IEEE.std_logic_1164.all;
entity concurrent is port(s,t,u,w: in std_logic; v: out std_logic); end entity concurrent;
architecture dataflow of concurrent is signal s1, s2: std_logic; begin L1: s1 <= s and t and u and w; L2: s2 <= (s and t) and (u and w); L3: v <= s1 or s2; end architecture dataflow;

## Slide 14: Operator Inferencing: Example
L1 and L2 are functionally equivalent
However, they lead to different implementations
Both implementation have three AND gates.
However, L2 leads to a faster circuit. Why?
L2 exploits the concurrency in logical expression.
Use of parentheses may be useful.
s
s2
u
w
v
s1
t
synthesized gate-level implementation
s
t
u
w
v
FPGA implementation
Xilinx XC4000E
What is the precedence for s1?
16x1
LUT

## Slide 15: Full Adder 1
we need two Xilinx XC4000E series LUTs to implement two Boolean functions with three variables (i.e. sum and c_out)
library IEEE; use IEEE.std_logic_1164.all;
entity full_adder is port(in1,in2,c_in: in std_logic; sum, c_out: out std_logic); end entity full_adder;
architecture dataflow of full_adder is signal s1, s2, s3: std_logic; begin sum <= in1 xor in2 xor c_in; c_out <= (in1 and in2) or (in1 and c_in) or (in2 and c_in); end architecture dataflow;

## Slide 16: Full Adder 1
sum
c_out
in1
in2
c_in
synthesized gate-level implementation
16x1
LUT
c_in
in2
in1
FPGA implementation
Xilinx XC4000E
16x1
LUT
c_out
sum

## Slide 17: Inference from Conditional Signal Assignment
Purely combinational
Priority order implied must be preserved in the text when the conditions are not mutually exclusive.
When conditions are mutually exclusive, synthesis compiler usually eliminates the priority logic
library IEEE; use IEEE.std_logic_1164.all;
entity mux4 is port(in0, in1, in2, in3: in std_logic; s0, s1: in std_logic; z: out std_logic); end entity mux4;
architecture behavioral of mux4 is begin z <= in0 when s0 = ‘0’ and s1 = ‘0’ else in1 when s0 = ‘0’ and s1 = ‘1’ else in2 when s0 = ‘1’ and s1 = ‘0’ else in3 when s0 = ‘1’ and s1 = ‘1’ else ‘0’; end architecture behavioral;

## Slide 18: MUX4
Synthesized Gate-Level Implementation (priority encoding preserved)
s0
s1
in3
z
in0
in1
in2

## Slide 19: MUX4
It implements z = in0 (s1’s0’) + in1 (s1s0’) (s1’s0’)’ + in2 (s1’s0) (s1s0’)’(s1’s0’)’ + in3 (s1s0) (s1’s0)’ (s1s0’)’ (s1’s0’)’
in2
in3
FPGA implementation
Xilinx XC4000E
s0
s1
in0
in1
z
F
G
H
F = in2 (s1’s0) + in3 (s1s0) G = in0 (s1’s0’) + in1 (s1s0’)
H = F + G
It eliminates the priority logic

## Slide 20: MUX4
No priority logic indeed!

## Slide 21: Priority Encoder
Not mutually exclusive anymore.
Priority encoding must be implemented.
Conditional CSA presents very natural construct for describing a priority logic.
library IEEE; use IEEE.std_logic_1164.all;
entity priority is port(datain: in std_logic_vector(3 downto 0); valid: in std_logic; z: out std_logic_vector(1 downto 0)); end entity priority;
architecture behavioral of priority is begin z <= “00” when datain(0) = ‘1’ and valid = ‘1’ else “10” when datain(2) = ‘1’ and valid = ‘1’ else “01” when datain(1) = ‘1’ and valid = ‘1’ else “11” when datain(3) = ‘1’ and valid = ‘1’ else “00”; end architecture behavioral;

## Slide 22: Priority Encoder
z(0) = [valid·datain(1)] [valid·datain(0)]’ [valid·datain(2)]’ + [valid·datain(3)] [valid·datain(1)]’[valid·datain(0)]’ [valid·datain(2)]’
z(1) = [valid·datain(1)] [valid·datain(0)]’ + [valid·datain(3)] [valid·datain(1)]’[valid·datain(0)]’ [valid·datain(2)]’
datain(3)
datain(1)
datain(2)
datain(0)
valid
z(0)
z(1)

## Slide 23: Priority Encoder

## Slide 24: How Don’t Cares is Synthesized
Don’t care values cannot be represented in hardware and cannot be compared against 0 or 1.
library IEEE; use IEEE.std_logic_1164.all;
entity priority is port(datain: in std_logic_vector(3 downto 0); valid: in std_logic; z: out std_logic_vector(1 downto 0)); end entity priority;
architecture behavioral of priority is begin z <= “00” when datain = “---1” and valid = ‘1’ else “10” when datain = “-100” and valid = ‘1’ else “01” when datain = “--10” and valid = ‘1’ else “11” when datain = “1000” and valid = ‘1’ else “00”; end architecture behavioral;

## Slide 25: Don’t Cares Cannot be Synthesized
In synthesis, if one of the signals in comparison operation is a don’t care, then the comparison always returns FALSE!
  In the previous example, the output will have value of either 11 or 00.
datain(0)
datain(1)
datain(3)
datain(2)
valid
z(0)
z(1)

## Slide 26: Don’t Cares is Synthesized Incorrectly

## Slide 27: Inference from Selected CSA
In the selected signal assignment there is no priority ordering among the options
Consider a 4-to-2 encoder
library IEEE; use IEEE.std_logic_1164.all;
entity encoder is port(datain: in std_logic_vector(3 downto 0); result: out std_logic_vector(1 downto 0)); end entity encoder;
architecture behavioral of encoder is begin with datain select result <= “00” when “0001”, “01” when “0010”, “10” when “0100”, “11” when “1000”, “XX” when others; -- outputs are undefined end architecture behavioral;

## Slide 28: A simple 4-to-2 Encoder
At most one of the input can have value 1 at any given time, otherwise the output of the circuit is undefined
  result(0) is 1 when datain(1) or datain(3) is 1
  result(1) is 1 when datain(2) or datain(3) is 1
This encoder can be realized using two LUTs in a CLB.
datain(1)
datain(3)
datain(2)
result(0)
result(1)

## Slide 29: A simple 4-to-2 Encoder

## Slide 30: The Keyword unaffected
unaffected keyword can be used within the select expression (VHDL’87 does not support)
  Be aware that a latch will be inferred when the keyword unaffected is in the select expression.
  It has been reported that some synthesis compilers do not support unaffected keyword.
with datain select result <= “00” when “0001”, “01” when “0010”, “10” when “0100”, “11” when “1000”, unaffected when others;

## Slide 31: Synthesis with unaffected Keyword

## Slide 32: Synthesis of the Resolved Signals
library IEEE; use IEEE.std_logic_1164.all; entity reso1 is port (a, b, c, d: in std_logic; Z: out std_logic); end entity reso1; architecture behavioral of reso1 is begin Z <= not a; Z <= not b; Z <= not c; Z <= not d; end architecture behavioral;
library IEEE; use IEEE.std_logic_1164.all; entity reso2 is port (a, b, c, d: in std_logic; Z: out std_logic); end entity reso2; architecture behavioral of reso2 is begin Z <= a; Z <= b; Z <= c; Z <= d; end architecture behavioral;

## Slide 33: Synthesis of the Resolved Signals
Entity reso1

## Slide 34: Synthesis of the Resolved Signals
Entity reso2

## Slide 35: Simulation Behavior vs. Synthesis Behavior
Semantic mismatch
  Simulation model of the VHDL model and the simulation of the synthesized hardware may not produce an identical behavior
  Delay Statements: In simulation model we can use any delay value for the components. In synthesis, those values are derived from the specifications of the real components.
  Comparison Logic: Comparisons to don’t cares(-), high impedance (Z), or other literals do not have meaningful hardware counterparts. Equality tests to other than 1/0 values return always FALSE for synthesis. However, recall that we can assign values such as Z or U to the signals in simulation.

## Slide 36: Synthesis Hints
Do not specify initial values in your declaration of signals.
  Most synthesis compilers ignore them. If you have to, do it using explicitly under the control of (probably asynchronous) reset signal. Constants can be initialized.
Specify the number of the bits necessary for a signal explicitly in a declaration
  This will tell the compiler exactly how many bits a signal would need. This will lead to less hardware in the form of the widths of signal paths, the number of gates necessary to process the signals, and the number of latches or flip-flops to store signal values.

## Slide 37: Synthesis Hints
Use of unaffected keyword in branches of signal assignments may cause latches
Using don’t care values to cover when others case in a selected signal assignments can enable synthesis compiler to optimize the logic and create a smaller logic. Use it consciously, though.
Use parentheses to control concurrency that may affect the speed of the logic
Use of selected signal assignments will produce less logic since priority among the options is not implied.

## Slide 38: Summary
Process of hardware inference from basic CSA.
  Every construct has a semantic as to how a construct is synthesized to logic.
  Simple and conditional signal assignments will lead to the synthesis of combinational circuit.
  unaffected clause in selected signal assignment can lead to synthesis of a latch since the output value must be “remembered” across execution.
Inferring signal data widths
Operator inferencing
Use of parentheses to control precedence and structure of synthesized circuit.

## Slide 39: Summary
Inference of combinational logic
Inference of latches in selected signal assignment statements.
Mismatches between the behavior of the simulation of VHDL code and simulation of the synthesized circuit.