## Slide 1: VHDL Structural Modeling
EL 310
Erkay Savaş
Sabancı University

## Slide 2: Structural Modeling
Behavioral Modeling (describing internal behavior of a component)
  CSA statements (dataflow model)
  Process
Structural Modeling
  Describes how the components are connected.
  Behavioral models are assumed to exist in local working directory or in a library.
  Structural modeling facilitate the use of hierarchy and abstraction in modeling complex systems
  Structural models can be integrated into models that also use processes and CSA statements

## Slide 3: Describing Structure
Block diagrams
  Components are represented by blocks interconnected by lines representing signals.
Full Adder
HA1
HA2
in1
in2
c_in
sum
c_out
s1
s2
s3
O1

## Slide 4: Full Adder
We assume that we have the description of half adders and or gate.
  Actually, we are not interested in the internal behavior of these components.
To connect them, what we need is the interface of each component.
x
y
sum
carry
x
y
z
Each component, signal and ports of components have names

## Slide 5: Connecting Components
List of components
Uniquely labeling components to distinguish among multiple instances of the same component.
Set of signals connecting them
Specify how signals are connected to ports of components.

## Slide 6: Structural Model of a Full Adder
library IEEE; use IEEE.std_logic_1164.all;
entity full_adder is port(in1, in2, c_in: in std_logic; sum, c_out: out std_logic); end entity full_adder;
architecture structural of full_adder is
component half_adder is port (x,y: in std_logic; sum, carry: out std_logic); end component half_adder;
component or_2 is port (x,y: in std_logic; z: out std_logic); end component or_2;
signal s1, s2, s3: std_logic; begin H1: half_adder port map(x=>in1, y=>in2, sum=>s1, carry=>s3);
H2: half_adder port map(x=>s1, y=>c_in, sum=>sum, carry=>s2);
O1: or_2 port map(x=>s2, y=>s3, z=>c_out);
end architecture structural;
component
declarations
signal
declarations
component
instantiation
statements

## Slide 7: Structural Model
Different instances of a component have identical input port names.
  This is not a problem; since the port name is associated with a specific instance through a unique label.
Components that are going to be used are declared within the declarative region of the architecture
  The actual description must be placed somewhere that CAD tools can locate: e.g. working directory, a library, or in some directory whose path is in the search path of CAD tools.

## Slide 8: Structural Model of a State Machine
Bit-serial adder
combinational
logic
Q
D
clk
R
Q’
0
1
11/0
00/1
x
y
z
carry
01/0
10/0
11/1
00/0
01/1
10/1
s2
s1

## Slide 9: Bit Serial Adder
library IEEE; use IEEE.std_logic_1164.all;
entity serial_adder is port(x, y, clk, reset: in std_logic; z: out std_logic); end entity serial_adder;
architecture structural of serial_adder is
component comb is port (x,y, c_in: in std_logic; z, carry: out std_logic); end component comb;
component dff is port (D,clk, R: in std_logic; Q, Qbar: out std_logic); end component dff;
signal s1, s2: std_logic; begin C1: comb port map(x=>x, y=>y, c_in=>s1, z=>z, carry=>s2);
D1: dff port map(D=>s2, clk=>clk, R=>reset, Q=>s1, Qbar=>open);
end architecture structural;
port on
the component
signal or port
on the entity
We cannot assume that port names are unique.
not connected

## Slide 10: Constructing Structural VHDL Models
Two Steps:
  Drawing the annotated schematics
  Converting it to VHDL
Make sure that description of components you will use is available.
  i.e. a working entity-architecture pair.
  Using entity descriptions, create a block for each component.
connect each port of every component to the port of another entity or to the input or output port of the entity being modeled.
Label each component
Label each internal signal
Label each system input and output port, define its mode and type

## Slide 11: Structural Model Template
library library-name-1, library-name-2; use library-name-1.package-name.all; use library-name-2.package-name.all;
entity entity_name is port(input signals: in type; output signals: out type); end entity entity_name;
architecture structural of entity_name is -- declare components used
component component1-name is port (input signals: in type; output signals: out type); end component component1-name ;
component component2-name is port (input signals: in type; output signals: out type); end component component2-name ;
-- declare al signals used to connect the components.
signal internal signals: type:=initialization; begin -- label each component and connect its ports to signals or entity ports Label1: component1-name port map(port=>signal, ...);
Label2: component2-name port map(port=>signal, ...); end architecture structural;

## Slide 12: Adder Design with Structural VHDL
ALU0
a0
b0
c0
ALU1
a1
b1
ALU2
a2
b2
s0
c1
1st Clock Cycle
s1
c2
2nd Clock Cycle
s2
c3
3rd Clock Cycle
ALU3
a3
b3
s3
c4
4th Clock Cycle
(1111) + (0001) worse case addition
Carry-ripple adder

## Slide 13: A Faster Adder
To add two corresponding bits of A an B, we have to know the carry from the sum of previous bits.
c1 = b0c0 + a0c0 + a0b0
c2 = b1c1 + a1c1 + a1b1 = (b1+a1)(b0c0+a0c0+a0b0)+a1b1
c3 = b2c2 + a2c2 + a2b2 = (b2+a2)(b1+a1)(b0c0+a0c0+a0b0)+a1b1+a2b2
c4 = b3c3 + a3c3 + a3b3 = (b3+a3)(b2+a2)(b1+a1)(b0c0+a0c0+a0b0) + a1b1 + a2b2 + a3b3 =
Can you imagine the length of the expression for c32?

## Slide 14: Carry Lookahead - 1
An approach in-between the two extremes
Motivation:
  If we didn't know the value of carry-in, what could we do?
  When would a carry be always generated? gi = aibi
  When would the carry be propagated? pi = ai+bi
Using them we can write the following formula ci+1 = gi+pici
To see where the signals get their names suppose gi=1  ci+1=1+pici= 1 that is, the adder generates the CarryOut (independent of CarryIn)

## Slide 15: Carry Lookahead – 2
gi = 0 and pi = 1  ci+1=ci
That is CarryIn is propagated to CarryOut.
c1 = g0 + p0c0
c2 = g1 + p1c1 = g1 + p1g0 + p1p0c0
c3 = g2 + p2c2 = g2 + p2g1 + p2p1g0 + p2p1p0c0
c4 = g3 + p3c3 = g3 + p3g2 + p3p2g1 + p3p2p1g0 + p3p2p1p0c0
Question: How can we compute pis and gis efficiently?

## Slide 16: Brent-Kung Formulation
An associative operation:
  (x, y)(w,z) = (x+yw, yz)
Apply this operation to the pis and gis
(c0, 1)
(g0, p0)(c0, 1)=(g0+ p0c0, p0)= (c1, p0)
(g1, p1)(c1, p0)=(g1+ p1c1, p1p0)=(c2, p1p0)
(g2, p2)(c2, p1)=(g2+ p2c2, p2p1p0)=(c2, p2p1p0)
...
(gi, pi)(ci, pi…p1p0)= (gi+ pici, pi…p1p0)=(ci+1, pi…p1p0)

## Slide 17: Brent-Kung Circuit
gi
pi
ci
pi-1 ...p1 p0
ci+1
pi pi-1 ...p1 p0
(gi, pi)(ci, pi…p1p0)= (gi+ pici, pi…p1p0)=(ci+1, pi…p1p0)

## Slide 18: Brent-Kung Formulation
(g0, p0 )
(c0, 1 )
(g1, p1 )
(gi, pi )
(c1, p0 )
(c2, p1 p0 )
(ci, pi ... p0 )
Computing carries becomes a prefix problem

## Slide 19: Prefix Problem
Input: x0, x1, x2, …, x7
Output: y0, y1, y2, …, y7
y0 = x0
y1 = x1x0
y2 = x2x1x0
y3 = x3x2x1x0
...
y7 = x7x6...x1x0
Various algorithms for prefix problem with different complexities.

## Slide 20: Prefix Algorithms
Sequential or Serial Algorithm
x2
x1
y1
x0
y0
y2
y3
x3
x7
y7
Depth: n-1
Size: n-1

## Slide 21: Prefix Algorithms
Obvious Parallelization Algorithm
x1
y1
x0
y0
x0
x1
x0
x3
x2
y3
Depth: log2n
Size: 0 +1 + 2 + 3 + … + n-1 = n(n-1)/2=O(n2)
x1
x0
x2
y2

## Slide 22: Ladner-Fischer Constructions
Depth: O(log2n)
Size: O(n)
Assumption: n=2d.
(n is the number of bits in our adder)
Ladner-Fischer constructions provide a family of circuits for n:
Pk(n) where 0  k  d and d = log2n.
For example: n = 2 (d = 1)  P0(2) and P1(2) n = 4 (d = 2)  P0(4) , P1(4), and P2(4). n = 8 (d = 3)  P0(8) , P1(8), P2(8), and P3(8)

## Slide 23: Ladner-Fischer Constructions
Properties of Pk(n) circuit:
  Depth: Dk(n) = d + k
  Size: Sk(n) = 2(1+2-k)n – F(5+d-k) + 1 – k where F is the Fibonacci number
i | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
f(i) | 0 | 1 | 1 | 2 | 3 | 5 | 8 | 13 | 21 | 34
S0(n) = 3n-F(5+d)+1
S1(n) = 3n-F(4+d)

## Slide 24: Ladner-Fischer Circuits
Pk(1) and k = 0  P0(1)
D = 0, S = 0
Pk(2) and k = 0, 1  P0(2) and P1(2)
P0(2)  D = 1 and S = 1
P1(2) does not exist since there is only one circuit to add two numbers.
Thus P1(2) = P0(2)
P0(2)
D = 1, S = 1

## Slide 25: Ladner-Fischer Circuits
Pk(4) and k = 0, 1, 2  P0(4) , P1(4), and P2(4)
There is no other circuit but P0(4) for n = 4.
Question: how to construct P0(4) from P0(2) ?
P0(2)
x2
x3
in our case these
corresponds to
Brent-Kung circuits
P1(2)
x0
x1
x0
x1x0
x2x1x0
x3x2x1x0

## Slide 26: P0(4) Circuit for Carry Calculation
(g0, p0)
(g1, p1)
(g2, p2)
(c0, 1)
(c0, 1)
(c1, p0)
(c2, p1 p0)
(c3, p2 p1 p0)
Brent-Kung Circuit

## Slide 27: General Construction Scheme for P0(n)
0
P1(n/2)
1
n/2-1
P0(n/2)
n/2
n-1

## Slide 28: General Construction Scheme for P1(n)
P0(n/2)
0
1
2
3
4
5
n-1
n-2

## Slide 29: P0(8)
P0(4)
0
P1(4)=P0(4)
1
3
4
7
2
5
6
76543210
6543210
543210
43210
3210
210
10
0
0  (c0, 1)
1  (g0, p0)
2  (g1, p1)
3  (g2, p2)
…
7  (g6, p6)
10  (c1, p0)
210  (c2, p1p0)
3210  (c3, p2p1p0)
…
7  210 (c7, p6 … p1p0)

## Slide 30: P1(8)
P0(4)
0
1
2
3
4
5
7
6

## Slide 31: Assignment
Construct CLA adders of 4-bit, 8-bit, 16-bit, 32-bit, and 64-bit using structural VHDL modeling.
  create a behavioral model of Brent-Kung circuit.
  construct P0(2)
  construct P0(4) using P0(2)
  construct P0(8) using P0(4)
  construct P1(8) using P0(4)
  construct P0(16) using P0(8) and P1(8)
  construct P1(16) using P0(8)
  construct P0(32) using P0(16) and P1(16)
  construct P1(32) using P0(16)
  construct P0(64) using P0(32) and P1(32)

## Slide 32: Hierarchy of Models
full_adder.vdh
or2.vdh
half_adder.vdh
and2.vdh
xor2.vdh
Hierarchy of models used in the full adder
At the lowest level, a behavioral description must exist.
-- top level
-- bottom level

## Slide 33: Structural Model of a Half Adder
architecture structural of half_adder is
component xor2 is port (x,y: in std_logic; z: out std_logic); end component xor2;
component and2 is port (x, y: in std_logic; z: out std_logic); end component and2;
begin EX1: xor2 port map(x=>x, y=>y, z=>sum);
AND1: and2 port map(x=>x, y=>y, z=>carry);
end architecture structural;
There may be a many levels of hierarchy in structural model.
No behavioral description.

## Slide 34: Flattening
When the simulator loads the hierarchy of structural model, it replace each component by its behavioral description.
  This process is repeated at each level of hierarchy.
This is called as flattening of hierarchy.
Flattening of the all hierarchy may result in a very complicated behavioral description of a very complex design.
  Simulation may take too long
  Preserving hierarchy in a structural model is a way of managing very complex systems.
  Components can be simulated in isolation.

## Slide 35: Parameterized Models
Aim: construct parameterized models.
  You use 5 ns delay for your 2-input and gates in your model.
  Thanks to developments in the technology, you would like to simulate your model using 1 ns propagation delay for your 2-input and gates.
  It is hard to change the delay of every 2-input gate delays manually.
  Solution: to be able to decide delay values at simulation time rather than design time.
Parameterized models are useful in creating libraries of models that can be shared and reused.

## Slide 36: Generics
library IEEE; use IEEE.std_logic_1164.all entity xor2 is generic(gate_delay: Time:= 2ns); port(x, y: in std_logic; z: out std_logic); end entity xor2;
architecture behavioral of xor2 is begin z <= (x and y) after gate_delay;
end architecture behavioral;
The default delay for xor2 gate is 2 ns.
The gate delay can be specified at the time of its use (during declaration or instantiation ).
xor gate is defined with generic

## Slide 37: Generics
architecture structural of half_adder is
component xor2 is generic(gate_delay: Time); port (x,y: in std_logic; z: out std_logic); end component xor2;
component and2 is generic(gate_delay: Time := 3 ns); port (x, y: in std_logic; z: out std_logic); end component and2;
begin EX1: xor2 generic map(gate_delay => 6 ns) port map(x=>x, y=>y, z=>sum);
AND1: and2 port map(x=>x, y=>y, z=>carry)
end architecture structural;

## Slide 38: Specifying Generics Constants
in the component declaration component and2 is generic(gate_delay: Time:=3 ns); port (x, y: in std_logic; z: out std_logic); end component and2;
in the component instantiation EX1: xor2 generic map(gate_delay => 6 ns) port map(x=>x, y=>y, z=>sum);
If both are specified, the value provided in the component instantiation takes precedence.
If neither is specified, the default value defined in the entity is used.

## Slide 39: Passing Generic Values through Hierarchy
library IEEE; use IEEE.std_logic_1164.all
entity half_adder is generic(gate_delay: Time:= 3ns); port(a, b: in std_logic; sum, carry: out std_logic); end entity half_adder;
architecture structural of half_adder is
component xor2 is generic(gate_delay: Time); port(x, y: in std_logic; z: out std_logic); end component xor2;
component and2 is generic(gate_delay: Time); port(x, y: in std_logic; z: out std_logic); end component and2;
begin
EX1: xor2 generic map(gate_delay=>gate_delay) port map(x=>a, y=>b, z=>sum); A1: and2 generic map(gate_delay=>gate_delay) port map(x=>a, y=>b, z=>carry);
end architecture structural;

## Slide 40: Passing Generic Values through Hierarchy
... H1: half_adder generic map(gate_delay => 6 ns) port map(a => in1, b => in2, sum => s1, carry=>s2); H2: half_adder ... ...
... EX1:xor2 generic map (gate_delay=>gate_delay) ...
A1:and2 generic map (gate_delay=>gate_delay)
... EX1:xor2 generic map (gate_delay=>gate_delay) ...
A1:and2 generic map (gate_delay=>gate_delay)
entity xor2 is generic(gate_delay: Time:= 2ns);-- ...
entity and2 is generic(gate_delay: Time:= 2ns); ...
6 ns
6 ns
6 ns
6 ns
6 ns
6 ns
The generic value coming from the upper level of hierarchy overrides the other values.
full_adder.vhd
half_adder.vhd
xor2.vhd
and2.vhd

## Slide 41: N-input AND Gate
entity and_gate is generic(n:natural:=2); port(x: in std_logic_vector(n-1 downto 0); z: out std_logic); end entity and_gate;
architecture beh of and_gate is
begin process(x) variable and_out: std_logic :=‘1’; begin and_out := ‘1’; --on an input signal transition it must be set to 1 for i in 1 to n loop and_out := and_out and x(i); exit when and_out = ‘0’; end loop; z <= and_out; end process;
end architecture beh;
entity or_gate is generic(m:integer:=2); port(x: in std_logic_vector(m downto 1); z: out std_logic); end entity or_gate;

## Slide 42: Another Example
entity another_gen_ex is end entity another_gen_ex;
architecture structural of another_gen_ex is -- component declaration for the gates component and_gate is generic(n:natural:=5); port(x: in std_logic_vector(n-1 downto 0); z: out std_logic); end component;
component or_gate is generic(m:integer); port(x: in std_logic_vector(m downto 1); z: out std_logic); end component; signal s1, s2, s3, s4: std_logic; signal sa: std_logic_vector(1 to 10); signal sb: std_logic_vector(2 downto 1); signal sc: std_logic_vector(1 to 10); signal sd: std_logic_vector(5 downto 0); begin -- component instantiations o1: or_gate generic map(6) port map(sd, s1); a1: and_gate generic map(N => 10) port map(sc, s3); a2: and_gate port map(sa, s4); -- size mismatch; but still legal -- o2: or_gate port map(sb, s2); -- illegal
end architecture structural;

## Slide 43: N-bit Register
library IEEE; use IEEE.std_logic_1164.all;
entity generic_reg is generic(n: positive := 2); port(clk, reset, enable: in std_logic; d: in std_logic_vector(n-1 downto 0); q: out std_logic_vector(n-1 downto 0)); end entity generic_reg;
architecture behavioral of generic_reg is
begin
reg_process: process(clk, reset) is begin if reset = ‘1’ then q <= (others => ‘0’); elsif (rising_edge(clk)) then if enable = ‘1’ then q <= d; end if; end if; end process reg_process;
end architecture behavioral;
Note the statement q <= (others => ‘0’);

## Slide 44: Trace of the Operation of a 2-bit Register

## Slide 45: Component Instantiation & Synthesis
Structural design
  The ability to instantiate specific components enables us to use previously synthesized and optimized implementation of common components
  Those implementation may be provided by the vendors, other design groups, or by yourself from a previous design.
  Performance critical components may be manually placed and routed to a specific target device.
  Manual place-and-routing is time-consuming.
  Vendors may take time to manually place and route key components such as adders/subtractors, shifters, counters, etc. and they provide those components in design libraries.

## Slide 46: Core Generators
A CAD tool
  allow you select and then configure the components of your choice.
  The CAD tool will then generate a synthesizeable model of this component and corresponding VHDL model.
  The CAD tools generally do a good job of producing models that will generate highly optimized implementations for the target FPGA device.
  The Core Generator and LogiBLOX of Xilinx Foundation are such tools.

## Slide 47: Core Generator

## Slide 48: Core Generator

## Slide 49: Xilinx Foundation LogiBLOX

## Slide 50: Xilinx Foundation LogiBLOX

## Slide 51: Xilinx Foundation LogiBLOX

## Slide 52: addsub8.vhi File
------------------------------------------------------
-- LogiBLOX ADD_SUB Module "addsub8"
-- Created by LogiBLOX version E.35
-- on Sun Nov 02 17:37:55 2003
-- Attributes
-- MODTYPE = ADD_SUB
-- BUS_WIDTH = 8
-- OPTYPE = ADD_SUB
-- REGISTERED = NONE
-- ENCODING = SIGNED
-- STYLE = MAX_SPEED
------------------------------------------------------
----------------------------------------------------

## Slide 53: addsub8.vhi File
-- Component Declaration
----------------------------------------------------
component addsub8
PORT(
ADD_SUB: IN std_logic;
C_IN: IN std_logic;
A: IN std_logic_vector(7 DOWNTO 0);
B: IN std_logic_vector(7 DOWNTO 0);
SUM: OUT std_logic_vector(7 DOWNTO 0);
OVFL: OUT std_logic;
C_OUT: OUT std_logic);
end component;
----------------------------------------------------
-- Component Instantiation
----------------------------------------------------
instance_name : addsub8 port map
(ADD_SUB => ,C_IN => , A => , B => , SUM => , OVFL => ,C_OUT => );

## Slide 54: Xilinx Foundation LogiBLOX
Caveat: Since we do not have the license, LogiBLOX will only provide the model in EDF format.
In the previous example, EDF format is saved in addsub8.EDO file.

## Slide 55: An Adder using addsub8
library IEEE;
use IEEE.std_logic_1164.all; entity add is port (CarryIn: in std_logic; a, b ,c: in STD_LOGIC_VECTOR (7 downto 0); CarryOut, OverFlow: out std_logic);
end add; architecture add_arch of add is component addsub8
PORT(ADD_SUB: IN std_logic; C_IN: IN std_logic; A: IN std_logic_vector(7 DOWNTO 0); B: IN std_logic_vector(7 DOWNTO 0); SUM: OUT std_logic_vector(7 DOWNTO 0); OVFL: OUT std_logic; C_OUT: OUT std_logic); end component;
begin
my_adder : addsub8 port map (ADD_SUB => ‘1’, C_IN => CarryIn, A => a, B => b, SUM => c, OVFL => OverFlow, C_OUT => CarryOut);
end add_arch;

## Slide 56: On-Chip Oscillator
XC4000 chips have an on-chip oscillator
  Signals generated from 8-MHz clock
  8 MHz, 500 KHz, 16 KHz, 490 Hz, 15 Hz
To use the oscillator
  component OSC4 is port (F8M: out std_logic; F500k: out std_logic; F15: out std_logic); end component OSC4;
Global low skew lines for distribution of global signals such as clocks.
  component BUFG is port (I: in std_logic; O: out std_logic); end component OSC4;

## Slide 57: Clock Distribution: Example
entity my_clocks is port (phi1, phi2: out std_logic); end entity my_clocks; architecture beh of my_clocks is component OSC4 is -- we will use the on-chip oscillator port(F8M: out std_logic; -- 8 MHz clock F500k: out std_logic; -- 500 KHz clock F15: out std_logic); -- 15 Hz clock end component;
component BUFG is port(I: in std_logic; O: out std_logic); end component BUFG;
signal local_F15, local_phi2: std_logic;
begin
O1: OSC4 port map(F15 => local_F15);
B1: BUFG port map(I => local_F15, O => phi1);
B2: BUFG port map(I => local_phi2, O => phi2);
local_phi2 <= not local_F15; -- phi2 is the complement of phi1
end architecture beh;

## Slide 58: Clock Distribution: Example

## Slide 59: Global Set/Reset Signals
Global set/reset signals throughput the chip
  low skew on chip signals
  Each flip-flop can be configured to use set or reset functionality, but not both.
  STARTUP component: component STARTUP is port(GSR: in std_logic); end component STARTUP;
  During synthesis the placement and routing of signals ensures that the reset signal will be connected to global set/reset signals

## Slide 60: Global Set/Reset: Example
entity startup_exm is port (clk, reset, x, y, z: in std_logic;
phi1, phi2: out std_logic); end entity startup_exm; architecture beh of startup_exm is component STARTUP is -- declare the STARTUP component port(GSR: in std_logic); -- 15 Hz clock end component STARTUP;
signal s1, s2: std_logic;
begin
U1: STARTUP port map(GSR => reset);
process is begin
wait until (rising_edge(clk)); if reset = ‘1’ then w <= ‘0’; s1 <= ‘0’; s2 <= ‘0’; else L1: s1 <= x xor y; L2: s2 <= s1 or z;
L3: w <= s1 xor s2; end if; end process;
end architecture beh;

## Slide 61: General Model
… entity entity_name is port(input signals: in type; output signals: out type); end entity entity_name;
architecture arch_name of entity_name is component component1-name is port (input signals: in type; output signals: out type); end component component1-name ;
component component2-name is port (input signals: in type; output signals: out type); end component component2-name ; signal internal signals: type:=initialization; begin -- label each component and connect its ports to signals or entity ports Label1: component1-name port map(port=>signal, ...);
Label2: component2-name port map(port=>signal, ...); concurrent signal assignment-1; concurrent signal assignment-2; process-1:...
process-2:... end architecture arch_name;

## Slide 62: Generate Statement
Structural models are based on component instantiation
A design may have large number of component instantiation
The design may have a very regular structure
  N-bit register from D flip-flops
It would be convenient to have a tool that automatically generates many number of component instances in an easy way
The tool is generate statement

## Slide 63: N-bit Register
entity dregister is port (din : in std_logic_vector(3 downto 0);
clock: in std_logic; qout: out std_logic_vector(3 downto 0)); end entity dregister; architecture beh of dregister is component dff is port(d, clock: in std_logic; q: out std_logic); end component dff;
begin
bit0: dff port map(d=>din(0), q=>qout(0), clock=>clock); bit1: dff port map(d=>din(1), q=>qout(1), clock=>clock); bit2: dff port map(d=>din(2), q=>qout(2), clock=>clock); bit3: dff port map(d=>din(3), q=>qout(3), clock=>clock);
end architecture beh;

## Slide 64: N-bit Register with Generate Statement
entity dregister is generic (n: natural:=16); port (din : in std_logic_vector(n-1 downto 0); clock: in std_logic; qout: out std_logic_vector(n-1 downto 0)); end entity dregister; architecture beh of dregister is component dff is port(d, clock: in std_logic; q: out std_logic); end component dff;
begin
dreg: for i in din’range generate reg: dff port map(din(i), clock, qout(i)); end generate; end architecture beh;

## Slide 65: Configurations
Different ways to model digital circuit
  behavioral
  structural
One entity may have more than one architecture
  Example: full adder using a half adder
  Design-1: behavioral description
  Design-2: structural description
Problem:
  which architecture is to be used?
  configurations explicitly associate an architecture with a component
  This process is known as binding an instance of the component to an architecture

## Slide 66: The Role of Configurations
entity
component…
component…
configuration
arch-1
arch-2
arch-3
arch-1
arch-2
arch-3
entity
entity

## Slide 67: Example
combinational
logic
Q
D
clk
R
Q’
x
y
z
carry
s2
s1
architecture gate_level of comb is …
architecture low_power of comb is …
architecture behavioral of comb is …
architecture high_speed of comb is …

## Slide 68: Default Binding Rules
If an entity, whose name is the same as the component name is found, then this entity is bound to the component.
  Note that a component can be bound to an entity with a different name.
  For this, ports of the entity must match those of component.
  And, ports of entity must map to those of the component.
If there are multiple architectures for the entity, then the last compiled architecture is used.

## Slide 69: Configuration Specification
The name of the library that contains the entity is given
  recall that a library name corresponds to a directory in most systems
  WORK is the default working directory
The name of the architecture is used
  half_adder(behavioral)
  half_adder(structural)
If only entity is specified but no architecture
  the last compiled architecture is used
  Components of the same type may use different architectures
  They may even bind to different entities.

## Slide 70: Configuration Specification: Example
library IEEE; library POWER; -- a new library use IEEE.std_logic_1164.all
entity full_adder is port (in1, in2, c_in : in std_logic; sum, c_out: out std_logic);
end entity full_adder ; architecture structural of full_adder is
component half_adder is port(x, y: in std_logic; sum_carry: out std_logic); end component half_adder;
component or_2 is generic (gate_delay: Time := 2 ns); port(x, y: in std_logic; z: out std_logic); end component or_2;
signal s1, s2, s3: std_logic;
... begin
...
end architecture structural;

## Slide 71: Configuration Specification: Example
... entity full_adder is port (in1, in2, c_in : in std_logic; sum, c_out: out std_logic); end entity full_adder ; architecture structural of full_adder is ... signal s1, s2, s3: std_logic; -- configuration specification for H1: half_adder use entity WORK.half_adder(behavioral); for H2: half_adder use entity WORK.half_adder(structural); for O1: or_2 use entity POWER.lpo2(behavioral) generic map(gate_delay=>gate_delay) port map (l1=>x, l2=>y, Z=>z);
begin H1: half_adder port map(x=>in1, y=>in2, sum=>s1, carry=>s2); H2: half_adder port map(x=>s1, y=>c_in, sum=>sum, carry=>s2);
O1: or_2 port map(x=>s2, y=>s3, z=>c_out); end architecture structural;
Library name
entity name
Architecture name
entity name is different than the component name

## Slide 72: Configuration Declaration
Configuration specification is part of the architecture
  must be placed in the architecture body.
  When we want to change the architecture for a component, then the architecture using the entity using this component must be edited and recompiled
Configuration declaration provide configuration information as separate design unit.
  configuration information is saved in a different file (e.g. config.vhd)
Late binding is possible
  bindings can be performed after the architecture body has been written.

## Slide 73: Configuration Declaration: Example
configuration Config_A of full_adder
for structural for H1: half_adder use entity WORK.half_adder(behavioral);
end for; for H2: half_adder use entity WORK.half_adder(structural);
end for; for O1: or_2 use entity POWER.lpo2(behavioral) generic map(gate_delay=>gate_delay) port map (l1=>x, l2=>y, Z=>z); end for;
end for;
end configuration Config_A;
config.vhd

## Slide 74: Test Bench for Full Adder
library IEEE; use IEEE.std_logic_1164.all; use WORK.all; entity test_bench is end test_bench; architecture testing of test_bench is
component full_adder is
port (in1, in2, c_in: in std_logic;
sum, c_out: out std_logic);
end component full_adder;
signal x, y, z, w, v: std_logic;
for F1: full_adder use configuration WORK.config_a;
begin
F1: full_adder port map(x, y, z, w, v);
x <= '0', '1' after 40 ns;
y <= '0', '1' after 20 ns, '0' after 40 ns, '1' after 60 ns;
z <= '0', '1' after 10 ns, '0' after 20 ns, '1' after 30 ns,
'0' after 40 ns, '1' after 50 ns, '0' after 60 ns,
'1' after 70 ns;
end architecture testing;
test_bench.vhd

## Slide 75: Simulation of Full Adder

## Slide 76: ModelSim Window

## Slide 77: Warning
Configuration specifications are not always supported for synthesis.
In this case, default binding rules apply.