## Slide 1: VHDL Design with Algorithmic State Machine (ASM) Charts
EL 310
Erkay Savaş
Sabancı University

## Slide 2: Motivation
Sequential systems are complex and require a formal notation to describe their functionality
From this formal notation, a state table and hence Boolean expressions can be derived.
Algorithmic State Machine (ASM) charts provide a less ambiguous description of a sequential system than state diagrams.
  State diagrams do not provide explicit timing information.
  For example, when an output signal is assigned a new value is sometimes not clear.

## Slide 3: State Diagram for a Traffic Signal Controller
Major road
Minor road
sensor
major=G minor=R
car/start_timer
timed
timed’
car’
major=R minor=G

## Slide 4: ASM Chart for Traffic Controller
ASM charts resemble flow charts, but contain implicit timing information
ASM charts represent real hardware.
Hardware cannot suddenly start or stop
Therefore, all transitions within ASM charts must form closed paths (except a reset signal).
major=Green minor=Red
G
major=Red minor=Green
R
car
start_timer
timed
0
0
1
1

## Slide 5: Components of ASM Charts
X=1 Y
A
state box
name
1011
state
assignment
output signals
The state represented by the state box takes a clock cycle to complete.
The output signals in the box take the specified values during this clock cycle.
The notation X  1 means that the signal is assigned during the next clock cycle and holds its value until otherwise set elsewhere.
asserted during the state and deasserted elsewhere

## Slide 6: Components of ASM Charts
Decision box
J
0
1
Decision box has two or more branches going out.
Decision is made based on the value of one or more input signals (e.g. signal J)
Decision box must follow and be associated with a state box.
Thus, the decision is made in the same clock cycle as the other actions of the state.
Hence, the input signals must be available and valid at the start of the clock cycle.

## Slide 7: Components of ASM Charts
Conditional output box
Z=1
A conditional output box must follow a decision box.
A conditional output box is attached to a state box through one or more decision boxes.
Therefore, the output signals in the conditional output box are asserted in the same clock cycle as those in the state box to which it is attached.
The output signals can change during that state as a result of changes on the inputs.
The conditional output signals are sometimes referred as Mealy outputs since they depend on the input signals as well.

## Slide 8: A State in ASM Charts
One state, or clock cycle, consists of more than just the state box.
Decision and conditional output boxes are also a part of the state.
major_green = 1 minor_green = 0
G
major_green = 0 minor_green = 1
R
car
start_timer
0
0
1
1
timed
1 clock cycle

## Slide 9: State Box vs. Conditional Output Box
Z
W
C
Y
0
1
Z
W
C
0
1
Y
(a)
(b)

## Slide 10: State Box vs. Conditional Output Box
W
clock
Z
Y, C=1
Y, C=0
Z
Y, C=1
W, C=1
Y, C=0
W, C=0
(a)
(b)
C is tested here

## Slide 11: Synthesis from ASM Charts
Present State | Car, Timed |  |  | 
 | 00 | 01 | 11 | 10
G | G,0 | G,0 | R,1 | R,1
R | R,0 | G,0 | G,0 | R,0
State and output table
Q | Car, Timed |  |  | 
 | 00 | 01 | 11 | 10
0 | 0,0 | 0,0 | 1,1 | 1,1
1 | 1,0 | 0,0 | 0,0 | 1,0
Transition and output table
Next State, start_timer
Q+, start_timer

## Slide 12: K-Maps for Traffic Signal Controller
car, Q | timed 00 | 01 | 11 | 10
0 | 0 | 0 | 1 | 1
1 | 1 | 0 | 0 | 1
Q+ = Q’ car + Q timed’
car, Q | timed 00 | 01 | 11 | 10
0 | 0 | 0 | 1 | 1
1 | 0 | 0 | 0 | 0
start_timer = Q’ car

## Slide 13: Hardware Implementation
timed
car
Q+
Q
Q’
start_timer
clk
The flip-flop outputs can be used directly to control the traffic signals.
Q=0  the signal for the major road is green and the signal for the minor road is red.

## Slide 14: VHDL Model for Traffic Control Signals
library IEEE; use IEEE.std_logic_1164.all;
entity traffic_signals is port(clock, timed, car: in std_ulogic; start_timer, major_green, minor_green: out std_ulogic); end entity traffic_signals;
architecture asm of traffic_signals is begin process(clock, timed, car) is type state_type is (G, R); variable state: state_type; begin start_timer <= ‘0’; if (rising_edge(clock)) then case state is when G => major_green <= ‘1’; minor_green <= ‘0’; if( car = ‘1’) then start_timer = ‘1’; state := R; end if; when R => major_green <= ‘0’; minor_green <= ‘1’; if( timed = ‘1’) then state := G; end if; end case; end if; end process; end architecture asm;

## Slide 15: Alternative VHDL Code
architecture asm2 of traffic_signals is type state_type is (G, R); variable state, next_state: state_type; begin seq: process(clock) is -- for sequential part begin if (rising_edge(clock)) then state <= next_state; end if; end process seq; com: process(timed, car, state) is -- for combinational part begin start_timer <= ‘0’; case state is when G => major_green <= ‘1’; minor_green <= ‘0’; if(car = ‘1’) then start_timer = ‘1’; next_state <= R; else next_state <= G; end if; when R => major_green <= ‘0’; minor_green <= ‘1’; if( timed = ‘1’) then next_state <= G; else next_state <= R; end if; end case; end process com; end architecture asm2;

## Slide 16: Binary Multiplier Design with ASM Charts
Start
Load
0
1
M0
Shift
Add
co_out
Shift
S0
S1
S2
co_out
0
S3
Done
1
1
0
1
0
The multiplier starts when Start= 1
The counter counts the number of shifts and outputs co_out = 1 just before the last shift occurs.
M0 is the LSB of the multiplier

## Slide 17: VHDL Code for Binary Multiplier
entity multiplier is port(clock, Start, co_out, M0: in std_ulogic; Load, Shift, Done, Add: out std_ulogic); end entity multiplier;
architecture asm_beh of multiplier is signal state, next_state: integer range 0 to 3; begin process(Start, co_out, M0, state) is begin Load <= ‘0’; Shift <= ‘0’; Add <= ‘0’; -- conditional outputs -- get default values case state is when 0 => if Start = ‘1’ then Load <= ‘1’; next_state <= 1; else next_state <= 0; end if; when 1 => if M0 = ‘1’ then Add <= ‘1’; next_state <= 2; else Shift <= ‘1’; if co_out = ‘1’ then next_state <= 3; else next_state <= 1; end if; end if; ... end architecture asm_beh;

## Slide 18: VHDL Code for Binary Multiplier
...
architecture asm_beh of multiplier is signal state, next_state: integer range 0 to 3; begin process(Start, co_out, M0, state) is begin Load <= ‘0’; Shift <= ‘0’; Add <= ‘0’; -- conditional outputs -- get default values case state is ... when 2 => Shift <= ‘1’; if co_out = ‘1’ then next_state <= 3; else next_state <= 1; end if; when 3 => done <= ‘1’; next_state <= 0; end case; end process;
process (clock)is begin if (rising_edge(clock)) then state <= next_state; end if; end process; end architecture asm_beh;

## Slide 19: ASM Chart for Sequence Detector
A
z = 1
x
y
y
1
0
B
z = 0
x
y
y
1
0
C
z = 0
x
y
y
1
0
0
0
1
1
1
0
1
0
A: sum  0 mod 3
B: sum  1 mod 3
C: sum  2 mod 3
0
1
0
1

## Slide 20: VHDL Code for Sequence Detector
entity seq_detector is port(clock, x, y: in std_ulogic; z: out std_ulogic); end entity seq_detector;
architecture asm_beh of seq_detector is type state_type is (state_A, state_B, state_C); signal state, next_state: state_type; begin process(x, y, state) is begin case state is when state_A => z <= ‘1’; if x = ‘0’ then if y = ‘0’ then next_state <= state_A; else next_state <= state_B; end if; else if y = ‘0’ then next_state <= state_B; else next_state <= state_C; end if; end if; ... end process; end architecture asm_beh;

## Slide 21: VHDL Code for Sequence Detector
...
architecture asm_beh of seq_detector is ... process(x, y, state) is ... case state is ... when state_B => z <= ‘0’; if x = ‘0’ then if y = ‘0’ then next_state <= state_B; else next_state <= state_C; end if; else if y = ‘0’ then next_state <= state_C; else next_state <= state_A; end if; end if; ... end process; end architecture asm_beh;

## Slide 22: VHDL Code for Sequence Detector
...
architecture asm_beh of seq_detector is ... process(x, y, state) is ... case state is ... when state_C => z <= ‘0’; if x = ‘0’ then if y = ‘0’ then next_state <= state_C; else next_state <= state_A; end if; else if y = ‘0’ then next_state <= state_A; else next_state <= state_B; end if; end if; end case; end process;
process (clock)is begin if (rising_edge(clock)) then state <= next_state; end if; end process; end architecture asm_beh;