## Slide 1: VHDL Designing Multiplier
EL 310
Erkay Savaş
Sabancı University

## Slide 2: Binary Multiplier
 |  |  |  | 1 | 1 | 0 | 1 | multiplicand (13)
 |  |  |  | 1 | 0 | 1 | 1 | multiplier (11)
 |  |  |  | 1 | 1 | 0 | 1 | 
 |  |  | 1 | 1 | 0 | 1 |  | 
 |  | 1 | 0 | 0 | 1 | 1 | 1 | partial products
 |  | 0 | 0 | 0 | 0 |  |  | 
 |  | 1 | 0 | 0 | 1 | 1 | 1 | partial products
 | 1 | 1 | 0 | 1 |  |  |  | 
1 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | result (143)
sequence of shift-and-adds

## Slide 3: Serial-Parallel Binary Multiplier
C
o
n
t
r
o
l
4-bit adder
carry
multiplier
multiplicand
product( and) partial result
ACC(0)
ACC
start
done
load
shift
add
clock
8
7
6
5
4
3
2
1
0

## Slide 4: Serial-Parallel Binary Multiplier
initial content of product reg. | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | ACC(11)
add since ACC(0) = 1 |  | 1 | 1 | 0 | 1 |  |  |  |  | (13)
after addition | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 
after shift | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 1 | ACC
add since ACC(0) = 1 |  | 1 | 1 | 0 | 1 |  |  |  |  | 
after addition | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 1 | 
after shift | 0 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 
skip addition since ACC(0) = 0 |  |  |  |  |  |  |  |  |  | 
after shift | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 
add since ACC(0) = 1 |  | 1 | 1 | 0 | 1 |  |  |  |  | 
after addition | 1 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 
after shift | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | (143)

## Slide 5: Control Circuit
S0
S1
S2
S4
S8
S7
S6
S9
S5
st’/0
st/Load
st = start
M = ACC(0)
sh = shift
S3
M/Add
-/sh
M/Add
-/sh
M/Add
M/Add
-/sh
-/done
M’/sh
M’/sh
M’/sh
M’/sh

## Slide 6: VHDL Code
library IEEE; use IEEE.std_logic_1164.all;
entity mult4x4 is port (clock, st: in std_logic; mplier, mcand: in std_logic_vector(3 downto 0); done: in std_logic); end entity mult4x4;
architecture beh of mult4x4 is
signal state: integer range 0 to 9;
signal ACC: std_logic_vector(8 downto 0); alias M: std_logic is ACC(0);
begin
process begin
end process;
end architecture;

## Slide 7: VHDL Code
process begin wait until (rising_edge(clock)); case state is
when 0 =>
if st = ‘1’ then
ACC(8 downto 4) <= “00000”; ACC(3 downto 0) <= Mplier”; state <= 1;
end if;
...
end case;
end process;
end architecture;

## Slide 8: VHDL Code
process ...
when 1|3|5|7 =>
if M = ‘1’ then
ACC(8 downto 4) <= add4(ACC(7 downto 4, Mcand, ‘0’); state <= state + 1;
else
ACC <= ‘0’ & ACC(8 downto 4);
state <= state + 2;
end if;
...
end case;
end process;
end architecture;

## Slide 9: VHDL Code
process ...
when 2|4|6|8 =>
ACC <= ‘0’ & ACC(8 downto 4);
state <= state + 1;
when 9 =>
state <= 0;
end case;
end process;
done <= ‘1’ when state = 9 else ‘0’;
-- concurrent statement since we want done signal is set -- to 1 in state 9, not in state 0.
end architecture;

## Slide 10: Multiplier with Counter
If the size of the operands are large, the previous approach does not work.
add-shift
control
counter
sh
Add
Load
Done
K
St
M
Completion signal

## Slide 11: State Diagram
S0
S1
S2
st/Load
S3
st’/0
K’M’/sh
M/Add
K’/sh
K/sh
-/done
KM’/sh

## Slide 12: Operation of the Counter
Time | state | counter | Product register | st | M | K | load | Add | Sh | Done
t0 | S0 | 00 | 000000000 | 0 | 0 | 0 | 0 | 0 | 0 | 0
t1 | S0 | 00 | 000000000 | 1 | 0 | 0 | 1 | 0 | 0 | 0
t2 | S1 | 00 | 000001011 | 0 | 1 | 0 | 0 | 1 | 0 | 0
t3 | S2 | 00 | 011011011 | 0 | 1 | 0 | 0 | 0 | 1 | 0
t4 | S1 | 01 | 001101101 | 0 | 1 | 0 | 0 | 1 | 0 | 0
t5 | S2 | 01 | 100111101 | 0 | 1 | 0 | 0 | 0 | 1 | 0
t6 | S1 | 10 | 010011110 | 0 | 0 | 0 | 0 | 0 | 1 | 0
t7 | S1 | 11 | 001001111 | 0 | 1 | 1 | 0 | 1 | 0 | 0
t8 | S2 | 11 | 100011111 | 0 | 1 | 1 | 0 | 0 | 1 | 0
t9 | S3 | 00 | 010001111 | 0 | 1 | 0 | 0 | 0 | 0 | 1