## Slide 1: VHDL Modeling Behavior from Synthesis Perspective - Part B -
EL 310
Erkay Savaş
Sabancı University

## Slide 2: The Wait Statement
Syntax
  wait until condition;
Different forms
  wait until(clk’event and clk = ‘1’);
  wait until(rising_edge(clk));
  wait until(falling_edge(clk));
It implies synchronous logic.
  Consider a circuit where signal values are stored in edge-triggered flip-flops and their values are updated in the clock edge.
  Therefore, all signals whose values are controlled by the wait statement will be synthesized into edge-triggered flip-flops.

## Slide 3: Wait vs. If-Then-Endif Statement
Only one wait statement is permitted in a process and it must be the first statement.
  Then, an edge-triggered flip-flop will be inferred for every signal in the process.
We do not always want to generate flip-flops for every signal
  Then we must use if-then-endif construct.
  Edge detection expression limits the flip-flop inference to signals assigned in the body of then statement.
  The remaining statements will lead to combinational logic.

## Slide 4: Synchronous Logic with Wait Statement
library IEEE; use IEEE.std_logic_1164.all;
entity edge is port (reset, clk: in std_logic; Aout, Bout: out integer range 0 to 3); end entity edge;
architecture behavioral of edge is begin process begin wait until (rising_edge(clk)); if reset = ‘1’ then Aout <= 0; Bout <= 1; else Aout <= 2; Bout <= 2; end if; end process;
end architecture behavioral;

## Slide 5: Synchronous Logic with Wait Statement

## Slide 6: Example in the Textbook
library IEEE; use IEEE.std_logic_1164.all;
entity edge is port (reset, clk: in std_logic; Aout, Bout: out integer range 0 to 3); end entity edge;
architecture behavioral of edge is begin process begin wait until (rising_edge(clk)); if reset = ‘1’ then Aout <= 1; else Aout <= 3; end if; Bout <= 0; end process;
end architecture behavioral;

## Slide 7: Example in the Textbook
Warning message gotten from the synthesis compiler:
All reachable assignments to bout(0) and bout(1) to assign ‘0’, register removed by optimization.

## Slide 8: Synchronous Logic with If Statement
library IEEE; use IEEE.std_logic_1164.all;
entity edge is port (reset, clk: in std_logic; x: in integer range 0 to 3; Aout, Bout: out integer range 0 to 3); end entity edge;
architecture behavioral of edge is begin process(clk, reset, x) is begin if reset = ‘1’ then Aout <= x; else Aout <= x+1; end if; if(rising_edge(clk)) then Bout <= x; end if; end process;
end architecture behavioral;

## Slide 9: Synchronous Logic with If Statement

## Slide 10: Synthesis vs. Simulation Semantics
library IEEE; use IEEE.std_logic_1164.all;
entity semantics is port (reset, clk, x, y, z: in std_logic; aout, bout: in std_logic); end entity semantics;
architecture behavioral of semantics is signal sig_a, sig_b: std_logic; begin process begin wait until (rising_edge(clk)); if reset='1' then sig_a <= '0'; sig_b <= '0'; else sig_a <= x and y; sig_b <= sig_a xor z; end if; aout <= sig_a bout <= sig_b; end process; end architecture behavioral;

## Slide 11: Synthesis vs. Simulation Semantics
Simulation and Synthesis semantics match in this specific example

## Slide 12: Synthesis vs. Simulation Semantics
library IEEE; use IEEE.std_logic_1164.all;
entity semantics is port (x, y, z: in std_logic; w: out std_logic); end entity semantics;
architecture behavioral of semantics is signal s1, s2: std_logic; begin process(x, y, z) is begin L1: s1 <= x xor y; L2: s2 <= s1 or z; L3: w <= s1 nor s2; end process; end architecture behavioral;

## Slide 13: Synthesis vs. Simulation Semantics
w = [(x  y) + ((x  y) + z)]’ = [(x  y) + z]’
Semantics of simulation and synthesis do not match
  In behavioral simulation, the value of the signal s1 used in statement L2 is the one before this execution of process. This implies usage of a latch.
  The synthesized logic is optimized and purely combinational
x
y
z
w

## Slide 14: Variables with Wait Statement
library IEEE; use IEEE.std_logic_1164.all;
entity var_wait is port (x, y, z, clk: in std_logic; w: out std_logic); end entity var_wait;
architecture behavioral of var_wait is begin process is variable a_var, b_var: std_logic; begin wait until (rising_edge(clk)); L1: a_var := x or y; L2: b_var := a_var nor z; L3: w <= b_var xor y; end process; end architecture behavioral;

## Slide 15: Variables with Wait Statement
Unlike signals, variable assignments take affect immediately.
Variables are usually collapsed into combinational logic unless a variable is used before it is defined.
x
y
z
w
clk
a_var_1
b_var
w_1
w

## Slide 16: Variables with Wait Statement
Let us change the statement L1 in the previous example as follows:
  a_var := (x or y) nor b_var;
x
y
z
w
clk
a_var
b_var
w_1
w
b_var_1

## Slide 17: Caveat
We expect that level-sensitive or edge-sensitive expressions within the conditional part of the code determine whether latches or flip-flops are inferred.
However, some synthesis compiler may still infer flip-flops regardless of whether the conditional expression is level- or edge- sensitive.

## Slide 18: Synthesis of State Machines
State
Elements
Inputs
Mealy Outputs
Next state
state
clk
Combinational Network
Output Function
Next State Function
Output Function
Combinational Network
Moore Outputs

## Slide 19: Encoding of State Elements
Function of number of states
  For example, eight states  3 bits to represent each state uniquely.
  Which state is numbered with what number?
State | Sequential | Gray Code | One Hot
0 | 000 | 000 | 00000001
1 | 001 | 001 | 00000010
2 | 010 | 011 | 00000100
3 | 011 | 010 | 00001000
4 | 100 | 110 | 00010000
5 | 101 | 111 | 00100000
6 | 110 | 101 | 01000000
7 | 111 | 100 | 10000000
most compact

## Slide 20: FSM Compiler & Explorer in Synplify Pro
FSM Compiler
  automatically recognizes state machines in your design and optimizes them.
  extracts the state machines as symbolic graphs, and then optimizes them by re-encoding the state representations
  Optimization with respect to time and/or area.
  and generating a better logic optimization starting point for the state machines.
FSM Explorer
  uses the state machines extracted by the FSM Compiler when it explores different encoding styles.

## Slide 21: Encoding in Synplify Pro
When FSM compiler is enabled
  default encoding style automatically assigns encoding based on the number of states in the state machine as follows:
  sequential for 0-4 states
  One Hot for 5-24 states
  gray for > 24 states
Syn_state_directive allows to choose
  sequential
  gray
  One Hot
  Safe: default encoding & add reset logic to force the state machine to a known state if it reaches an invalid state.

## Slide 22: State Machine Synthesis: Example
library IEEE; use IEEE.std_logic_1164.all;
entity state_machine is port (reset, x, clk: in std_logic; w: out std_logic); end entity state_machine ;
architecture behavioral of state_machine is type state_type is (state0, state1); signal state, next_state: state_type; begin process is begin wait until (rising_edge(clk)); if reset = ‘1’ then w <= ‘0’; else ... end if; end process; end architecture behavioral;

## Slide 23: State Machine Synthesis: Example
...
process begin wait until (rising_edge(clk)); if reset = ‘1’ then w <= ‘0’; else case state is when state0 => if x = ‘0’ then state <= state1; w <= ‘1’; else state <= state0; w <= ‘0’; end if; when state1 => if x = ‘1’ then state <= state0; w <= ‘1’; else state <= state1; w <= ‘0’; end if; end case; end if; end process; end architecture behavioral;
This is a Mealy machine where output w is a function of both the state and the input.

## Slide 24: State Machine Synthesis: Example
unnecessary flip-flop for output signal
one flip-flop
for encoding two state

## Slide 25: State Machine Synthesis: Better VHDL
... ns_process: process(state, x) is begin case state is when state0 => if x = '0' then next_state <= state1; w <= '1'; else next_state <= state0; w <= 0; end if; when state1 => if x = '0' then next_state <= state0; w <= '0'; else next_state <= state1; w <= '1'; end if; end case; end process ns_process;
clk_process: process(reset, clk) begin if (rising_edge(clk)) then if (reset = '1') then state <= state_type'left; else state <= next_state; end if; end if; end process clk_process;
end architecture;

## Slide 26: State Machine Synthesis: Better VHDL
No unnecessary latch for output signal which is dependent on the state and input

## Slide 27: Another Example
entity sm1_2 is port (x, clk: in std_logic; z: out std_logic); end entity sm1_2;
architecture behavioral of sm1_2 is subtype s_type is integer range 0 to 7; signal state, next_state: s_type; constant s0: s_type := 0; constant s1: s_type := 4; constant s2: s_type := 5; constant s3: s_type := 7; constant s4: s_type := 6; constant s5: s_type := 3; constant s6: s_type := 2; begin
clk_process: process(clk) begin if (rising_edge(clk)) then state <= next_state; end if; end process clk_process;

## Slide 28: Another Example
ns_process: process(state, x) is begin z <= '0'; next_state <= s0; case state is when s0 => if x = '0' then z <= '1'; next_state <= s1; else z <= '0'; next_state <= s2; end if; when s1 => if x = '0' then z <= '1'; next_state <= s3; else z <= '0'; next_state <= s4; end if; when s2 => if x = '0' then z <= '0'; next_state <= s4; else z <= '1'; next_state <= s4; end if; when s3 => if x = '0' then z <= '0'; next_state <= s5; else z <= '1'; next_state <= s5; end if; when s4 => if x = '0' then z <= '1'; next_state <= s5; else z <= '0'; next_state <= s6; end if; when s5 => if x = '0' then z <= '0'; next_state <= s0; else z <= '1'; next_state <= s0; end if; when s6 => if x = '0' then z <= '1'; next_state <= s0; when others => null; end case; end process; end architecture;

## Slide 29: Null Statement
a sequential statement that does not cause any action to take place; execution continues with the next statement.
  In the previous example, when others => null; implies that no action needs to be performed when state is any other than specified in the case statement.
  Recall that all choices must be covered in case statements.
  Sometimes it is useful to explicitly say that no action needs to be performed
  case or if statements.

## Slide 30: Design Process
Develop the VHDL models and use simulation to verify the functional correctness of the model.
The model is then synthesized
Synthesized model is simulated to verify the performance.
Simulation of VHDL model and simulation model of the synthesized model may behave differently.
This is what is called semantic mismatch.

## Slide 31: Simulation vs. Synthesis
Incomplete sensitivity list:
  In VHDL model simulation, sensitivity list can include only a few signals and exclude the others.
  Especially, if the process produces a combinational logic, then the circuit will be “sensitive” to a change on any of the signals that are manipulated in the process.
  process (sel) is begin if(sel=‘1’ and En=‘0’) then A<=‘1’; else A<= ‘0’; end if; end process;
  The synthesized circuit will also be sensitive to the signal En.

## Slide 32: Simulation vs. Synthesis
Sequential signal assignments in a process
  the code below show sequential behavior in VHDL simulation
  process (x, y, z) begin L1: s1 <= x xor y; L2: s2 <= s1 or z; L3: w <= s1 nor s2; end process;
  However, synthesis compiler will generally optimize this sequence to produce combinational logic and avoid latches.

## Slide 33: Simulation vs. Synthesis
User specified delays may not match the actual delays in the synthesized circuit.
Simulation Overhead:
  Conditional and selected CSA can be modeled using process.
  Since CSAs are always active, it has more simulation overhead.
  CSAs, on the other hand, are better for synthesis.
Speed:
  Use of variables in process will result in faster simulation.
  Use of process may obscure the concurrency within the process and may reduce the effectiveness of the inference mechanisms.

## Slide 34: Synthesis Hints
The while-loop statement may not be supported by some synthesis compiler, since iteration number is data dependent.
All for loop indices must have statically determinable loop ranges.
In order to avoid inference of an unnecessary latch for a signal, every execution path through the process must assign a value for that signal.
A latch will be inferred for a variable if it is used before it is defined.
Initialize your signals (if you must do so) explicitly under the control of reset signal. Otherwise, initialization may be ignored by the compiler.

## Slide 35: Synthesis Hints
Include all signals in a process in the sensitivity list of the process.
The VHDL code should imply hardware. Avoid purely algorithmic descriptions of hardware.
To avoid latches for a signal that appears in conditional statements, make sure that default values are assigned to this signals before a conditional block of code.
Try to minimize dependencies between statements.
Using don’t care values to cover when others case in a case statement can enable the compiler to optimize the logic. Try to avoid setting signals to specific values “0000” or “1111” in when others.

## Slide 36: Synthesis Hints
If possible try to specify data ranges for signals.
Minimize signal assignment statements in a process and use variables.
Use if-then-else statements to infer flip-flops rather than wait statements. To infer flip-flop with a wait statement necessitates that wait statement must be the first and only wait statement in the process; thus leading to flip-flop inference for every signal in the process.
Do not use don’t care symbols in comparisons. Such comparisons will always return FALSE.
Check vendor specific constraints on the permitted types and range for the for-loop index

## Slide 37: Synthesis Hints
Move common complex operations out of the branches of conditional statements.
Using a case statement rather than if-then-elsif will produce less logic since priority logic will have to be generated for the latter.
The choice of coding style must be guided by the building blocks that are available in the target technology. For example, if latches are not available, then level sensitive expressions will lead to the synthesis of latches in gate level equivalents. This will complicate the circuit and timing analysis.