## Slide 1: VHDL Miscellaneous
EL 310
Erkay Savaş
Sabancı University

## Slide 2: VHDL as a High-Level Synthesis Tool
VHDL is proposed to model the behavior of the existing hardware
VHDL was not originally intended for automatic synthesis of hardware.
In 1987, when the VHDL standard was written, there were no automatic synthesis tools in widespread use.
The meanings of some VHDL constructs in hardware are derived later.
As a consequence, some parts of VHDL are not suitable for synthesis.
Aim is to fully automate the design process using high-level behavioral model.

## Slide 3: VHDL as a High-Level Synthesis Tool
Specification
Architectural
design
state machine/
RTL design
gate-level
logic design
place and
route
RTL
synthesis
Behavioral
synthesis

## Slide 4: RTL Synthesis vs. Behavioral Synthesis
RTL synthesis tools take a VHDL description of a design in terms of registers, state machines and combinational logic functions and generate a netlist of gates and library cells.
Behavioral synthesis tools take algorithmic VHDL models and transform them to gates and cells.
  For example,there is no need to specify clock inputs
  one may simply specify a certain time interval in which a particular operation is completed.
RTL synthesis tools are in widespread use while behavioral synthesis tools are rare.

## Slide 5: RTL Synthesis
Starting point is a model described in terms of combinational and sequential building blocks and state machines.
We have to know all the inputs and outputs of the system, including the clock and resets.
We may also have to know the number of states in state machines
  RTL synthesis tools, in general, do not perform state minimization.
Constraints can be specified
  particular form of state encoding, area and speed constraints, etc.
  Constraints are not part of VHDL and unique to particular tools, but some of them may be included in the VHDL description.

## Slide 6: RTL Synthesis
Three styles of VHDL
Structural
Dataflow (CSA)
  was originally intended for RTL modeling,
  most of dataflow constructs are synthesizeable.
Behavioral
  intended for high-level, algorithmic modeling

## Slide 7: IEEE 1076.6-1999 Standard
It defines a subset of VHDL for synthesis
The purpose is a minimum subset that can be accepted to any synthesis tool.
Certain constructs, for example delays and floating-point operators are not synthesizeable.
  Floating-point data types will be rejected by synthesis tools because they require at least 32 bits and the hardware required for many operations is too large for most ASICs and FPGAs.

## Slide 8: Non-synthesizeable VHDL
The following VHDL constructs are either ignored or rejected by RTL synthesis tools
after, transport, inertial keywords.
  A model can be synthesized to meet various constraints, but cannot be synthesized to meet some exact timing model.
  For example, it is not possible to specify that a gate will have a delay of exactly 5 ns.
  But it is reasonable to require synthesis tool to generate a block of combinational logic such that its total delays is less than, say 20 ns.

## Slide 9: Non-synthesizeable VHDL
wait for construct is also ignored
  we may not be able to built a piece of hardware whose delay is exactly specified.
File operations
default values must be specified for parameterized models.
pointers, specified by the access keyword are not recognized by synthesis tools.
  high-level data structures, such as linked lists and trees, that is possible with pointers are not, therefore, supported.
Initial values of signals and variables are ignored.

## Slide 10: Constraints
For any non-trivial digital function, there exist a number of alternative implementations.
What we want is a infinitely fast, infinitesimally small, and totally testable system that consumes no power.
The designer should decide the objectives
These objectives are expressed to synthesis tools as constraints.
  a design must fit on a particular FPGA, has to operate at a particular clock frequency, etc.
  But sometimes, these objectives may not be met.

## Slide 11: Constraints
A
B
C
D
E
Implementation 1: 16 transistor, 4 gate delays
D
C
A
B
D
E
Implementation 2: 18 transistor, 3 gate delays

## Slide 12: Timing Constraints
Assume we want a circuit to operate synchronously with a clock at a particular frequency, say 20 MHz
  Then, the maximum delay through the state registers and the next state logic must be at most 50 ns.
  A constraint can be expressed as the clock frequency or maximum delay through the combinational logic.
DFF
Q
clk (clock frequency is 50 MHz, maximum delay through combinational logic is 48 ns)
DFF
Q
combinational
logic
delay 1 ns
delay 1 ns

## Slide 13: Timing Constraints
What synthesis tool does is
  delay through combinational logic can only be estimated.
  exact delay depends on how the combinational logic is laid out.
  Synthesis is performed using an estimate of the likely delays
  In the end, the design objectives may not be met.
  Synthesis must be restarted.
  to speedup the hardware more operations are performed concurrently, which means that the design is larger.

## Slide 14: Synthesis for FPGAs
Xilinx and Actel FPGAs
Xilinx is based on Static RAM technology,
  volatile
  it has tri-state buffers
Actel is based on antifuse technology.
  A connection is normally open circuit, but the application of a suitably large voltage causes a short circuit to be formed.
  not reversible.
  no tri-state buffers

## Slide 15: Synthesis for FPGAs
Both FPGA technologies feature high ratio of flip-flops to combinational logic.
  emphasis is not on minimizing the number of flip-flops, but the combinational logic surrounding them.
  One-hot state encoding is popular, particularly for relatively small state machines.
A single asynchronous set or reset is the most efficient way of initializing all the flip-flops in an FPGA device
  Each flip-flop has an asynchronous set and reset, but only only one of these may be used at one time.

## Slide 16: Synthesis for FPGAs
In both technologies, the flip-flops are edge-sensitive
  level-sensitive latches have to be synthesized from combinational logic.
  This can waste flip-flops and they are best avoided.
It is desirable to instantiate predefined library components for certain functions.
  It is safer (talk about it later)
  Not only the logic is defined, but the configuration of logic blocks is already known
  This potentially simplifies both RTL synthesis and place and route tasks.

## Slide 17: Synthesis for FPGAs
ACTEL technology does not support tri-state buffers,
  language constructs that will result in tri-state buffer usage must be avoided.
The two technologies have different limitations with respect to fan-outs.
  In antifuse technology, one output can drive up to 16 inputs without degradation of the signal.
  CMOS SRAM technology has higher fan-out limit.
  A design that can easily be synthesized to a Xilinx technology may not be synthesized to an ACTEL FPGA without rewriting.

## Slide 18: Fan-Out Limitations: Example
signal a, b: std_ulogic_vector(31 downto 0);
begin
p0: process (enable, b) is begin
if enable = ‘1’ then a <= b;
else
a <= (others => ‘0’);
end if;
end process
end;
this simple VHDL code fragment may not be synthesized since enable signal is controlling 32 multiplexers.
Instead, it must be split into two using buffers, and each buffered signal then controls half the bus.

## Slide 19: Fan-Out Limitations: Example
signal a, b: std_ulogic_vector(31 downto 0);
signal en0, en1: std_ulogic;
begin
b0: buf port map (enable, en0);
b1: buf port map (enable, en1);
p0: process (en0, en1, b) is begin if en0 = ‘1’ then a(15 downto 0) <= b (15 downto 0);
else a (15 downto 0) <= (others => ‘0’);
end if;
if en1 = ‘1’ then a(31 downto 16) <= b (31 downto 16);
else a (31 downto 16) <= (others => ‘0’);
end if;
end process
end;
A good synthesis tool should recognize the fan-out limits, and automatically insert buffers

## Slide 20: Asynchronous Sequential Design
Why bother with asynchronous logic design?
  power considerations
  Due to ultra fast clocks (as a result high clock skews) systems may consist of synchronous islands that communicate asynchronously.
However, it is better to avoid asynchronous structures
  synthesis tools are intended for the design of synchronous systems, normally with a single clock.
For example, the following concurrent VHDL construct
q <= d when c = ‘1’ else q;
would be synthesized to an asynchronous circuit structure.

## Slide 21: Asynchronous Sequential Design
Similarly the above sequential block would also be synthesized to an asynchronous latch.
But the circuit structures for these two constructs are not identical.
In fact, a IEEE 1076.6 compliant synthesis tool would infer a latch from the incomplete if statement and use a latch from library.
process (d, c) is begin if c = ‘1’ then q <= d;
end if;
end process;

## Slide 22: Asynchronous Latch Inference
The latch created by Boolean minimization (the first case) and the library latch is not the same.
Indeed, the RTL synthesis standard, IEEE 1076.6, explicitly forbids the use of such concurrent statements
It only permits the use of incomplete if and case statements.
To see why, we have to look at a basic D latch and its timing characteristics.

## Slide 23: D-Latch
Assume each gate has a delay of 1 unit time, say 1 ns.
We will show that oscillatory behavior will occur.
D
C
C’
E
F
Q
q <= (d and c) or (q and not c);

## Slide 24: Oscillatory Behavior of D-Latch
D
C
C’
E
F
Q
1 ns
2
3
4
5
6
7
8
9

## Slide 25: Gate Level Implementation of D-Latch
library ieee; use ieee.std_logic_1164.all;
entity d_latch is
generic (delay: Time := 1 ns);
port(q: inout std_logic;
q_bar: out std_logic;
d, c: in std_logic);
end entity d_latch;
architecture concurrent of d_latch is
signal e, f, c_bar: std_logic;
begin
e <= d nand c after delay;
c_bar <= not c after delay;
f <= c_bar nand q after delay;
q <= e nand f after delay;
q_bar <= not q;
end architecture concurrent;

## Slide 26: Test Bench for D-Latch
library ieee;
use ieee.std_logic_1164.all;
entity d_latch_tb is
end entity d_latch_tb;
architecture concurrent of d_latch_tb is
component d_latch is
generic (delay: Time := 1 ns);
port(q: inout std_logic; q_bar: out std_ulogic;
d, c: in std_ulogic);
end component d_latch;
signal D, C, Q: std_ulogic := '1';
signal Q_bar: std_ulogic := '0';
begin
d0: d_latch port map(q => Q, q_bar => Q_bar, d => D, c => C);
C <= '0' after 1 ns;
Q_bar <= not Q;
end architecture concurrent;

## Slide 27: Simulation Results

## Slide 28: More Realistic Model for Timing
library ieee; use ieee.vital_primitives.all;
...
architecture vtl of d_latch is
signal e, f, c_bar: std_logic;
begin
VitalNAND2(e, d, c, (delay, delay), (delay, delay));
VitalINV(c_bar, c, (delay, delay));
VitalNAND2(f, c_bar, q, (delay, delay), (delay, delay));
VitalNAND2(q, e, f, (delay, delay), (delay, delay));
q_bar <= not q;
end architecture vtl;

## Slide 29: Behavioral Synthesis
RTL synthesis requires that the design be specified in terms of register operations.
Behavioral synthesis takes the process one stage further
  the hardware to be synthesized in terms of an algorithm. from which, the registers and logic are derived.
Main obstacle is the inefficient or infeasible hardware generated by the behavioral synthesis tools
  with the decreasing cost of silicon, it seems safe to predict that behavioral synthesis will become in widespread usage in the future.

## Slide 30: Behavioral Synthesis: Example
package iir_defs is
constant precision: positive := 16;
subtype int is integer range –2**(precision – 1) to
2**(precision –1) – 1;
type integer_array is array (natural range <>) of int;
constant order: positive := 5;
end package iir_defs;
5th order infinite impulse response (IIR) filter

## Slide 31: IIR Filter Design
use work.iir_defs.all;
entity iir is
generic(coeffa: integer_array(0 to order);
coeffb: integer_array(0 to order-1));
port(input: in int;
strobe: in bit;
output: out int);
end entity iir;

## Slide 32: IIR Filter Design
architecture beh of iir is begin
process is
variable input_sum, output_sum: int;
variable delay:integer_array(0 to order):=(others => 0);
begin
input_sum := input;
for j in 0 to order-1 loop input_sum := input_sum + (delay(j)*coeffb(j))/1024; end loop;
output_sum := (input_sum*coeffa(order))/1024;
for k in 0 to order-1 loop input_sum := input_sum + (delay(k)*coeffa(k))/1024; end loop;
...

## Slide 33: IIR Filter Design
...
for m in 0 to order-1 loop delay(m) := delay(m+1); end loop;
delay(order) := input_sum;
output <= output_sum;
wait on strobe;
end process;
end architecture beh;
A C version of the algorithm would look very similar
It has neither a clock nor a reset.
If this code is given to RTL synthesis tool, the resulting hardware would have 12 16-bit combinational multipliers 11 16-bit adders.
The same operation can be done by using one adder and one multiplier.

## Slide 34: Principles of Behavioral Design
For sake of simplicity, consider a first-order filter.
input_sum := input + delay(0)*coeffb(0);
output_sum := input_sum*coeffa(1);
output_sum := output_sum + delay(0)*coeffa(0);
output := output_sum + delay(1)*coeffa(1);
To figure out the data dependency, rewrite the code fragment as follows
input_sum := input + delay(0)*coeffb(0);
output_sum0 := input_sum*coeffa(1);
output_sum1 := output_sum0 + delay(0)*coeffa(0);
output := output_sum1 + delay(1)*coeffa(1);

## Slide 35: Principles of Behavioral Design
Data dependency graph of first-order IIR filter

+
output
input
delay(0)
coeffb(0)
coeffa(1)
coeffa(0)
delay(1)

input_sum
+
output_sum0
+
output_sum1



## Slide 36: Principles of Behavioral Design
ASAP schedule
+

+
+
output
input
delay(0)
coeffb(0)
coeffa(1)
coeffa(0)
delay(1)
cycle
1
2
3
4
5




## Slide 37: Principles of Behavioral Design
Unconstrained ALAP Schedule

+

+
+
output
input
delay(0)
coeffb(0)
coeffa(1)
coeffa(0)
delay(1)


cycle
1
2
3
4
5

## Slide 38: Principles of Behavioral Design
Resource constrained schedule

+

+
+
output
input
delay(0)
coeffb(0)
coeffa(1)
coeffa(0)
delay(1)


cycle
1
2
3
4
5
6
7

## Slide 39: Mapping of Operations onto Resources

+


+

+
output
input
delay(0)
coeffb(0)
coeffa(1)
coeffa(0)
delay(1)
cycle
1
2
3
4
5

## Slide 40: Schedule Showing Registers

+


+

+
output
input
delay(0)
coeffb(0)
coeffa(1)
coeffa(0)
delay(1)
cycle
1
2
3
4
5
R1
R2
R3
R4
R5
R6
R7
R8
R9
R10
R11

## Slide 41: Hardware Implementation of First-Order Filter

+
delay(0)
coeffa(1)
coeffb(0)

delay(1)
coeffa(0)
coeffa(1)
delay(0)
R2/R7
R3/R6
R5/R9
R8/R11
R1
input
R4/R10
output

## Slide 42: ASM Chart of Controller
R1 input
R2delay(0) * coeffb(0)
R3delay(0) * coeffa(0)
R4 R1 + R2
R5R3
R3delay(1) * coeffa(1)
R2 R4 * coeffa(1)
R8R5
R5R3
R4 R2 * R8
R8R5
output R4 + R8

## Slide 43: VHDL Standards
IEEE Std 1076-1993
  Formal definition of VHDL
IEEE Std 1076.1-1999 (VHDL-AMS)
  Analog and mixed extensions to IEEE Standard VHDL
IEEE Std 1076.2-1996
  IEEE standard VHDL mathematical packages
  real and complex functions for VHDL
IEEE Std 1076.3-1997
  IEEE standard VHDL synthesis packages
  define signed and unsigned types and arithmetic functions, for use with synthesis tools

## Slide 44: VHDL Standards
IEEE Std 1076.4-1995
  IEEE standard VITAL ASIC modeling
  VITAL (VHDL Initiative Towards ASIC Libraries) is a set of low-level primitives for accurate timing simulations of gate-level models.
IEEE Std 1076.6-1999
  IEEE standard for VHDL register transfer level synthesis
  defines a subset of VHDL appropriate to RTL synthesis.
IEEE Std 1164-1993
  IEEE standard multivalue logic system for VHDL model interoperability.

## Slide 45: VHDL Standards
IEEE Std 1029.1-1998
  IEEE standard for waveform and vector exchanges (WAVES)
  WAVES (Waveform and Vector Exchange to Support Design and Test Verification) is a set of VHDL methods to assist in verifying and testing hardware.
  The motivations is to allow test vector files to be shared between VHDL simulators and hardware testers.

## Slide 46: Verilog
Seen as an alternative to VHDL
developed in early 1980s by Gateway Design Automation, which was later taken over by Cadence.
It is an IEEE standard (1364).
Resembles the C programming language while VHDL is closer to Ada.
Said to be simpler and closer to hardware than VHDL.
It can be used to model logic circuits at the transistor or switch level.

## Slide 47: Verilog
Fault simulators have been developed to use Verilog, while such tools are almost non-existent for VHDL.
On the other hand, VHDL has high-level constructs and abstract data types that Verilog does not have
  This feature makes VHDL much more suitable to behavioral modeling.
Many simulation and RTL synthesis tools accept both.
  use VHDL for high-level design and Verilog for low-level post-synthesis timing and fault simulation

## Slide 48: Basics of Verilog
A Verilog Model of two-input NAND gate
// comment
module NAND (in1, in2, out);
input in1, in2;
output out;
assign out = ~(in1 & in2);
endmodule // Note no semicolon
Verilog is case-sensitive
It does not have separate interface and implementation section – everything in a module.
Signals do not have types.
A signal can take the values: 0, 1, X, Z.
assign introduces a assignment statement analogous to CSA.

## Slide 49: Basics of Verilog
The bitwise operators: ~, &, |, ^.
To instantiate a module, it simply has to be invoked.
module simple (a, b, c, d);
input a, b, c;
output d;
wire p, q; // can be omitted
NAND g1(a, b, p);
NAND g2(a, c, q);
NAND g3(p, q, d);
endmodule

## Slide 50: Procedures with Verilog
module MUX (SEL, A, B, C, D, Y);
input [1:0] SEL; // two bit vector
input A, B, C, D;
output Y;
reg Y; // needed for procedural assignment
always @(SEL or A or B or C or D)
case (SEL)
2’b00 : Y = A;
2’b01 : Y = B;
2’b10 : Y = C;
2’b11 : Y = D;
default : Y = A;
endcase
endmodule

## Slide 51: Basics of Verilog
module LATCH (enable, D, Q);
input enable, D;
output Q;
reg Y; // needed for procedural assignment
always @(enable or D)
if (enable)
Q = D;
endmodule
Level-sensitive latch can be modeled using an incomplete if statement (as in VHDL)

## Slide 52: Non-Blocking Assignment Statements
module LATCH (enable, D, Q);
input enable, D;
output Q;
reg Y;
reg M;
always @(enable or D)
if (enable)
begin
M <= D
Q <= M;
end
endmodule
Like VHDL signal assignments, all non-blocking assignments are completed at the end of the current time period.
No concept of delta delays
This example will synthesize to two latches.

## Slide 53: Blocking Assignment Statements
module LATCH (enable, D, Q);
input enable, D;
output Q;
reg Y;
reg M;
always @(enable or D)
if (enable)
begin
M = D;
Q = M;
end
endmodule
A blocking statement must be completed before control passes to the next statement.
This is similar to variable assignment in VHDL.
One latch will be inferred.

## Slide 54: Edge-Triggered Flip-Flop
module DFF (clock, D, Q);
input clock, D;
output Q;
reg Q;
always @(posedge clock)
Q = D;
endmodule
A negative edge would be detected using negedge

## Slide 55: Flip-Flop with Asynchronous Reset
module DFF (clock, reset, D, Q);
input clock, reset, D;
output Q;
reg Q;
always @(posedge clock or negedge reset)
if (!reset)
Q = 0;
else
Q = D;
endmodule
Verilog does not have enumerated types
State machines require that the state assignment to be explicitly stated.

## Slide 56: State Machines with Verilog
module vending (clock, reset, twenty, ten, ready, dispense, ret, coin);
input clock, reset, twenty, ten;
output ready, dispense, ret, coin;
reg ready, dispense, ret, coin;
parameter A = 0, B = 1, C = 2, D = 3, F = 4, I = 5;
reg [0:2] present_state, next_state;
always @(posedge clock or posedge reset)
if (reset)
present_state = A;
else
present_state = next_state;
...
endmodule

## Slide 57: State Machines with Verilog
module vending (clock, reset, twenty, ten, ready, dispense, ret, coin);
...
always @(twenty or ten or present_state)
begin ready = 0;
dispense = 0;
ret = 0;
coin = 0;
case (present_state)
A: begin
ready = 1;
if (twenty) next_state = D;
else if (ten) next_state = C;
else next_state = A;
end
...
endmodule

## Slide 58: State Machines with Verilog
case (present_state)
...
B: begin
dispense = 1; next_state = A;
end
C: begin
coin = 1;
if (twenty) next_state = F;
else if (ten) next_state = D;
else next_state = C;
end
...
endmodule

## Slide 59: State Machines with Verilog
case (present_state)
...
D: begin
coin = 1;
if (twenty) next_state = B;
else if (ten) next_state = F;
else next_state = D;
end
F: begin
coin = 1;
if (twenty) next_state = I;
else if (ten) next_state = B;
else next_state = F;
end
...
endmodule

## Slide 60: State Machines with Verilog
...
case (present_state)
...
I: begin
ret = 1;
next_state = A;
end
default next_state = A;
endcase
end
endmodule

## Slide 61: Testbench with Verilog
‘timescale 1ns / 100 ps
module testbench;
reg clock, reset, twenty, ten;
wire ready, dispense, ret, coin;
vending vm (clock, reset, twenty, ten, ready, dispense, ret, coin);
initial clock = 0;
always #10 clock = !clock;
initial
begin
reset = 1; twenty, = 0; ten = 0;
#1 reset = 0;
#64 twenty = 1;
#80 twenty = 0;
#20 ten = 1;
#20 ten = 0;
#20 twenty = 1;
#20 twenty = 0;
end
endmodule

## Slide 62: Switch-Level Modeling with Verilog HDL
Two types of MOS switches are specified in Verilog HDL
  nmos (drain, source, gate);
  pmos (drain, source, gate);
Switch level implementation of an inverter
  module inverter(Y, A); input A; output Y; supply1 PWR; supply0 GRD; pmos(Y, PWR, A); nmos(Y, GRD, A); endmodule

## Slide 63: Switch-Level Modeling with Verilog HDL
Switch level implementation of 2-input NAND gate
  module NAND2(Y, A, B); input A, B; output Y; supply1 PWR; supply0 GRD; wire W1; pmos(Y, PWR, A); pmos(Y, PWR, B); nmos(Y, W1, A); nmos(W1, GRD, B); endmodule