## Slide 1: VHDL Sub-Programs, Packages, & Libraries
EL 310
Erkay Savaş
Sabancı University

## Slide 2: Motivation
Structuring VHDL programs
  modularity
Design reuse
Manage the complexity
Available VHDL tools:
  procedures,
  functions,
  packages,
  libraries

## Slide 3: Issues
VHDL programs model physical systems
There may have some issues we have to deal with such as:
Can wait statements be used in a procedure?
Can signals be passed to procedures and be modified within the procedure?
How are procedures synthesized?
Can functions operate on signals?

## Slide 4: Packages & Libraries
Groups of procedures and functions that are related can be aggregated into a module that is called package.
A package can be shared across many VHDL models.
A package can also contains user defined data types and constants.
A library is a collection of related packages.
Packages and libraries serve as repositories for functions, procedures, and data types.

## Slide 5: Functions
A function computes and returns a value of specified type using the input parameters.
Function declaration:
  function rising_edge(signal clock: in std_logic) return Boolean;
Parameters are used but not modified within the function.
  the mode of input parameters is in.
  functions do not have parameters of mode out.
  In fact, we do not have to specify the mode.

## Slide 6: Function Definition
function rising_edge(signal clock: std_logic) return Boolean is
--
-- declarative region: declare variables local to the function
--
begin
--
-- body
--
return (value);
end function rising_edge;
formal parameters
The function is called with the actual parameters.
Example: rising_edge(enable);
Types of formal and actual parameters must match.
Actual parameters could be variable, signal, constant or an expression.

## Slide 7: Functions
When no class is specified, parameters are by default constants.
wait statements cannot be used in functions’ body.
  functions execute in zero simulation time.
Functions cannot call a procedure that has a wait statement in it.
Parameters have to be mode in.
  signals passed as parameters cannot be assigned values in the function body.

## Slide 8: Pure vs. Impure Functions
VHDL’93 supports two distinct types of functions:
Pure functions
  always return the same value when called with the same parameter values.
Impure functions
  may return different values even if they are called with the same parameter values at different times.
  All the signals in the architecture is visible within the function body
  Those signals may not appear in the function parameter list (e.g. ports of the entity)

## Slide 9: Example
library IEEE; use IEEE.std_logic_1164.all;
entity dff is port(d, clock: in std_logic; q, qbar: out std_logic); end entity dff;
architecture beh of dff is function rising_edge(signal clock:std_logic) return Boolean is variable edge: Boolean:=FALSE; begin edge:= (clock = ‘1’ and clock’event); return (edge); end function rising_edge; begin
output: process is begin wait until (rising_edge(clock)); q <= d after 5 ns; qbar <= not d after 5 ns; end process output;
end architecture beh;
declarative
region of
architecture

## Slide 10: Type Conversion Functions
function to_bitvector(svalue: std_logic_vector) return bit_vector is
variable outvalue: bit_vector(svalue’length-1 downto 0);
begin
for i in svalue’range loop –- scan all elements of the array
case svalue(i) is
when ‘0’ => outvalue(i) := ‘0’;
when ‘1’ => outvalue(i) := ‘1’;
when others => outvalue(i) := ‘0’;
end case;
end loop;
return outvalue;
end function to_bitvector;
Unconstrained array

## Slide 11: std_logic_arith
type UNSIGNED is array (NATURAL range <>) of STD_LOGIC;
type tbl_type is array (STD_ULOGIC) of STD_ULOGIC;
constant tbl_BINARY : tbl_type :=
('X', 'X', '0', '1', 'X', 'X', '0', '1', 'X');
function CONV_INTEGER(ARG: UNSIGNED) return INTEGER is
variable result: INTEGER;
variable tmp: STD_ULOGIC;
-- synopsys built_in SYN_UNSIGNED_TO_INTEGER
-- synopsys subpgm_id 366
begin
-- synopsys synthesis_off
assert ARG'length <= 31
report "ARG is too large in CONV_INTEGER"
severity FAILURE;
result := 0;

## Slide 12: std_logic_arith
for i in ARG'range loop result := result * 2;
tmp := tbl_BINARY(ARG(i));
if tmp = '1' then
result := result + 1;
elsif tmp = 'X' then
assert false
report "There is an 'U'|'X'|'W'|'Z'|'-' in an arithmetic operand, the result will be 'X'(es)."
severity warning;
assert false
report "CONV_INTEGER: There is an 'U'|'X'|'W'|'Z'|'-' in an arithmetic operand, and it has been converted to 0."
severity WARNING;
return 0;
end if;
end loop;
return result; -- synopsys synthesis_on
end;

## Slide 13: std_logic_arith
function CONV_INTEGER(ARG: STD_ULOGIC) return SMALL_INT is
variable tmp: STD_ULOGIC; -- synopsys built_in SYN_FEED_THRU -- synopsys subpgm_id 370 begin -- synopsys synthesis_off tmp := tbl_BINARY(ARG);
if tmp = '1' then
return 1;
elsif tmp = 'X' then assert false report "CONV_INTEGER: There is an 'U'|'X'|'W'|'Z'|'-' in an arithmetic operand, and it has been converted to 0."
severity WARNING;
return 0;
else
return 0; end if;
-- synopsys synthesis_on
end;

## Slide 14: Resolution Functions
For system busses, we use resolved signals
CPU
MEM
Disk
I/O

## Slide 15: Resolution Functions
Wired-logic implementations
Z
weak pull up
device
0
X1
0
X2
0
Xn
Any Xi = 0 turns the switch on driving Z = 0
switch
with active
low input

## Slide 16: Resolution Functions
entity wired_and is
port( X1, X2, X3: in bit; Z : out resolved_bit); end entity;
architecture beh of wired_and is begin x_process: process(X1) is begin Z <= X1; end process;
y_process: process(X2) is begin Z <= X2; end process; z_process: process(X3) is begin Z <= X3; end process;
end architecture beh;

## Slide 17: Resolved Types in the IEEE 1164 Standard
type std_ulogic is ( ‘U’, -- uninitialized ‘X’, -- forcing unknown ‘0’, -- forcing 0 ‘1’, -- forcing 1 ‘Z’, -- high impedance ‘W’, -- weak unknown ‘L’, -- weak 0 ‘H’, -- weak 1 ‘-’, -- don’t care );
function resolved (s: std_ulogic_vector) return std_ulogic;
subtype std_logic is resolved std_ulogic;
Resolution function must perform an associative operations so that the order in which the multiple signal drivers are examined does not
affect the resolved value of the signal.

## Slide 18: Resolution Table for std_logic
 | U | X | 0 | 1 | Z | W | L | H | -
U | U | U | U | U | U | U | U | U | U
X | U | X | X | X | X | X | X | X | X
0 | U | X | 0 | X | 0 | 0 | 0 | 0 | X
1 | U | X | X | 1 | 1 | 1 | 1 | 1 | X
Z | U | X | 0 | 1 | Z | W | L | H | X
W | U | X | 0 | 1 | W | W | W | W | X
L | U | X | 0 | 1 | L | W | L | W | X
H | U | X | 0 | 1 | H | W | W | H | X
- | U | X | X | X | X | X | X | X | X

## Slide 19: Example: Multiple Drivers
entity resol is end entity;
architecture beh of resol is signal X, Y, Z, T: std_logic; begin X <= 'U', '1' after 10 ns, '0' after 20 ns; Y <= '1', 'W' after 10 ns, '-' after 20 ns; Z <= 'W', 'Z' after 10 ns, 'L' after 20 ns;
x_process: process(X) is begin T <= X; end process;
y_process: process(Y) is begin T <= Y; end process; z_process: process(Z) is begin T <= Z; end process;
end architecture beh;

## Slide 20: Example: Waveforms

## Slide 21: Resolution Function
architecture beh of resol02 is
function resolution (drivers: std_ulogic_vector) return std_logic is
type my_array_type is array (std_logic, std_logic) of STD_ULOGIC;
constant my_array : my_array_type :=
(('U', 'U', 'U', 'U', 'U', 'U', 'U', 'U', 'U'),
('U', 'X', 'X', 'X', 'X', 'X', 'X', 'X', 'X'),
('U', 'X', '0', 'X', '0', '0', '0', '0', 'X'),
('U', 'X', 'X', '1', '1', '1', '1', '1', 'X'),
('U', 'X', '0', '1', 'Z', 'W', 'L', 'H', 'X'),
('U', 'X', '0', '1', 'W', 'W', 'W', 'W', 'X'),
('U', 'X', '0', '1', 'L', 'W', 'L', 'W', 'X'),
('U', 'X', '0', '1', 'H', 'W', 'W', 'H', 'X'),
('U', 'X', 'X', 'X', 'X', 'X', 'X', 'X', 'X'));
variable tmp: std_ulogic;
begin
tmp := my_array(drivers(drivers'length-1),drivers(drivers'length-2));
for i in drivers'length-3 downto 0 loop
tmp := my_array(tmp, drivers(i));
end loop;
return tmp;
end function;

## Slide 22: Resolution Function
signal Z: std_ulogic;
begin
Z <= resolution("1HWW") after 20 ns;
end architecture beh;

## Slide 23: Example: Resolution Functions
Multi-chip module with multiple die
chip carrier
global
error
signal
die

## Slide 24: Example: Resolution Functions
library IEEE; use IEEE.std_logic_1164.all;
entity mcm is –- and empty entity declaration end entity mcm;
architecture beh of mcm is
function wire_or(sbus:std_ulogic_vector) return std_ulogic is begin for i in sbus’range loop if sbus(i) = ‘1’ then return ‘1’; end if; end loop; return ‘0’; end function wire_or;
subtype wire_or_logic is wire_or std_ulogic;
signal error_bus: wire_or_logic;
...
resolution function
base type

## Slide 25: Example: Resolution Functions
...
subtype wire_or_logic is wire_or std_ulogic;
signal error_bus: wire_or_logic; begin
chip1: process is begin ... error_bus <= ‘1’ after 2 ns; ... end process chip1; chip2: process is begin ... error_bus <= ‘0’ after 2 ns; ... end process chip2;
end architecture beh;

## Slide 26: Synthesis Example
entity func is port(data: in std_logic_vector( 7 downto 0); count: out integer range 0 to 7); end entity func;
architecture beh of func is
function ones(signal data: std_logic_vector) return integer is variable count: integer range 0 to 7; begin for i in data’range loop if data(i) = ‘1’ then count:= count + 1; end if; end loop; return (count); end function ones;
begin
check: process(data) is begin count <= ones(data); end process check;
end architecture beh;

## Slide 27: Synthesis Example (cont.)
count <= ones(data);
each time this function is called, internal variables are initialized, the function is executed, and output value is returned.
Internal variables do not retain value across different invocations.
The loop is unrolled if data(0) = ‘1’ then count := count + 1; end if; if data(1) = ‘1’ then count := count + 1; end if; ...
When synthesized, it will produce a combinational circuit with a long dependency.

## Slide 28: Synthesis Example (cont.)

## Slide 29: Yet Another Example
entity func02 is
port(data: in std_logic_vector(7 downto 0); parity: out std_logic);
end entity func02;
architecture beh of func02 is
function parity_func(signal data: std_logic_vector) return std_logic is
variable parity: std_logic:='0';
begin
for i in data'range loop
parity := parity xor data(i);
end loop;
return (parity);
end function parity_func;
begin
parity_process: process(data) is
begin
parity <= parity_func(data);
end process check;
end architecture beh;

## Slide 30: Yet Another Example

## Slide 31: Procedures
Similar to functions
distinguishing feature is that procedures can modify input parameters.
Syntax:
  procedure read_v1d(file fname: in text; v: out std_logic_vector);
  a procedure that reads data from a file called fname.
Parameters can be of in, out, inout modes.
  default class is constant for input parameters.
  default class is variable for out and inout mode parameters.

## Slide 32: Procedures
Variables declared within a procedure are initialized in each call
Variables do not retain values across procedure calls.
Example:
entity CPU is port(write_data: out std_logic_vector(31 downto 0); ADDR: out std_logic_vector(2 downto 0); MemRead, MemWrite: out std_logic; read_data: in std_logic_vector(31 downto 0); S: in std_logic); end entity CPU;

## Slide 33: Example: CPU + Memory
architecture beh of CPU is
procedure mread( address: in std_logic_vector(2 downto 0); signal R: out std_logic; signal S: in std_logic; signal ADDR: out std_logic_vector(2 downto 0); signal data: out std_logic_vector(31 downto 0)) is
begin ADDR <= address; R <= ‘1’; wait until S = ‘1’; data <= read_data; R <= ‘0’; end procedure mread;
...
end architecture beh;

## Slide 34: Example: CPU + Memory
architecture beh of CPU is
...
procedure mwrite( address: in std_logic_vector(2 downto 0); signal data: in std_logic_vector(31 downto 0); signal ADDR: out std_logic_vector(2 downto 0); signal W: out std_logic; signal DO: out std_logic_vector(31 downto 0)) is
begin ADDR <= address; DO <= data; W <= ‘1’; wait until S = ‘1’; W <= ‘0’; end procedure mwrite;
...
end architecture beh;

## Slide 35: Example: CPU + Memory
architecture beh of CPU is
...
-- CPU description here begin process is begin
-- -- behavioral description -- end process; process is begin
-- -- behavioral description -- end process;
end architecture beh;

## Slide 36: Using Procedures
Signals can be passed to procedures and updated within procedures
Signals cannot be declared within procedures
Visibility rules apply here
  procedure can update signals visible to it even if these signals do not appear in the parameter list.
  This is sometimes called as side effect of procedure.
  updating signals that do not appear in the parameter list is a poor programming practice.
A process calling a procedure with a wait statement cannot have sensitivity list

## Slide 37: Concurrent vs. Sequential Procedure Calls
Concurrent procedure call
  procedure calls can be made in concurrent signal assignments
  execution of a procedure is concurrent with other concurrent procedures, CSA statements, or processes.
  The procedure is invoked when there is an event on a signal that is a parameter to the procedure.
  Parameter list cannot include a variable in a concurrent procedure call (shared variables can be included though).
Sequential procedure call
  executed within the body of a process.
  executions is determined by the order.

## Slide 38: Example: Concurrent Procedure Call
entity serial_adder is port(a, b, clk, reset: in std_logic; z: out std_logic); end entity; architecture structural of serial adder is component comb is port(a, b, c_in: in std_logic; z, carry: out std_logic); end component; procedure dff(signal d, clk, reset: in std_logic; signal q, qbar: out std_logic) is begin if(reset =‘0’) then q <= ‘0’ after 5 ns; qbar <= ‘1’ after 5 ns; elsif(rising_edge(clk)) then q <= d after 5 ns; qbar <= not d after 5 ns; end if; end procedure; signal s1, s2: std_logic;
begin C1: comb port(a=>a, b=>b, c_in=>s1, z=>z, carry=>s2);
dff(clk=>clk, reset=>reset, d=>s2, q=>s1, qbar=>open); end architecture structural;
behavioral
description
explicitly
associating
formal and
actual
parameters

## Slide 39: Example: Sequential Procedure Call
entity serial_adder is port(a, b, clk, reset: in std_logic; z: out std_logic); end entity; architecture structural of serial adder is component comb is port(a, b, c_in: in std_logic; z, carry: out std_logic); end component; procedure dff(signal d, clk, reset: in std_logic; signal q, qbar: out std_logic) is ...
end procedure; signal s1, s2: std_logic;
begin C1: comb port(a=>a, b=>b, c_in=>s1, z=>z, carry=>s2);
process begin
dff(clk=>clk, reset=>reset, d=>s2, q=>s1, qbar=>open); wait on clk, reset, s2; end process; end architecture structural;

## Slide 40: Synthesis & Procedures
In-lining approach
  during synthesis, the compiler replaces the procedure calls with the corresponding code (flattening)
  therefore, inferencing techniques are applicable
Latch inference
  local variables do not retain value across invocations; they will be synthesized into wires
  signals of mode out may infer latches.
  for example, if procedure resides in a conditional block of code, latches will be inferred for output signals of the procedure

## Slide 41: Synthesis & Procedures
Wait statements
  recall that synthesis compilers allows only one wait statement in a process.
  procedures that are being called within a process that has already a wait statement cannot have a wait statement of its own.
  Therefore, wait statements are generally not supported in procedures for synthesis.
For synchronous logic
  use if statements in the procedure

## Slide 42: Example
entity proc_call is port(data:in std_logic_vector(7 downto 0); count: out std_logic); end entity proc_call; architecture beh of proc_call is procedure ones(signal data: in std_logic_vector; signal count: out std_logic) is variable parity: std_logic:=‘0’; begin for i in data’range loop parity := parity xor data(i); end loop; count <= parity;
end procedure ones; begin ones(data, count); -- concurrent procedure call end architecture beh;

## Slide 43: Example

## Slide 44: Yet Another Example
entity proc_call is port(reset, clock: in std_logic; data:in std_logic_vector(7 downto 0); count: out std_logic); end entity proc_call; architecture beh of proc_call is procedure ones(signal data: in std_logic_vector; signal count: out std_logic) is variable parity: std_logic:=‘0’; begin for i in data’range loop parity := parity xor data(i); end loop; count <= parity;
end procedure ones; begin process(reset, clock) is begin if reset = ‘0’ and rising_edge(clock) then ones(data, count); end if; end process; end architecture beh;

## Slide 45: Yet Another Example

## Slide 46: Subprogram Overloading
Subprograms
  functions and procedures
Sometimes, it is convenient to have two or more subprograms with the same name
  function count (oranges: integer) return integer; function count (apples: bit) return integer;
  dff(clk, d, q, qbar); dff(clk, d, q, qbar, reset, clear);
In this case, subprograms are overloaded.
  compiler will decide which subprogram to call based on the number and type of arguments.
  and, or etc are overloaded in std_logic_1164 package.

## Slide 47: Operator Overloading
An operator that behaves different depending on the operands is said to be overloaded
  For example, “*” and “+” are defined for certain predefined types of the language such as integers.
  What if we want to use these operators to do multiplication and addition one data types we newly defined.
Example
  function “*” (arg1, arg2: std_logic_vector) return std_logic_vector;
  function “+” (arg1, arg2: signed) return signed;
  these examples are taken from std_logic_arith.vhd package.

## Slide 48: Operator Overloading
You can define a new multi-value logic and logic operations on the data of this new type. type MVL is (‘U’, ‘0’, ‘1’, ‘Z’); function “and” (L, R: MVL) return MVL; function “or” (L, R: MVL) return MVL; function “not” (R: MVL) return MVL;
Example: signal a, b, c: MVL; a <= ‘z’ or ‘1’; b <= “or”(‘0’, ‘1’); c <= (a or b) and (not c);

## Slide 49: Packages
A package provides a convenient mechanism to store items that can be shared across distinct VHDL programs:
  Those items are type definitions, functions, procedures, etc.
  We group logically related sets of functions and procedures into a package.
  When working with a large design project consisting of many small VHDL programs, it is convenient to have common procedures and functions in separate packages.
  For example, a package containing definition of new types for registers, instructions, memories, etc. will certainly be useful for microprocessor design.

## Slide 50: Package Declaration
Package declaration
  contains information about what is available in the package that we can use in our VHDL programs.
  In other words, it contains interface or specifications of the functions and procedures that are available in the package.
  For example,
  list of functions and procedures,
  what are the parameters they take
  the type of input parameters
  What it returns,
  what is the type of the returning value
  etc.

## Slide 51: Package Declaration: Syntax
package package-name is package-item-declarations  these may be: -- subprogram declarations -- type declarations -- subtype declarations -- constant declarations -- signal declarations -- variable declarations -- file declarations -- alias declarations -- component declarations -- attribute declarations -- attribute specifications -- disconnection specifications -- use clauses end [package] [package-name];

## Slide 52: Package Declaration: Example
package synthesis_pack is constant low2high: time := 20 ns; type alu_op is (add, sub, mul, div, eql); attribute pipeline: Boolean; type mvl is (‘U’, ‘0’, ‘1’, ‘Z’); type mvl_vector is array (natural range <>) of mvl; subtype my_alu_op is alu_op range add to div; component nand2 port(a, b: in mvl; c: out mvl); end component; end synthesis_pack;
Items declared in a package declaration can be accessed by other design units by using library and use clauses.
use work.synthesis_pack.all;

## Slide 53: Yet Another Example
use work.synthesis_pack.all; -- include all declarations -- from package synthesis_pack package program_pack is constant prop_delay: time; -- deferred constant function “and” (l, r: mvl) return mvl; procedure load (signal array_name: inout mvl_vector; start_bit, stop_bit, int_value: in integer); end_package program_pack;

## Slide 54: Package Declaration: std_logic_1164
package std_logic_1164 is type std_ulogic is (‘U’, ‘X’, ‘0’, ‘1’, ‘Z’, ‘W’, ‘L’, ‘H’ , ‘-’); type std_ulogic_vector is array (natural range <>) of std_ulogic; function resolved(s: std_ulogic_vector) return std_ulogic; subtype std_logic is resolved std_logic; type std_logic_vector is array (natural range <>) of std_logic; function “and”(l, r: std_logic_vector) return std_logic_vector; function “and”(l, r: std_ulogic_vector) return std_ulogic_vector; ... end package std_logic_1164;

## Slide 55: Package Body
It basically contains the code that implements the subprograms
Syntax:
package body package-name is package-body-item-declarations  These are: -- subprogram bodies -- complete constant declarations -- subprogram declarations -- type and subtype declarations -- file and alias declarations -- use clauses end [package body] [package-name];

## Slide 56: Package Body: Example
package body program_pack is use work.tables.all; constant prop_delay: time := 15 ns; function “and”(l, r: mvl) return mvl; begin return table_and(l, r); -- table_and is a 2-D constant defined in -- another package, called “tables” in the -- current working directory end “and”; procedure load(signal array_name: inout mvl_vector; start_bit, stop_bit, int_value: in integer) is begin -- procedure behavior here end load; end program_pack;

## Slide 57: Libraries
Design units (design files)
  entity declaration,
  architecture body,
  configuration declaration,
  package declaration,
  package body
Each design unit is analyzed (compiled) and placed in a design library.
  recall that libraries are generally implemented as directories and are referenced by a logical name.
  this logical name corresponds to physical path to the corresponding directory.

## Slide 58: Compilation Process
WORK
VHDL analyzer verify the syntactic and semantic correctness of the source
then compiles each design unit into an intermediate form.
Each intermediate form is stored in a design library called working library.
design file
VHDL
Analyzer
intermediate form
STD
IEEE
LIB1
design libraries

## Slide 59: Libraries: Visibility
Implicit visibility
  In VHDL, the libraries STD and WORK are implicitly declared.
Explicit visibility is achieved through
  library clause
  use clause
  Example: library IEEE; use IEEE.std_logic_1164.all;
Once a library is declared, all of the subprograms, type declarations in this library become visible to our programs through the use of use clause.

## Slide 60: Context Clauses
Examples for context clauses:
  library IEEE; use IEEE.std_logic_1164.all;
Context clauses only applies the following design entity
  if a file contains more than one entity, context clauses must precede each of them to provide the appropriate visibility to each design entity.

## Slide 61: How to Create a Library?

## Slide 62: How to Add Packages to a Library?

## Slide 63: Package Declaration
library IEEE;
use IEEE.std_logic_1164.all;
package my_pack_a is
subtype word is std_logic_vector(15 downto 0);
function "+" (op1, op2: word) return word;
function "-" (op1, op2: word) return word;
function "*" (op1, op2: word) return word;
end package my_pack_a;

## Slide 64: Package Body
library IEEE; use IEEE.std_logic_1164.all; use IEEE.std_logic_signed.all;
use IEEE.std_logic_arith.all;
package body my_pack_a is function "+" (op1, op2: word) return word is variable result: word; variable a, b, c: integer; begin a := conv_integer(op1); b := conv_integer(op2); c := a + b; result := conv_std_logic_vector(c, 16); return result; end function;
...
end package body my_pack_a;

## Slide 65: Package Body
...
function "-" (op1, op2: word) return word is variable result: word; variable a, b, c: integer; begin a := conv_integer(op1); b := conv_integer(op2);
c := a - b;
result := conv_std_logic_vector(c, 16);
return result;
end function; function "*" (op1, op2: word) return word is variable result: word; variable a, b, c: integer;
begin
a := conv_integer(op1);
b := conv_integer(op2);
c := a * b;
result := conv_std_logic_vector(c, 16);
return result;
end function;
end package body my_pack_a;

## Slide 66: Example using this Package
library IEEE;
library my_lib;
use IEEE.std_logic_1164.all;
use my_lib.my_pack_a.all;
entity aritmetik is
end entity;
architecture beh of aritmetik is
signal a, b, c: word;
begin
a <= x"abcd";
b <= x"1347";
c <= a + b;
end architecture beh;

## Slide 67: Simulation Results

## Slide 68: Summary
Hierarchy
Functions
Procedures
subprogram overloading
operator overloading
packages
libraries