## Slide 1: VHDL Introduction
EL 310
Erkay Savaş
Sabancı University

## Slide 2: What is VHDL ?
VHDL stands for VHSIC Hardware Description Language
VHSIC =Very High-Speed Integrated Circuit
Initialized by US DoD as a sponsored program
Standardized as IEEE 1076-1987 in 1987
Revised in 1993 (used in this course)
Other HDLs: Verilog and ABEL
DoD requires that VHDL descriptions be delivered for all ASICs.
every major CAD vendors supports VHDL

## Slide 3: VHDL Provides
Portability
Interoperability across vendors
Code reuse
Distributed design
Reliable design process
Minimized design time and cost

## Slide 4: Programming Languages vs. HDLs
Procedural programming languages (C or Pascal) typically provide procedures for
  Performing a computation (e.g. matrix multiplication)
  Manipulating data (e.g. sorting)
Hardware description language is used to describe a digital system
  Simulate the behavior of the system without actually constructing the system
  Synthesis compilers can use the description to actually build a digital system implementing this behavior
  VHDL is primarily used for digital system design

## Slide 5: Why Describing Systems ?
Design specification
  Unambiguous definition of components and interfaces in a large design.
Design Simulation
  Verify system/subsystem/chip performance prior to implementation
Design Synthesis
  Automated generation of hardware implementing the digital system

## Slide 6: Describing Digital System
Different levels of abstractions
Application Level
System Level
Architecture Level
Device or Circuit Level

## Slide 7: Design Flow:Top-down approach
Functional Design
Register Transfer Level Design
Logic Design
Circuit Design
Physical Design
Requirements
Description for Manufacture
Behavioral simulation
RTL Simulation Validation
Logic simulation, Verification Fault Simulation
Timing simulation Circuit Analysis
Design Rule Checking
Memory,
Adder etc.
transistor
gates
ASIC Design Process

## Slide 8: Levels of Abstraction
Design tools support to perform simulation at each level
  These simulations are for anticipating behavior, physical properties, and performance of the circuit
  Simulation at lower levels offers more accurate predictions, but takes longer.
  If design errors are discovered at lower levels, changes in the design to correct faults may be expensive longer development times
  Having simulation capability at different level helps detect and correct the design errors at earlier stages

## Slide 9: Synthesis Design Flow for FPGA
Functional Design
Register Transfer Level Design
Synthesis
Place and Route
Timing Extraction
Requirements
VHDL Model
VHDL Model
Behavioral Simulation
(VHDL)
More realistic timing values
Logic Simulation

## Slide 10: Need of Shorter Design Cycle?
Market Rise
Market Fall
The first 10%-20% of the design cycle can determine 70%-80% of final system cost.
5%-10% of design cycle is spent on studying and formulating requirements, whereas 70% of manufacturing costs are affected by customer requirements.
revenue
time
Maximum revenue
Revenue loss
delay

## Slide 11: The Role of HDL -1: Y-Chart
Point tools are good for a single aspect of design
Transfer information btw these tools is hard
Physical
Behavioral
Structural
processors
registers
gates
transistor
boards
chips
modules
cells
Algorithms
Register transfer
Boolean expressions
Transfer functions

## Slide 12: The Role of HDL - 2
Digital design is structured around a hierarchy of representations
HDLs can describe distinct aspects of a design at multiple levels of abstraction
Interoperability : tools that are designed for different aspects of design can transfer information to each other
Technology independence: a design environment that is independent of a particular target technology
  We do not have to describe a system at gate level

## Slide 13: The Role of HDL - 3
Timing analysis
  Prior to physical design, a detailed timing information can be extracted via simulation to ensure that performance requirements can be met.
Hardware/software co-design (or prototyping)
  simulate a processor architecture for functional accuracy so that application software developers can start coding before the actual chip is produced.
Design re-use
  Libraries of VHDL models of components
  They can be shared exactly as software libraries
  You can include a highly optimized component in your project

## Slide 14: Summary
HDL for describing digital systems
  specification
  simulation
  synthesis
Description at various levels of abstraction
  system, architectural, RTL, logic, gate, etc.
  VHDL integrates point tools into a cohesive design process
VHDL is independent of technology
faster time-to-market