## Slide 1: VHDL Complex Sequential Systems
EL 310
Erkay Savaş
Sabancı University

## Slide 2: Partitioned Design
Any synchronous sequential system could be described by an ASM chart.
It does not make much sense to design the whole system using a single ASM chart.
What makes the design process manageable is to partition the design in some way.
The most straightforward way to partition a design is to split it in two:
  datapath: consists of components that store and manipulate data
  control: can be designed as a state machine that controls functioning of those datapath components.

## Slide 3: Our Old Example
major=Green minor=Red
G
major=Red minor=Green
R
car
start_timer
timed
0
0
1
1
Major road
Minor road
sensor

## Slide 4: Our Old Example
Traffic light controller with a timer:
major=Green minor=Red
G
car
1
s0
s255
0
Assume that the clock frequency is such that the timed interval is completed in 256 clock cycles.
There is an abundance of states.
states from s0 to s255 map to a simple controller
we can just separate the traffic light controller from the timer.

## Slide 5: Linked ASM Charts
major=Green minor=Red
G
car
1
R
0
timed
1
0
start
IDLE
start
1
timed
0
s0
s255
Hardware subroutine model

## Slide 6: Alternative Linked ASM Chart
G
car
1
enable
R
0
timed
1
0
IDLE
enable
1
timed
0
s0
s255
enable
timed
1
0
A conventional counter

## Slide 7: Datapath/Controller Partitioning
In our previous example, the ASM chart in the right hand side is a simple 8-bit counter.
It would be more efficient to use an existing 8-bit controller instead of designing it using our ASM chart.
  Existing counter may correspond to an existing hardware or a VHDL model.
Then it is convenient to think of a sequential system in terms of
  the datapath whose components that have been previously designed (or can be adapted)
  the controller which is a design-specific state machine

## Slide 8: Datapath/Controller Partitioning
Controller
Datapath
Control Signals
Status Signals
System Inputs
System Outputs
clock, reset

## Slide 9: Datapath/Controller Partitioning
G
car
1
enable
R
0
timed
1
0
IDLE
enable
1
timed
0
s0
s255
enable
timed
1
0
Controller
Datapath

## Slide 10: Register Transfer Operations
The datapath would normally contain registers.
The functionality of the system can be described in terms of register transfer operations.
We can express register transfer operations in the extended ASM chart notation.
Z  1
The notation means that Z takes the value 1 at the end of the state indicated, and holds that value until it is set to another value or reset.

## Slide 11: Extended ASM Chart Notation
If Z is reset to 0 and it is only set to 1 in the present state, the registered output would be implemented as a flip-flop and a multiplexor.
Z  1
Z
1
ENABLE
clock
1
0
Z
1
clock
ENABLE
ENABLE

## Slide 12: A More Complex Example
B0  X0
B1  X1
B2  X2
A
B0 0
B1  B0
B2  B1
B0  B0  B1
B1  B1  B2
B2  B2·B1·B0
X0
B0  B1
B1  B2
B2  0
0
1
1
0
00
01
10
11

## Slide 13: Implementation of Controller
Next state equations for the controller

## Slide 14: Implementation of Datapath
0
1
2
3
0
1
2
3
0
1
2
3
S1S0
S1S0
S1S0
D
D
D
Q
Q
Q
B2
B1
B0
X2
X1
X0
&


0
0
clock

## Slide 15: A Simple Microprocessor Design
High level language expressions
Assembler instructions
Machine instructions.
  8, 16, 32-bit numbers
Example: 8-bit processor (opcode three bits, operands are five bits)
  a = b + c; translated into
  LOAD b 00000001
  ADD c 01000010
  STORE a 00100011

## Slide 16: A Simple Microprocessor Design
Example
  opcode LOAD 000 ADD 010 STORE 001
  addresses a 00001 b 00010 c 00011
Datapath/controller partition
controller (a.k.a. sequencer) is a state machine.
Bits of the opcode are input to the controller
  the opcode may be decoded to generate a larger set of inputs to the controller (micro-coding approach)

## Slide 17: A Simple Microprocessor Design
In our instructions,
  first three bits are the opcode
  the remaining five bits are the address
  direct addressing mode.
Other addressing mode (immediate)
  a = b + 5;
  LOAD b ADD #5 STORE a
  The opcodes for direct add and immediate add will be different.
  Controller will go through different states when executing these two instructions

## Slide 18: Designing the Simple Microprocessor
Design approach
  Partition the design into datapath and controller
8-bit microprocessor
  datapath components and bus are all 8-bit wide.
Features
  A single bus
  Each component uses a three-state buffers so that only one component is attempting to drive the bus.
  Fully synchronous with a single clock
  a synchronous reset

## Slide 19: Block Diagram of the Processor
Control Signals
IR
PC
ACC
Flags
RAM
MDR
MAR
Controller
opcode

## Slide 20: Inside the CPU
Memory
  Main memory is commonly implemented as asynchronous SRAM.
  Synchronous registers act as buffers between the main memory and the CPU.
    Memory Address Register (MAR)
    Memory Data Register (MDR)
Arithmetic Logic Unit
  performs operation such as add, sub, and, or, etc.
  combinational
  One input is the ACC and the other is the bus.

## Slide 21: Inside the CPU
ALU (cont.)
  It usually has other outputs called flags (for testing overflow, zero result, etc).
  Flags act as inputs to the controller (status signals)
ACC (accumulator)
  a synchronous register
  It always acts as one of the source and destination registers.
PC (program counter)
  Instructions in a program are held sequentially in memory
  The PC register holds the address of the current instruction to be executed

## Slide 22: Inside the CPU
PC (cont.)
  The content of PC is automatically updated.
  It must also be possible to load a new address in case of branch and jump instructions.
IR (instruction register)
  The instruction to be executed is read from the memory
  IR holds the current instruction during the execution of it.
  bits of opcode (operation code ) field of the instruction are input to the controller.

## Slide 23: Controller (Sequencer)
Perform a subtract operation in the ALU
ALU_sub
Perform an add operation in the ALU
ALU_add
Read, Not Write. When false, contents of MDR are stored in memory
R_NW
Chip Select. Use contents of MAR to set up memory address
CS
drive bus with operand part of instruction held in IR
Addr_bus
Increment PC and save the result in PC
INC_PC
Load ACC with result from ALU
ALU_ACC
load MDR from bus
load_MDR
drive bus with contents of MDR
MDR_bus
load MAR from bus
load_MAR
load IR from bus
load_IR
drive bus with contents of PC
PC_bus
load ACC from bus
load_ACC
drive bus with contents of ACC (enable three-state output)
ACC_bus
Explanation
Control signal

## Slide 24: Reminder: Block Diagram of the Processor
PC
IR
Controller
Control Signals
ACC
Flags
RAM
MDR
MDR
opcode

## Slide 25: ASM Chart for the Controller
MAR PC
PC  PC+1
s0
CS
R_NW
s1
IRMDR
s2
op=store
MARAddr
s3
CS
s5
op=load
op=add
Fetch
MDRACC
s4
1
ACC  MDR
s7
1
ACC MDR + ACC
1
CS
R_NW
s6
0
s8
0
ACC MDR - ACC
0
Execute

## Slide 26: ASM Chart with Control Signals
PC_bus
Load_MAR INC_PC
s0
CS
R_NW
s1
MDR_bus
load_IR
s2
op=store
Addr_bus load_MAR
s3
CS
s5
op=load
op=add
Fetch
ACC_bus load_MDR
s4
1
MDR_bus load_ACC
s7
1
ALU_add
1
CS
R_NW
s6
0
ALU_sub
0
Execute
MDR_bus ALU_ACC
0
s8

## Slide 27: ASM Chart with Branching
op=load
op=add
ACC MDR + ACC
1
CS
R_NW
s6
s8
0
ACC MDR - ACC
0
ACC  MDR
s7
1
op=bne
0
z_flag
PC  MDR
s9
1
0

## Slide 28: Reminder: Block Diagram of the Processor
PC
IR
Controller
Control Signals
ACC
Flags
RAM
MDR
MDR
opcode

## Slide 29: Methods to Synthesize Bus
library IEEE;
use IEEE.std_logic_1164.all;
entity multiplexor is
port(a, b, c, d, e: in std_ulogic;
s: in std_ulogic_vector(4 downto 0);
y: out std_ulogic);
end entity multiplexor;
Recall that tri-state buffers are used for constructing busses.
The following method can be used with Xilinx FPGA; but not with Actel FPGA since this technology does not support three-state logic.

## Slide 30: Methods to Synthesize Bus
architecture version1 of multiplexor is
begin p0: process(s, a, b, c, d, e) is begin case s is when "00001" => y <= a; when "00010" => y <= b; when "00100" => y <= c; when "01000" => y <= d; when others => y <= e; end case; end process p0; end architecture version1;
architecture version2 of multiplexor is begin y <= a when s(0) = '1' else 'Z'; y <= b when s(1) = '1' else 'Z'; y <= c when s(2) = '1' else 'Z'; y <= d when s(3) = '1' else 'Z'; y <= e when s(4) = '1' else 'Z'; end architecture version2;

## Slide 31: Synthesis Results with SinplifyPro
Version 1 Architecture

## Slide 32: Synthesis Results with SinplifyPro
Version 2 Architecture
three–state buffers

## Slide 33: Synthesis Results with Synopsys

## Slide 34: VHDL Model: Package Declaration
library ieee; use ieee.std_logic_1164.all;
package cpu_defs is type opcode is (load, store, add, sub, bne); constant word_w: natural := 8; -- # of bits for bus constant op_w: natural := 3; -- # of bits for opcode constant rfill: std_ulogic_vector(op_w-1 downto 0):= (others => ‘0’); -- padding for address
-- two functions to do conversion between opcode bits of -- std_ulogic_vector and opcode type
function slv2op (slv: in std_ulogic_vector) return opcode; function op2slv (op: in opcode) return std_ulogic_vector;
end package cpu_defs;
package body cpu_defs is ...

## Slide 35: VHDL Model: Package Body
... package body cpu_defs is type optable is array(opcode) of std_ulogic_vector(op_w – 1 downto 0);
constant trans_table: optable := (“000”, “001”, “010”, “011”, “100”);
function op2slv (op: in opcode) return std_ulogic_vector is begin return trans_table(op); end function op2slv;
function slv2op (slv: in std_ulogic_vector) return opcode is begin
...
end function slv2op;
end package body cpu_defs;

## Slide 36: VHDL Model: Package Body
... package body cpu_defs is ...
function slv2op (slv: in std_ulogic_vector) return opcode is
variable transop: opcode; begin -- this is how it should be done, but some synthesis -- tools may not support it. for i in opcode loop if slv = trans_table(i) then transop := i; end if; end loop;
end function slv2op;
end package body cpu_defs;

## Slide 37: VHDL Model: Package Body
... package body cpu_defs is ...
function slv2op (slv: in std_ulogic_vector) return opcode is
variable transop: opcode; begin -- this is a less elegant method;
-- if the definitions of the opcode and/or trans_table are -- changed, then this code also has to be changed. -- There is therefore potential for inconsistency case slv is when “000” => transop := load; when “001” => transop := store; when “010” => transop := add; when “011” => transop := sub; when “100” => transop := bne; end case;
return transop;
end function slv2op;
end package body cpu_defs;

## Slide 38: Controller: Entity Declaration
library ieee; use ieee.std_logic_1164.all; use work.cpu_defs.all;
entity controller is port(clock, reset: in std_logic;
op: in opcode;
z_flag: in std_ulogic; -- status signal
ACC_bus, load_ACC, PC_bus, load_PC,
load_IR, load_MAR, MDR_bus, load_MDR,
ALU_ACC, ALU_add, ALU_sub, INC_PC,
Addr_bus, CS, R_NW: out std_ulogic);
end entity controller;
architecture rtl of controller is ... end architecture rtl;

## Slide 39: Controller: Sequential Part
architecture rtl of controller is
type state is (s0, s1, s2, s3, s4, s5, s6, s7, s8, s9);
signal present_state, next_state: state;
begin
seq: process(clock, reset) is
begin
if reset = ‘1’ then
present_state <= s0;
elsif rising_edge(clock) then
preset_state <= next_state;
end if;
end process seq;
... end architecture rtl;

## Slide 40: Controller: Combinational Part
...
comm: process(present_state, op, z_flag) is begin -- reset all the control signals to a default
ACC_bus <= ‘0’; load_ACC <= ‘0’; PC_bus <= ‘0’; load_PC <= ‘0’; load_IR <= ‘0’; load_MAR <= ‘0’; MDR_bus <= ‘0’; load_MDR <= ‘0’; ALU_ACC <= ‘0’; ALU_add <= ‘0’; ALU_sub <= ‘0’; INC_PC <= ‘0’; Addr_bus <= ‘0’; CS <= ‘0’; R_NW <= ‘0’; ... end process com;
end architecture rtl;

## Slide 41: Controller: Combinational Part
...
comm: process(present_state, op, z_flag) is begin
... case present_state is
when s0 => -- current inst address to be loaded in -- MAR, PC incremented, etc.
PC_bus <= ‘1’;
load_MAR <= ‘1’;
INC_PC <= ‘1’; load_PC <= ‘1’;
next_state <= s1;
... end case; end process com;
end architecture rtl;

## Slide 42: Controller: Combinational Part
...
comm: process(present_state, op, z_flag) is begin
... case present_state is
...
when s1 => -- memory is read, MDR contains the inst.
CS <= ‘1’;
R_NW <= ‘1’;
next_state <= s2;
when s2 => -- inst. transferred from MDR to IR
MDR_bus <= ‘1’;
load_IR <= ‘1’;
next_state <= s3;
... end case; end process com;
end architecture rtl;

## Slide 43: Controller: Combinational Part
...
comm: process(present_state, op, z_flag) is begin
... case present_state is
...
when s3 => -- direct address to be loaded in MAR
Addr_bus <= ‘1’;
load_MAR <= ‘1’;
if op = store then next_state <= s4; else next_state <= s6;
end if;
... end case; end process com;
end architecture rtl;

## Slide 44: Controller: Combinational Part
...
comm: process(present_state, op, z_flag) is begin
... case present_state is
...
when s4 => -- store (memory to be written)
ACC_bus <= ‘1’;
load_MDR <= ‘1’;
next_state <= s5;
when s5 => -- select memory to write it with MDR
CS <= ‘1’;
next_state <= s0;
... end case; end process com;
end architecture rtl;

## Slide 45: Controller: Combinational Part
...
comm: process(present_state, op, z_flag) is begin
... case present_state is
...
when s6 =>
CS <= '1'; R_NW <= '1'; -- read the memory just in case
if op = load then next_state <= s7;
else
if op = bne then
if z_flag = '1' then next_state <= s9; -- taken
else next_state <= s0; -- not taken
end if;
else next_state <= s8; -- not a branch
end if;
end if;
... end case; end process com;
end architecture rtl;

## Slide 46: Controller: Combinational Part
...
comm: process(present_state, op, z_flag) is begin
... case present_state is
...
when s7 => -- load instruction
MDR_bus <= ‘1’; -- ACC gets content of MDR
load_ACC <= ‘1’;
next_state <= s0;
... end case; end process com;
end architecture rtl;

## Slide 47: Controller: Combinational Part
...
comm: process(present_state, op, z_flag) is begin
... case present_state is
...
when s8 => -- ALU operation
MDR_bus <= ‘1’; -- one operand from MDR
ALU_ACC <= ‘1’; -- the other from ACC if op = add then ALU_add <= ‘1’; elsif op = sub then
ALU_sub <= ‘1’;
end if;
next_state <= s0;
... end case; end process com;
end architecture rtl;

## Slide 48: Controller: Combinational Part
...
comm: process(present_state, op, z_flag) is begin
... case present_state is
...
when s9 => -- completing the branch instruction
MDR_bus <= ‘1’;
load_PC <= ‘1’;
next_state <= s0; end case; end process com;
end architecture rtl;

## Slide 49: IEEE.NUMERIC_STD Package
-- Library : This package shall be compiled into a library symbolically
-- : named IEEE.
-- :
-- Developers : IEEE DASC Synthesis Working Group, PAR 1076.3
-- :
-- Purpose : This package defines numeric types and arithmetic functions
-- : for use with synthesis tools. Two numeric types are defined:
-- : --> UNSIGNED : represents unsigned number in vector form
-- : --> SIGNED : represents a signed number in vector form
-- : The base element type is type STD_LOGIC.
-- : The leftmost bit is treated as the most significant bit.
-- : Signed numbers are represented in two's complement form.
-- : This package contains overloaded arithmetic operators on
-- : the SIGNED and UNSIGNED types. The package also contains
-- : useful type conversions functions.
-- :
-- : If any argument to a function is a null array, a null array is
-- : returned (exceptions, if any, are noted individually).

## Slide 50: Datapath Design: ALU
library ieee; use ieee.std_logic_1164.all;
use ieee.numeric_std.all; use work.cpu_defs.all;
entity ALU is port (clock, reset: in std_ulogic; ACC_bus, load_ACC, ALU_ACC, ALU_add, ALU_sub: in std_ulogic;
system_bus: inout std_ulogic_vector(word_w-1 downto 0); z_flag: out std_ulogic);
end entity ALU;
architecture rtl of ALU is
...
end architecture rtl;

## Slide 51: Datapath Design: ALU
architecture rtl of ALU is
signal acc: unsigned(word_w-1 downto 0);
constant zero: unsigned(word_w-1 downto 0) := (others => ‘0’);
begin system_bus <= std_ulogic_vector(acc) when ACC_bus = ‘1’
else (others => ‘Z’);
z_flag <= ‘1’ when acc = zero else ‘0’;
process(clock, reset) is begin
...
end process;
end architecture rtl;

## Slide 52: Datapath Design: ALU
architecture rtl of ALU is
...
process(clock, reset) is begin
if reset = ‘1’ then acc <= (others => ‘0’);
elsif rising_edge(clock) then
if ALU_ACC = ‘1’ then
if ALU_add = ‘1’ then acc <= acc + unsigned(system_bus);
elsif ALU_sub = ‘1’ then acc <= acc - unsigned(system_bus);
end if;
elsif load_ACC = ‘1’ then acc <= unsigned(system_bus);
end if;
end if;
end process
end architecture rtl;

## Slide 53: Datapath Design: PC
library ieee; use ieee.std_logic_1164.all;
use ieee.numeric_std.all; use work.cpu_defs.all;
entity PC is port (clock, reset: in std_ulogic; PC_bus, load_PC, INC_PC: in std_ulogic;
system_bus: inout std_ulogic_vector(word_w-1 downto 0));
end entity PC;
architecture rtl of PC is
...
end architecture rtl;

## Slide 54: Datapath Design: PC
architecture rtl of PC is
signal count: unsigned (word_w – op_w – 1 downto 0);
begin system_bus <= refill & std_ulogic_vector(count)
when PC_bus = ‘1’ else (others => ‘Z’);
process (clock, reset) is begin if reset = ‘1’ then count <= (others => ‘0’); elsif rising_edge(clock) then if load_PC = ‘1’ then if INC_PC = ‘1’ then count <= count + 1; else count <= unsigned(system_bus(word_w-op_w-1 downto 0);
end if; end if;
end if;
end process;
end architecture rtl;

## Slide 55: Datapath Design: IR
library ieee; use ieee.std_logic_1164.all; use work.cpu_defs.all;
entity IR is port (clock, reset: in std_ulogic; Addr_bus, load_IR: in std_ulogic;
system_bus: inout std_ulogic_vector(word_w-1 downto 0); op: out opcode);
end entity IR;
architecture rtl of IR is
...
end architecture rtl;

## Slide 56: Datapath Design: IR
architecture rtl of IR is
signal instr_reg: std_ulogic_vector(word_w – 1 downto 0);
begin
system_bus <= refill & instr_reg(word_w-op_w-1 downto 0)
when Addr_bus = ‘1’ else (others => ‘Z’);
op <= slv2op(instr_reg(word_w – 1 downto word_w – op_w));
process(clock, reset)
begin
if reset = ‘1’ then instr_reg <= (others => ‘0’); elsif rising_edge(clock) then if load_IR = ‘1’ then instr_reg <= system_bus; end if;
end process;
end architecture rtl;

## Slide 57: Datapath Design: RAM
library ieee; use ieee.std_logic_1164.all;
use ieee.numeric_std.all; use work.cpu_defs.all;
entity RAM is port (clock, reset: in std_ulogic; MDR_bus, load_MDR, load_MAR, CS, R_NW: in std_ulogic;
system_bus: inout std_ulogic_vector(word_w-1 downto 0));
end entity RAM;
architecture rtl of RAM is
...
end architecture rtl;

## Slide 58: Datapath Design: RAM
architecture rtl of RAM is
signal mdr: std_ulogic_vector(word_w-1 downto 0);
signal mar: std_ulogic_vector(word_w – op_w -1 downto 0);
begin system_bus <= mdr when MDR_bus = ‘1’ else (others => ‘Z’);
process (clock, reset) is
type mem_array is array(0 to 2**(word_w-op_w-1) of std_ulogic_vector(word_w-1 downto 0);
variable mem: mem_array;
...
end process;
end architecture rtl;

## Slide 59: Datapath Design: RAM
...
process (clock, reset) is
type mem_array is array(0 to 2**(word_w-op_w-1) of std_ulogic_vector(word_w-1 downto 0);
variable mem: mem_array;
constant prog: mem_array := ( 0 => op2slv(load)& std_ulogic_vector(to_unsigned(4, word_w - op_w)),
1 => op2slv(add)& std_ulogic_vector(to_unsigned(5, word_w - op_w)),
2 => op2slv(store)& std_ulogic_vector(to_unsigned(6, word_w-op_w)),
3 => op2slv(bne)& std_ulogic_vector(to_unsigned(7, word_w-op_w)),
4 => std_ulogic_vector(to_unsigned(2, word_w)),
5 => std_ulogic_vector(to_unsigned(3, word_w)),
others => (others => ‘0’));
...
end process;
end architecture rtl;

## Slide 60: Datapath Design: RAM
...
process (clock, reset) is
begin
if reset = ‘1’ then
mdr <= (others => ‘0’);
mar <= (others => ‘0’);
mem <= prog;
elsif rising_edge(clock) then
... end if;
end process;
end architecture rtl;

## Slide 61: Datapath Design: RAM
process (clock, reset) is
begin
...
elsif rising_edge(clock) then
if load_MAR = ‘1’ then
mar <= unsigned(system_bus(word_w-op_w-1 downto 0));
elsif load_MDR = ‘1’ then
mdr <= system_bus;
elsif CS = ‘1’ then
if R_NW then mdr <= mem(to_integer(mar));
else mem(to_integer(mar)) := mdr;
end if;
end if; end if;
end process;
end architecture rtl;

## Slide 62: Putting Everything Together
Structural Modeling
  Components can be put together by instantiating them.
Issues
  system bus must be resolved at this level
  it must be declared with the type std_logic_vector.
  system bus is chosen to be treated as a port; it could have been a signal
  Type conversion during instantiation
  if the port is an input (mode in) x => to_bit(y) where x is of type bit while y is of type std_ulogic.

## Slide 63: Putting Everything Together
Type conversion during instantiation
  if the port is an output (mode out) to_std_ulogic(x) => y
  simply means that x is converted to std_ulogic
  before being assigned to y.
  if the port is bidirectional (mode inout) to_std_ulogic(x) => to_bit(y)

## Slide 64: CPU: Entity
library ieee; use ieee.std_logic_1164.all; use work.cpu_defs.all;
entity CPU is port (clock, reset: in std_ulogic; system_bus: inout std_logic_vector(word_w-1 downto 0));
end entity CPU;
architecture top of CPU is
...
end architecture CPU;

## Slide 65: CPU: Architecture
architecture top of CPU is
component controller is port(clock, reset: in std_logic;
op: in opcode;
z_flag: in std_ulogic;
ACC_bus, load_ACC, PC_bus, load_PC,
load_IR, load_MAR, MDR_bus, load_MDR,
ALU_ACC, ALU_add, ALU_sub, INC_PC,
Addr_bus, CS, R_NW: out std_ulogic);
end component controller;
component IR is port (clock, reset: in std_ulogic; Addr_bus, load_IR: in std_ulogic;
system_bus: inout std_ulogic_vector(word_w-1 downto 0); op: out opcode);
end component IR;
...
end architecture CPU;

## Slide 66: CPU: Architecture
architecture top of CPU is
...
component PC is port (clock, reset: in std_ulogic; PC_bus, load_PC, INC_PC: in std_ulogic;
system_bus: inout std_ulogic_vector(word_w-1 downto 0));
end component PC;
component RAM is port (clock, reset: in std_ulogic; MDR_bus, load_MDR, load_MAR, CS, R_NW: in std_ulogic;
system_bus: inout std_ulogic_vector(word_w-1 downto 0));
end component RAM;
...
end architecture CPU;

## Slide 67: CPU: Architecture
architecture top of CPU is
...
component ALU is port (clock, reset: in std_ulogic; ACC_bus, load_ACC, ALU_ACC, ALU_add, ALU_sub: in std_ulogic;
system_bus: inout std_ulogic_vector(word_w-1 downto 0); z_flag: out std_ulogic);
end component ALU;
signal ACC_bus, load_ACC, PC_bus, load_PC, load_IR, load_MAR, MDR,bus, load_MDR, ALU_ACC, ALU_add, ALU_sub, INC_PC, Addr_bus, CS, R_NW: std_ulogic;
signal z_flag: std_ulogic;
signal op: opcode;
begin
...
end architecture CPU;

## Slide 68: CPU: Architecture
architecture top of CPU is
...
begin
CNTRL1: controller port map(
clock => clock, reset => reset, op => op,
z_flag => z_flag, ACC_bus => ACC_bus,
load_ACC => load_ACC, PC_bus => PC_bus,
load_PC => load_PC, load_IR => load_IR,
load_MAR => load_MAR, MDR_bus => MDR_bus,
load_MDR => load_MDR, ALU_ACC => ALU_ACC,
ALU_add => ALU_add, ALU_sub => ALU_sub,
INC_PC => INC_PC, Addr_bus => Addr_bus,
CS => CS, R_NW => R_NW);
...
end architecture CPU;

## Slide 69: CPU: Architecture
architecture top of CPU is
...
begin
I1: IR port map(
clock => clock, reset => reset, Addr_bus => Addr_bus,
load_IR => load_IR, op => op,
std_logic_vector(system_bus) => std_ulogic_vector(system_bus));
P1: PC port map(
clock => clock, reset => reset, PC_bus => PC_bus,
load_PC => load_PC, INC_PC => INC_PC,
std_logic_vector(system_bus) => std_ulogic_vector(system_bus));
...
end architecture CPU;

## Slide 70: CPU: Architecture
architecture top of CPU is
...
begin
A1: ALU port map(
clock => clock, reset => reset, ACC_bus => ACC_bus,
load_ACC => load_ACC, ALU_add => ALU_Add,
ALU_sub => ALU_sub,
std_logic_vector(system_bus) => std_ulogic_vector(system_bus),
z_flag => z_flag);
R1: RAM port map(
clock => clock, reset => reset, MDR_bus => MDR_bus,
load_MDR => load_MDR, load_MAR => load_MAR,
CS => CS, R_NW => R_NW,
std_logic_vector(system_bus) => std_ulogic_vector(system_bus));
end architecture CPU;

## Slide 71: A Simple Testbench
library ieee; use ieee.std_logic_1164.all; use work.cpu_defs.all;
entity test_cpu is
end entity cpu;
architecture tb of testcpu is
component CPU is port (clock, reset: in std_ulogic; system_bus: inout std_logic_vector(word_w-1 downto 0));
end component CPU;
...
end architecture tb;

## Slide 72: A Simple Testbench
architecture tb of testcpu is
component CPU is port (clock, reset: in std_ulogic; system_bus: inout std_logic_vector(word_w-1 downto 0));
end component CPU;
signal clock, reset: std_ulogic := ’0’;
signal system_bus: std_logic_vector(word_w – 1 downto 0);
begin
C1: CPU port map (clock, reset, system_bus);
reset <= ‘1’ after 1 ns, ‘0’ after 2 ns;
clock <= not clock after 10 ns;
end architecture tb;

## Slide 73: Configuration Unit
configuration mapping of testcpu is
for tb
for C1: CPU use entity work.cpu(top);
for top
for CNTRL1: Controller use entity work.controller(rtl); end for;
for I1: IR use entity work.ir(rtl); end for;
for P1: PC use entity work.pc(rtl); end for;
for A1: ALU use entity work.alu(rtl); end for;
for R1: RAM use entity work.ram(rtl); end for;
end for;
end for;
end for;
end configuration mapping;