## Slide 1: VHDL Memory Models
EL 310
Erkay Savaş
Sabancı University

## Slide 2: ROM
library ieee; use ieee.std_logic_1164.all;
entity rom16x8 is port(address: in integer range 0 to 15; data: out std_ulogic_vector(7 downto 0)); end entity;
architecture sevenseg of rom16x8 is type rom_array is array (0 to 15) of std_ulogic_vector (7 downto 0);
constant rom: rom_array := ( “11111011”, “00010010”, “10011011”, “10010011”, “01011011”, “00111010”, “11111011”, “00010010”, “10100011”, “10011010”, “01111011”, “00010010”, “10101001”, “00110110”, “11011011”, “01010010”);
begin
data <= rom(address);
end architecture;

## Slide 3: Static RAM
Static RAM
2n word of
m bits
n
m
CS’
OE’
WE’
Address
Data input/output
CS’ - when asserted low, memory read and write operations are possible.
OE’ - when asserted low, memory output is enabled onto an external bus
WE’ - when asserted low, memory can be written

## Slide 4: A Cell of Static RAM
The RAM contains address decoders and a memory array.
A cell of RAM that stores one bit of data
D
G
Q
data_out
data_in
SEL’
WR’
Read mode: SEL’ = ‘0’ and WR’ = ‘1’, (G=‘0’) and data_out = Q
Write mode: SEL’ = ‘0’ and WR’ = ‘0’, (G=‘1’) and Q = data_in
When SEL’ = ‘1’ or WR’ = ‘1’, the data is stored in the latch
When SEL’ = ‘1’, data_out = ‘Z’

## Slide 5: Truth Table of Static RAM
CS’ | OE’ | WE’ | Mode | I/O pins
H | X | X | not selected | high-Z
L | H | H | output disabled | high-Z
L | L | H | read | data_out
L | X | L | write | data_in

## Slide 6: 6116 Static CMOS RAM
Memory Matrix
128 x 128
Row
Decoder
Column I/O
Column Decoder
input
data
control
A10
A4
A3
A2
A1
A0
I/O7
I/O0
OE’
WE’
CS’

## Slide 7: Read Cycle Timing I
tRC
Adress
dout
previous data valid
data valid
tOH
tAA
tOH
CS’ = 0, OE’ = 0 WE’ = 1
After the address changes, the old data remains at the output for a time tOH
Then there is a transition period during which the data may change (cross-hatching section)
The new data is stable at the memory after the address access time tAA
The address must be stable for the read cycle time, tRC

## Slide 8: Read Cycle Timing II
CS’
dout
data valid
tCLZ
tACS
tCHZ
Address is stable, OE’ = 0, WE’ = 1

## Slide 9: WE’ Controlled Write Cycle Time (OE’ = 0).
address
CS’
tWC
CS’ goes low before or at the same time as WE’ goes low
WE’ goes high before or at the same time as CS’ goes high
tCW
tWR
WE’
tAS
tWP
tAW
dout
tWHZ
tOW
din
tDW
valid data
tDH

## Slide 10: CS’ controlled write cycle time (OE’ = 0).
Adress
CS’
tWC
WE’ goes low before or at the same time as CS’ goes low
CS’ goes high before or at the same time as WE’ goes high
tCW
tWR
WE’
tAS
tAW
dout
din
tDW
new data
tDH
high - Z
old data or high-Z

## Slide 11: Writing to the Memory
In both CS’ and WE’ controlled write cycles, writing to memory occurs when both CS’ and WE’ are low,
writing is completed when either one of these signals goes high.

## Slide 12: Timing Specifications for CMOS SRAM
Parameter | Symbol | 61162-2 |  | 43258A-25 | 
 |  | min | max | min | max
Read Cycle Time | tRC | 120 | - | 25 | -
Address Access Time | tAA | - | 120 | - | 25
Chip Select Access Time | tACS | - | 120 | - | 25
Chip selection to output in low-Z | tCLZ | 10 | - | 3 | -
Output enable to output valid | tOE | - | 80 | - | 12
Output enable to output in low-Z | tOLZ | 10 | - | 0 | -
Chip de-selection to output in high-Z | tCHZ | 10 | 40 | 3 | 10
Chip disable to output in high-Z | tOHZ | 10 | 40 | 3 | 10
Output hold from address change | tOH | 10 | - | 3 | -

## Slide 13: Timing Specifications for CMOS SRAM
Parameter | Symbol | 61162-2 |  | 43258A-25 | 
 |  | min | max | min | max
Write Cycle Time | tWC | 120 | - | 25 | -
Chip selection to end of write | tCW | 70 | - | 15 | -
Address valid to end of write | tAW | 105 | - | 15 | -
Address setup time | tAS | 0 | - | 0 | -
Write pulse width | tWP | 70 | - | 15 | -
Write recovery time | tWR | 0 | - | 0 | -
Write enable to output in high-Z | tWHZ | 10 | 35 | 3 | 10
Data valid to end of write | tDW | 35 | - | 12 | -
Data hold from end of write | tDH | 0 | - | 0 | -
Output active from end of write | tOW | 10 | - | 0 | -

## Slide 14: Simple Memory Model
library ieee; use ieee.std_logic_1164.all;
use ieee.std_logic_arith.all;
entity ram6116 is port(address: in unsigned(7 downto 0); data: inout std_logic_vector(7 downto 0); WE_b, CS_b, OE_b: in std_ulogic);
end entity ram6116;

## Slide 15: Simple Memory Model
architecture simple_ram of ram6116 is type ram_type is array (0 to 2**8-1) of std_logic_vector(7 downto 0);
signal ram1: ram_type:= (others => (others => ’0’));
begin
process
begin
data <= (others => ‘Z’); -- chip is not selected
if (CS_b = ‘0’) then
if rising_edge(WE_b) then -- write
ram1(conv_integer(address’delayed)) <= data; wait for 0 ns;
end if;
if WE_b = ‘1’ and OE_b = ‘0’ then -- read
data <= ram1(conv_integer(address));
else
data <= (others => ‘Z’); end if;
end if;
wait on WE_b, CS_b, OE_b, address;
end process; end simple_ram;

## Slide 16: Synthesizeable Memory Model
architecture simple_ram of ram6116 is type ram_type is array (0 to 2**8) of std_logic_vector(7 downto 0);
signal ram1: ram_type;
begin
process (address, CS_b, WE_b, OE_b) is
begin
data <= (others => ‘Z’); -- chip is not selected
if (CS_b = ‘0’) then
if WE_b = ‘0’ then -- write
ram1(conv_integer(address)) <= data; end if;
if WE_b = ‘1’ and OE_b = ‘0’ then -- read
data <= ram1(conv_integer(address));
else
data <= (others => ‘Z’); end if;
end if;
end process;
end simple_ram;

## Slide 17: Timing Model for SRAM I
library ieee; use ieee.std_logic_1164.all;
use ieee.std_logic_arith.all;
entity ram6116 is
generic (constant t_AA: Time := 120 ns; constant t_ACS: Time := 120 ns; constant t_CLZ: Time := 10 ns; constant t_CHZ: Time := 10 ns; constant t_OH: Time := 10 ns; constant t_WC: Time := 120 ns; constant t_AW: Time := 105 ns; constant t_WP: Time := 70 ns; constant t_WHZ: Time := 35 ns; constant t_DW: Time := 35 ns; constant t_DH: Time := 0 ns; constant t_OW: Time := 10 ns);
port(address: in unsigned(7 downto 0); data: inout std_logic_vector(7 downto 0); WE_b, CS_b, OE_b: in std_ulogic);
end entity ram6116;

## Slide 18: Timing Model for SRAM II
architecture SRAM of ram6116 is type ram_type is array(0 to 2**8) of std_logic_vector(7 downto 0); signal ram1: ram_type := (others => (others => ‘0’));
begin ram: process begin
if (rising_edge(WE_b) and CS_b’delayed = ‘0’) or (rising_edge(CS_b) and WE_b’delayed = ‘0’) then -- write
ram1(conv_integer(address’delayed)) <= data’delayed;
-- data’delayed is the value of data just before the falling_edge
data <= transport data’delayed after t_OW;
end if;
if (falling_edge(WE_b) and CS_b = ‘0’) then –- enter write mode data <= transport “ZZZZZZZZ” after t_WHZ;
end if;

## Slide 19: Timing Model for SRAM III
architecture SRAM of ram6116 is ... begin ram: process begin ...
if CS_b’event and OE_b = ‘0’ then
if CS_b = ‘1’ then -- RAM is de-selected data <= transport “ZZZZZZZZ” after t_CHZ;
elsif WE_b = ‘1’ then –- read data <= “XXXXXXXX” after t_CLZ; data <= transport ram1((conv_integer(address)) after t_ACS; end if; end if;
if address’event and CS_b = ‘0’ and OE_b = ‘0’ and WE_b = ‘1’ then data <= “XXXXXXXX” after t_OH; data <= transport ram1(conv_integer(address)) after t_AA;
end if;
wait on CS_b, WE_b, address;
end process RAM;
...

## Slide 20: Timing Model for SRAM IV
architecture SRAM of ram6116 is ... begin ...
check: process begin
if CS_b’delayed = ‘0’ and NOW /= 0 ns then
if address’event then
assert (address’delayed’stable(t_WC)) –- t_RC = t_WC
report “address cycle is too short”
severity WARNING;
end if;
...

## Slide 21: Timing Model for SRAM V
architecture SRAM of ram6116 is ... begin ...
check: process begin
if CS_b’delayed = ‘0’ and NOW /= 0 ns then
... if rising_edge(WE_b) then
assert (address’delayed’stable(t_AW)) report “address not long enough to end of write” severity WARNING;
assert (WE_b’delayed’stable(t_WP)) report “write pulse is too short” severity WARNING;
assert (data’delayed’stable(t_DW)) report “data setup time is too short” severity WARNING;
wait for t_DH; assert (data’last_event >= t_DH) report “data hold time is too short” severity WARNING;
end if;
end if;
wait on WE_b, address, CS_b;
end process check;
end architecture sram;

## Slide 22: Dynamic RAM
library ieee; use ieee.std_logic_1164.all;
entity dram1024 is port(address: in integer range 0 to 2**5-1; data: inout std_ulogic_vector(7 downto 0); RAS, CAS, WE: in std_ulogic);
end entity;

## Slide 23: Dynamic RAM
architecture beh of dram1024 is begin
p0: process(RAS, CAS, WE) is type dram_array is array (0 to 2**10-1) of std_ulogic_vector (7 downto 0);
variable row_address: integer range 0 to 2**5-1;
variable mem_address: integer range 0 to 2**10-1;
variable mem: dram_array;
begin
...
end process p0;
end architecture;

## Slide 24: Dynamic RAM
architecture beh of dram1024 is begin
p0: process(RAS, CAS, WE) is begin
data <= (others => ‘Z’);
if falling_edge(RAS) then row_address := address;
elsif falling_edge(CAS) then mem_address := row_address*2**5 + address;
if RAS = ‘0’ and WE = ‘0’ then mem(mem_address) := data;
end if;
if CAS = ‘0’ and RAS = ‘0’ and WE = ‘1’ then data <= mem(mem_address);
end if;
end process p0;
end architecture;