## Slide 1: VHDL Modeling Digital Systems
EL 310
Erkay Savaş
Sabancı University

## Slide 2: Simulation and Synthesis
VHDL programs are unlike programs written in Pascal, C, C++.
VHDL is for describing a digital system for mainly two purposes
  Simulation
  Synthesis
The idea is to come up with a description that behaves like the real system with a desired level of accuracy

## Slide 3: Describing System
A system is an assemblage of objects united by some form of regular interaction or interdependence
  Could be anything from single chips to large supercomputers
What aspects of a digital system we want to describe
  Interface
  Function: Structural or Behavioral
  Structural and behavioral descriptions are complementary of each other and are expected to be supported by any HDL.

## Slide 4: A digital system
Consists of
  Binary signals that may take values of 1 or 0.
  Components
    Gates, flip-flops, counters, etc.
    Transforms input signals to output signals
  Wires that connect components.
Half adder
a
b
sum
carry
a | b | sum | carry
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1

## Slide 5: Events and Propagation Delays
Event: when a signal changes values (1-to-0, 0-to-1)
Propagation delay: time elapsed before changes at input will produce a change at output (5 ns for this example)
b
a
carry
sum
event
5 ns
10
15
20
25
30

## Slide 6: Concurrency of Operations
From our previous example
  When a change occurs at one of the inputs, say a, the two gates concurrently compute the values of output signals, sum and carry.
  New events occur at these signals  trigger more events
a
sum
c_in
b
carry
s2
s3
s1
Events on signals lead to computations that may generate events on other signals

## Slide 7: Full Adder 1
Truth table
a | b | c_in | sum | carry
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1

## Slide 8: Full Adder 2
b
a
carry = s2 + s3
c_in
sum = s1  c_in
15
20
25
30
35
40
45
s1 = a  b
s2 = s1 · c_in
s3 = a · b
5 ns
10

## Slide 9: Waveforms and Timing
The sequence of events that occur on a signal produces a waveform on that signal
D
clk
Q
DFF
Q
Q’
D
clk
R’
S’
S’ | R’ | clk | D | Q | Q’
0 | 1 | X | X | 1 | 0
1 | 0 | X | X | 0 | 1
1 | 1 | R | 1 | 1 | 0
1 | 1 | R | 0 | 0 | 1
0 | 0 | X | X | ? | ?
15
20
25
30
35
40
5
10

## Slide 10: Synchronous Circuit
Synchronous circuits operate with a periodic signal commonly referred to as clock.
  clock serves as a common time base
  The transition in clock (rising or falling) determines when the computation of output events is initiated.
  The input value on signal is sampled at clock transition,
  if there is an event on input signal before the clock transition occurs, the output may also change.
  This change, of course, takes some time (propagation time).

## Slide 11: Asynchronous 1
No global clock
  Request-acknowledge protocols
  Or handshaking
  Need to wait for events on specific signals
  Example: Asynchronous communication channels
transmit
ack

## Slide 12: Asynchronous 2
Transmitter
Receiver
transmit
ack
data bus

## Slide 13: Signal Values
Binary values
  0 or 1 (driven by a power supply or the output of a gate)
  Voltage values
  [0-0.8] V  logic 0
  [2.0 – 3.3] V  logic 1
  What if a signal is disconnected? (high-impedance)
  What if a signal is currently driven to both a 0 and a 1 value? (unknown)
  What if the initial value of a signal is unknown?
  How about the signal strength.
Recall that we want to describe a digital system as accurately as possible.

## Slide 14: Signal Values
0 V
3.3 V
2 V
Logic 1
Logic 0
Question: Why do we want to represent a situation which apparently corresponds to a design error?
  we may want to observe the effects of a design error.
  how is it propagated?

## Slide 15: Signal Values: IEEE 1164
This nine valued system is not a part of VHDL language; but rather a standard definition that vendors are motivated to support for portability.
Value | Interpretation
U | Uninitialized
X | Forcing Unknown
0 | Forcing 0
1 | Forcing 1
Z | High impedance
W | Weak unknown
L | Weak 0
H | Weak 1
- | Don’t care
Use the package that contains this definition.
Not all these values are synthesizeable.

## Slide 16: Signal Values: IEEE 1164
IEEE 1164 package defines multivalue logic values
logic operations for multivalue logic
and some conversion routines from this logic to other types that are part of language
  function TO_BIT(S: STD_ULOGIC, XMAP:BIT:=‘0’) return BIT;
  function TO_BITVECTOR(S: STD_ULOGIC_VECTOR, XMAP:BIT:=‘0’) return BIT_VECTOR;
  function TO_STDULOGIC(B:BIT) return STD_ULOGIC;

## Slide 17: Shared Signals
Multiple drivers for input and multiple destinations for output signals
  Bus construction
  Drivers (transmitters): tri-state buffers can be controlled by a decoder to ensure that only one source is driving the bus at a time
  There may be multiple receivers listening the bus
i1
o1
e1
i2
o2
e2
in
on
en

## Slide 18: Multiple Drivers
Wired logic
  Buses permit one transmitter at a time
  However, certain forms of switching circuits are designed based on wired logic and permit multiple transmitters.
  Wires in these circuits produce AND and OR Boolean functions.
  wired-AND logic: if at least one device driving the signal to a 0, the value of the signal will be 0.
  HDL must be expressive enough to describe such circuits for accurate simulation.
  See resolved signals for this.
  Synthesis compilers produce logic that arbitrates among accesses to shared signals. For example, when only one source is permitted then a decoder must be synthesized to control multiple drivers.

## Slide 19: Overview
We seek to describe attributes of digital systems common to multiple levels of abstraction
  Events, propagation delays, concurrency
  Waveforms and timing (synchronous vs. asynchronous)
  Shared signals
Hardware description languages must provide constructs for naturally describing these attributes of a specific design
  Simulators use such descriptions for mimicking the physical system
  Synthesis compilers use such descriptions for synthesizing hardware